## Slide 1: WF on RRM requirements for FR2 Inter-band DL CA and UL CA
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #99-e
E-meeting, May 19th – 27th, 2021
R4-2108340
Document for: Approval

## Slide 2: Topic #1 Inter-band DL CA enhancements Sub-topic 1-1 MRTD for CBM
Issue 1-1-1: MRTD value for FR2 inter-band CA
  Proposals (To be discussed in GTW):
    Option 1: Do not define any requirements for CBM UEs for FR2 inter-band CA
    Option 2: Introduce UE capability
      Option 2a: Introduce UE capability to support MRTD = 260ns and MRTD = 3us (vivo)
      Option 2b: Introduce UE capability to support MRTD = 3us (Intel, NEC)
        RAN4 to agree on the baseline implementation which should be considered for CBM UEs which support capability of MRTD = 3us (Intel)
    Option 3: MRTD = 260ns
    Option 4: MRTD = 3us
      3us if there are no critical issues such as connectivity problem or significant throughput degradation
      An agreed and approved UE capability indication, as in the bullet above, is a precondition for proposals in this document.
    Option 5: MRTD shall not be larger than “CP length - UE Rx beam switch time - 2 x DL timing error”
    Option 6: MRTD =3us allowing certain performance degradation
    Option 7: See next slide.

## Slide 3: Topic #1 Inter-band DL CA enhancements Sub-topic 1-1 MRTD for CBM
    Option 7: MRTD of 3us for inter-band CA in FR2 under CBM with a note to stating if the MRTD exceed [TBD us or CP or CP/2] a performance degradation is expected. Illustrated as below:
      RAN4 would then next discuss the condition of when the performance degradation may be expected:
        a fixed time limit if [x]us
        CP/2
        CP/2 – additional latencies as proposed by QC
        CP as used for intra-band non-contiguous CA
        Other
Frequency Range of the pair of carriers | Maximum receive timing difference (µs)
FR1 | 33
FR2 | 8 note1
FR2 | 3note2
Between FR1 and FR2 | 25
Note1: This requirement applies to the UE capable of independent beam management for FR2 inter-band CA. Note2: This requirement applies to the UE capable of common beam management for FR2 inter-band CA. If the receive time difference exceeds [the cyclic prefix length of that SCS], demodulation performance degradation is expected for the first symbol of the slot. | 

## Slide 4: Topic #1 Inter-band DL CA enhancements Sub-topic 1-1 MRTD for CBM
Issue 1-1-2: How to derive MRTD for FR2 inter-band CA?
FFS:
  Option 1: MRTD = TAE + Δ_propagation_time (Docomo, NEC, Huawei, ZTE, Nokia, Ericsson)
  TAE is 3µs, i.e. keep Rel-15 values for BS TAE unchanged
  Option 2: MRTD requirements for CBM UEs shall not rely on FR2 inter-band TAE requirement. (Xiaomi, Qualcomm)
  Option 3: focus on Issue 1-1-1. (Vivo, Mediatek, Intel)
Issue 1-1-3: Symbol level alignment assumption
  Following RAN4#98bis-e agreements:
    We come back to this issue once MRTD value in Issue 1-2-1 is agreed if needed.

## Slide 5: Topic #1 Inter-band DL CA enhancements Sub-topic 1-1 MRTD for CBM
Issue 1-2-4: Performance degradation due to Rx beam switching
FFS:
  Option 1: UE can switch RX beams without major performance degradation even if MRTD is larger than CP length (NEC, Huawei, Ericsson, ZTE)
  Option 2: Any timing impacts should be identified and should need to be accounted in the UE requirements (OPPO, Nokia, Vivo, Qualcomm, Vivo).
  Option 3: The performance degradation is significant and unacceptable (Xiaomi, Vivo, Mediatek, Qualcomm, LG, OPPO, Intel).
  Option 4: RAN4 needs to identify the scenarios where UE Rx beam switching is needed and study whether there have performance impacts due to Rx beam switching for each scenario. (Huawei)
  Option 5: RAN4 should evaluate on the feasibility of UE to perform Rx beam switch within the DL2UL guard period for CBM capable UE in inter-band CA (Nokia)

## Slide 6: Topic #1 Inter-band DL CA enhancements Sub-topic 1-2 MRTD for CBM
Issue 1-1-5: Rx beam switch delay
  Following RAN4#98bis-e agreements:
    This should be discussed in RF session

## Slide 7: Topic #1 Inter-band DL CA enhancements Sub-topic 1-2 RRM requirements for CBM
Issue 1-2-1: RRM requirements baseline
  Tentative Agreements:
    RAN4 need to discuss each requirement separately and update the Rel-15 FR2 intra-band CA RRM requirements for defining FR2 inter-band CA requirements with CBM when needed when needed to cover specific CBM related requirements.
Issue 1-2-2: Interruption requirements
  FFS:
    Option 1: The existing Rel16 interruption requirements of intra-band CA shall be applied (Xiaomi, OPPO, Ericsson, MTK)
    Option 2: Existing interruption requirements for inter-band CA in R15/R16 can be reused for CBM type UE in R17 (Huawei)
    Option 3: Existing non-IBM UE interruption requirements would be applicable for an inter-band CA CBM UE. (Nokia)
    Option 4: Need to agree on Issue 1-1-1 first (Intel)

## Slide 8: Topic #1 Inter-band DL CA enhancements Sub-topic 1-2 RRM requirements for CBM
Issue 1-2-3: Scheduling restriction
  Tentative Agreements:
    RAN4 to discuss in detail whether and how to introduce scheduling restriction for the following section
      RRM
        9.2.5.3.3 Scheduling availability of UE performing measurements on FR2
        9.10.2.6.2 Scheduling availability of UE performing CSI-RS based measurements in FR2
      Radio Link Monitoring
        8.1.7.3 Scheduling availability of UE performing radio link monitoring on FR2
      Link Recovery
        8.5.7.3 Scheduling availability of UE performing beam failure detection on FR2
        8.5.8.3 Scheduling availability of UE performing L1-RSRP measurement on FR2
        8.5.8.3 Scheduling availability of UE performing L1-RSRP measurement on FR2
      L1-RSRP/SINR measurements (Serving cell measurement)
        9.5.6.3 Scheduling availability of UE performing L1-RSRP measurement on FR2
        9.8.6.3 Scheduling availability of UE performing L1-SINR measurement on FR2

## Slide 9: Topic #1 Inter-band DL CA enhancements Sub-topic 1-2 RRM requirements for CBM
Issue 1-2-4: Measurement requirements
  FFS：
    Option1: RAN4 to discuss in detail whether and how to introduce scheduling restriction for the following section
      Radio Link Monitoring
        8.1.2.3 Measurement restrictions for SSB based RLM
        8.1.3.3 Measurement restrictions for CSI-RS based RLM
      Link Recovery
        8.5.2.3 Measurement restriction for SSB based beam failure detection
        8.5.3.3 Measurement restrictions for CSI-RS beam failure detection
        8.5.5.3 Measurement restriction for SSB based candidate beam detection
        8.5.6.3 Measurement restriction for CSI-RS based candidate beam detection
      L1-RSRP/SINR measurements (Serving cell measurement)
        9.5.5.1 Measurement restriction for SSB based L1-RSRP
        9.5.5.2 Measurement restriction for CSI-RS based L1-RSRP
        9.8.5.1 Measurement restriction if SSB configured for L1-SINR Measurement
        9.8.5.2 Measurement restriction if CSI-RS configured for L1-SINR measurement
        9.8.5.3 Measurement restriction if CSI-IM configured for L1-SINR measurement
    Option 2: RAN4 not to define any measurement restrictions for CBM operation in FR2 inter-band CA
      CBM UEs only need to perform RLM/BFD/CBD/L1-RSRP measurements on one CC (PCC or PSCC).
    Option 3: Measurement restriction requirements need to be defined for CBM capable UE for inter-band CA scenario.
      Existing Measurement restriction requirements would be applicable for an inter-band CA CBM UE but may need clarification aligned with the MRTD agreement.
    Option 4: CBM UE is not required to perform layer 1 measurements on multiple CCs
    Option 5: Need to agree on Issue 1-1-1 first

## Slide 10: Topic #1 Inter-band DL CA enhancements Sub-topic 1-2 RRM requirements for CBM
Issue 1-2-5: SCell activation delay
  Tentative Agreements:
    Principle: Case 2: if PCell/PSCell and the target SCell are in a FR2 band pair with CBM and the target SCell is unknown,
      Option 1: the SCell activation requirements shall be reduced
        Option 1a: SSB samples for Rx beam sweeping shouldn’t be accounted for in unknown SCell activation latency requirement.
        Option 1b: L1-RSRP measurement delay is not required in SCell activation delay
Issue 1-2-6: Beam management
  Tentative Agreements:
    The existing FR2 BFD/CBD requirements in Rel-16 can be applied for FR2 inter-band CA with CBM type UE.

## Slide 11: Topic #1 Inter-band DL CA enhancements Sub-topic 1-3 MTTD for CBM
Issue 1-3-1: The MTTD value for FR2 inter-band CA with CBM
  Follow RAN4#98bis-e agreements:
    The RRM requirements for FR2 inter-band CA based on CBM shall not be pursued in Rel-17

## Slide 12: Topic #2 Inter-band UL CA enhancements Sub-topic 2-1 RRM requirements for IBM
Issue 2-1-1: General
  Tentative agreements:
    RAN4 to update the applicability of requirements in the specification to include FR2 inter-band UL CA.
Issue 2-1-2: Interruption due to UL carrier RRC reconfiguration
  FFS:
    Option 1: The UL carrier reconfiguration only impact activate serving cells within the band of the UL carrier being reconfigured.
    Option 2: Existing interruption requirements at UL carrier RRC reconfiguration can be reused in R17
    Option 3: FFS

## Slide 13: Topic #2 Inter-band UL CA enhancements Sub-topic 2-2 RRM requirements for IBM
Issue 2-1-3: Interruption at active BWP switching
  FFS:
    Option 1: Only the band in which the UL BWP switch should be impacted by the BWP switch.
    Option 2: Interruption at active BWP switching will occur on all serving cells within FR if UE supports per FR gaps; otherwise interruption occurs on all serving cells.
    Option 3: FFS
Issue 2-1-4: DL interruption at UE Tx switching between two uplink carriers
  Tentative agreements:
    check the applicability of UL switching to FR2 and come back to this in next meeting

## Slide 14: Topic #2 Inter-band UL CA enhancements Sub-topic 2-1 RRM requirements for IBM
Issue 2-1-5: DL Interruption at NR SRS carrier based switching
  FFS:
    Option 1: Interruptions in DL due to SRS carrier switching in one of the two bands used in FR2 UL inter-band CA, will not cause interruptions in the DL of the 2nd band. (Nokia)
    Option 2: Wait for RF room on conclusion of applicable SRS carrier switching time for inter-band CA in FR2 (Nokia, Qualcomm)
    Option 3: Interruption due to SRS carrier switching in one band will occur on all serving cells within FR if UE supports per FR gaps; otherwise interruption occurs on all serving cells. (Ericsson, MTK)