## Slide 1: 3GPP TSG-RAN WG4 Meeting #99-e Electronic Meeting, 19 – 27 May, 2021
Intel
WF on R17 NR MG enhancements –NCSG
R4-21xxxxx

## Slide 2
Agreements in the 1st round/GTW
Agreements in the 2nd round
open for 2nd round discussion
Still open after 2nd round discussion

## Slide 3: Scenarios and use cases
In principle, NCSG can be used for intra-frequency measurements with MG, inter-frequency measurements with MG, inter-RAT measurements.
  FFS on whether NW should configure the legacy MG rather than NCSG even UE can support both of them.
Measuring deactivated SCC shall be studied as one of NCSG usage as we agreed unless the critical issues was acknowledged.

## Slide 4: NCSG pattern(1)
Define NCSG patterns for subset of the legacy MG patterns in [TS38.133 v16.5.0].
  FFS on which subset of legacy MG patterns
FFS on RAN4 needs to be define separate NCSG patterns for sync an asyc scenarios
  Option 1 (Ericsson, Nokia, Intel, Qualcomm): Yes
    Different NCSG patterns for synchronous and asynchronous operations in FR1
    Same NCSG patterns for synchronous and asynchronous operations in FR2.
  Option 2 (ZTE, OPPO, Huawei,MTK,vivo, CATT):
    No need to separate NCSG patterns needed for synchronous and asynchronous operations.
  Option 3 (CMCC, MTK, vivo, Apple): same NCSG patterns for synchronous and asynchronous operations, provided that the NCSG pattern only comprise the RF retuning time and ML. Interruption is not captured in VIL(RRT) and specified separately.

## Slide 5: NCSG pattern (2)
FFS on gap pattern index for NCSG
VIL:
  Option 1a (Qualcomm, Intel, Ericsson, vivo, ZTE): VIL should be explicitly defined base on the number of interrupted durations in absolute time
  Option 1b (Apple, CATT, Qualcomm, ZTE): VIL should be explicitly defined based on the number of interrupted duration in slot
  Option 2( MTK, Huawei, CMCC, Nokia): based on absolute RF retuning time (tentatively denoted as “RRT”).

## Slide 6: NCSG pattern (2)
FFS on ML of NCSG (or the total length of NCSG).
  Option 1: the total length of NCSG (“ML + VIL1+VIL2”) is same as MGL of the legacy gap
  Option 2: the total length of NCSG (“ML + VIL1+VIL2”) is larger than MGL of the legacy and the effective measurement window of NCSG (which is equal to ML) is same as “legacy MGL – 2 *RTT)”.

## Slide 7: NCSG configuration
FFS on explicit configuration for NCSG
  Option 1 (OPPO, Intel) NCSG configuration shall be based on legacy MG configuration
  Option 1a (MTK, HW, OPPO ) : Introduce a single bit for existing MeasGapConfig to transform the legacy gap into NCSG (detail to be left to RAN2).
  Option 2(CATT): Up to RAN2
  FFS other options

## Slide 8: Impacts on RRM requirements due to NCSG(1)
FFS on Interruption requirements
  Option 1: The interruption requirements in TS38.133 and TS36.133 shall be revisited
  Option 2: Existing interruption requirements for SCell activation/deactivation can serve as starting point for the study of VIL requirements
  Option 3: the interruption is proposed as following
  Option 3a :Translate 1ms(FR1) and 0.75ms(FR2) into the number of interrupted slots for defining the interruption requirements for the synchronous case and one more slot is added for asychrnous case.
  Option 4
    VIL on active victim serving cells is the number of interrupted slots calculated based on
      Aggressor reference cell RRT,
      Victim cell SCS, and
      Sync or async. operation
  Option 5: RAN4 to further discuss the condition, capability and impacts to measurement requirements for UE to use NCSG to control interruptions due to measurement on deactivated SCC or Scell in dormancy
The existing measurement mode requirements (effective MGRP, data scheduling depends on gap configuration) can be the baseline
SCS | Synchronous |  | Asynchronous | 
 | interruption length before measurement | interruption length after measurement | interruption length before measurement | interruption length after measurement
15KHz SCS | 1 slot | 1 slot | 2 slots | 2 slots
30KHz SCS | 2 slots | 2 slots | 3 slots | 3 slots
60KHz SCS | 3 slots | 3 slots | 4 slots | 4 slots
120KHz SCS | 6 slots | 6 slots | 7 slots | 7 slots

## Slide 9: Impacts on RRM requirements due to NCSG(2)
FFS on Per-UE or Per-FR capability support
  Option 1:per UE and per FR NCSG for RRM measurement needs the specific UE capability.
  Option 2: No additional NCSG capability for per-UE and per-FR differentiation is needed
  Others
CCSF
  Only one layer can be measured for each NCSG occasion, which is the assumption for deriving CSSF

## Slide 10: Measurement applicability
Defer to the discussion on simultaneous configuration of NCSG and legacy MG based on concurrent MG framework in a 2nd stage of this WI.
FFS on Rx beam limitation
  Option 1. (MTK, Ericsson, Huawei): NCSG pattern is also supported for FR2
  Option 1a. (MTK)NW needs to be informed that the inter-frequency measurements with NCSG is CBM or IBM with serving cells in FR2.
  Option 2(CATT) NCSG in FR2 should be deprioritized in current stage.
FFS on scheduling and measurement restriction
  Option 1 (Ericsson, CATT): When NCSG is configured then during the ML the existing scheduling restriction requirements defined in TS 38.133 shall also apply,
  Option 1a(Qualcomm): RAN4 to discuss if existing scheduling restrictions of 9.2.5.3.3 for measurement on FR2 intra-frequency cell shall be extended for the use case of measurement on intra- or inter-frequency cell via NCSG instead of legacy MG.
  Option 2(Huawei, OPPO, Intel): Scheduling restriction for NCSG is FFS, and check with RAN2 on the feasibility of informing NW the CBM or IBM between inter-frequency measurements and serving cells in FR2.

## Slide 11: Signaling
FFS on necessary signaling for NCSG
  Option 1 (Huawei, Qualcomm): Signalling supports for NCSG include at least
    NCSG configuration
    UE capability related to NCSG patterns and per-UE/per-FR NCSG
    UE capability related to need for NCSG for a target carrier
  Option 2 (Nokia, Ericsson): Defer these discussions after NCSG pattern design as well as NCSG applicability and UE capability support are finalized
  Other options was not excluded
FFS on How to consider the relation between NCSG and ‘NeedForGap’?
  Option 1 (Intel, Apple): The “NeedForGap” signaling structure can be reused for NR NCSG as a start point
  Option 1a (MTK, ZTE, Apple): Rel-17 NCSG capability is reported on top of existing RAN2 ‘NeedForGap’ signaling structure with a new component ‘NCSG’.
  Option 2 (Ericsson, CMCC, OPPO, Qualcomm): Don’t reuse Rel-16 ‘NeedForGap’ ignaling for NCSG
  Option 3(Ericsson, CATT, Qualcomm): Let RAN2 decide NCSG signaling details and any relation between NCSG and ‘NeedForGap’ based on RAN4 technical input on NCSG pattern design
  Note: regardless of the selected option, decision will involve RAN2 feedback