## Slide 1: WF on timing requirements for NR NTN
Xiaomi
3GPP TSG-RAN WG4 Meeting #99-e R4-2108350
Electronic Meeting, 19 May -27 May, 2021
Agenda Item: 9.12.4.3
Agreement in 1st round
Agreement in GTW
Agreement in 2nd round

## Slide 2: WF on UE specific TA estimation error (1/2)
    Whether to define a separate accuracy requirement for UE specific TA estimation
  Option 1: Yes (Intel, NEC, THALES, Ericsson)
  Option 2: No(QC, CATT, Xiaomi, CMCC, LGE, CATT, Apple, Huawei, MTK, Ericsson, ZTE)
  FFS the UE specific TA estimation accuracy
    Whether to define the update rate for UE specific TA estimation
  Option 1: Yes (Intel, CMCC, Ericsson)
  Option 2: No (CATT, Xiaomi, Apple, Huawei, MTK, Qualcomm, ZTE, THALES)
  Option 3: Under discussion in RAN1 (LGE)
    Whether to define UE behaviour related to UE specific TA estimation
  Option 1: Defer discussion for specifying UE behaviour related to UE specific TA estimation, and wait RAN1 conclusion (CATT, CMCC)
  Option 2: Specify UE behaviour related to the combination of UE specific TA estimation () and self-estimated TA common () (THALES, Ericsson, Intel)
  Option 3: No need to define UE behavior for UE specific TA estimation as a requirement, as long as UE can meet the timing requirement, i.e., Te/Tq/Tp (Apple, Xiaomi, Huawei, Qualcomm, ZTE)
    Wait RAN1/RAN2 conclusions on UE specific TA pre-compensation reporting to determine whether we need to define separate UE specific TA estimation requirement or not

## Slide 3: WF on UE specific TA estimation error (2/2)
    Whether to define a separate accuracy requirement for self-estimated TA common ()
  Option 1: Yes (THALES, Ericsson)
  Option 2: No (Apple, Xiaomi, Huawei, Qualcomm, CATT, CMCC)
    Whether to define a separate accuracy requirement for the combination of
  Option 1: Yes (THALES, Ericsson)
  Option 1: No (Apple, Xiaomi, Huawei, Qualcomm, CATT)
    Whether UE should use the referenceTimeInfo-R16 and GNSS-provided time reference to calculate TA at the UE
  Option 1: FFS (Nokia, Apple)
    RAN4 should discuss whether the use os the time provided by referenceTimeInfo-R16 is beneficial to securing that the initial transmission timings are kept by a UE.
  Option 1: Up to RAB1/RAN2 decision (Xiaomi, Huawei, Qualcomm, CATT, Ericsson, ZTE THALES)

## Slide 4: WF on UE initial transmit timing requirements (1/2)
    The composites should be considered for initial transmit timing requirement in NTN (Te_NTN)
  Option 1: (QC, Xiaomi, Huawei, LGE, ZTE, NEC, CMCC)
    UE position estimation error
    Serving-satellite position estimation error
    The current UE transmit timing error requirement
  Option 1a: (LGE, MTK, Huawei, ZTE)
    GNSS inaccuracy
    The current UE transmit timing error requirement
  Option 2: (Apple)
    legacy Te
    UE specific TA estimation error (without ephemeris uncertainty)
  Option 3: (THALES, Ericsson)
    The accuracy of UE specific TA estimation (N_(TA,UE-specific)) and self-estimated TA common (N_(TA,common)) is counted into the UE transmit timing error requirement.

## Slide 5: WF on UE initial transmit timing requirements (2/2)
    GNSS position error assumption for Te_NTN
  Option 1: (QC)
    at least 50m, and further relax up to 100m
  Option 2: (Xiaomi, CATT, THALES)
    50m
  Option 3: (CMCC, CATT)
    50m as the worst case and 20m as the typical case
  Option 4: (MTK, Xiaomi, THALES, NEC, Intel)
    For UL SCS of 15/30 kHz: <= 50 m
    For UL SCS of 60/120 kHz: <= 30 m
  Option 5: (Apple, LGE, Nokia)
    The worst case: 100m
    Whether to define general GNSS positioning accuracy requirements?
  Option 1: (Huawei, Ericsson, Nokia, THALES)
    Yes, it is suggested to define general GNSS positioning accuracy requirements which can be referred for deriving other RRM requirements.
  Option 2: No (Apple, Xiaomi, QC, CATT, CMCC, Intel)
    FFS
    FFS the reference timing for UE initial transmit timing

## Slide 6: WF on gradual timing adjustment requirements (1/2)
    RAN4 to introduce new gradual timing adjustment requirements for NTN network.
      FFS the minimum aggregate adjustment rate: Tp_NTN
      FFS the maximum aggregate adjustment rate: Tq_NTN
    Whether define different gradual timing adjustment requirements for different NTN topologies e.g. GEO, MEO, LEO
  Option 1: Yes (CATT, Xiaomi, Ericsson)
  Option 2: FFS (QC, CMCC, Apple, Huawei, ZTE, THALES, NEC, CMCC, Intel)
    The assumptions will be used to define gradual timing adjustment requirements for NTN network
  Option 1: UE performs timing adjustment for downlink reception timing drifting and UE specific TA change separately. (Huawei, MTK, Ericsson)
  Option 2: UE performs timing adjustment with combining downlink reception timing drifting and UE specific TA change as one adjustment. (Huawei, Apple, QC, THALES, CMCC, Intel)

## Slide 7: WF on gradual timing adjustment requirements (1/2)
    Whether the maximum delay variation should be considered in the gradual timing adjustment requirement in NTN?
  Option 1: Yes (Xiaomi, CMCC, Ericsson, Apple, Huawei, QC, Ericsson)
  Option 2: FFS (CATT, MTK, THALES, NEC)
    FFS the direction of timing adjustment for NTN UE pre-compensation

## Slide 8: WF on TA adjustment accuracy requirement
    Not define TA adjustment accuracy requirement in RRC_IDLE mode.
    Whether the UE position and satellite position estimation error should be accounted for TA adjustment accuracy requirement?
  Option 1: Yes (Xiaomi, LGE, Nokia)
  Option 2: No (QC, CMCC, LGE, CATT, CMCC)
  Option 3: Depends on RAN1 design (Apple, Huawei, NEC)
    TA adjustment accuracy requirement in RRC_CONNECTED mode
  Option 1: (NEC, Huawei, Ericsson, Apple, MTK, NEC)
    Reuse the existing timing advance adjustment accuracy requirements defined in TS 38.133.
  Option 1a: (NEC)
    RAN4 to reuse the existing TA adjustment accuracy requirement defined in TS 38.133 with considering of UL timing quantization accuracy.
  Option 2: (Xiaomi, CMCC, LGE)
    RAN4 is to define a relaxed TA adjustment accuracy requirement for NR NTN
  Option 2a: (QC)
    Request RAN1 whether and how to reflect a propagation delay change, i.e. open loop TA update, from a slot when UE received timing advance command to a slot when the indicated timing advance shall be applied to uplink transmission. If defined, depending on RAN1 design NTN UE timing advance adjustment accuracy requirements may have to be relaxed to account for UE position and satellite position estimation error. And if it is decided to relax the requirement, the accuracy requirement relaxation shall be the same as that for initial timing error requirement.
    UE behaviour before applying timing advance adjustment for its uplink transmission
    FFS the TA adjustment accuracy impact due to the open loop and closed loop TA adjustment.