## Slide 1: WF on NR positioning enhancements
Ericsson
3GPP TSG-RAN WG4 Meeting # 99-e
Electronic Meeting, 19th – 27th May 2021
Agenda: 9.20.1
R4-2108360

## Slide 2: Definition of new or updated RRM requirements in relation to timing error mitigation
Monitor progress of other RAN WGs to determine impact of timing error mitigation on existing RRM requirements or the need to define new RRM requirements. No impact on current RRM specification can be identified.
RAN4 is studying the feasibility of proposed timing error mitigation mechanisms by RAN1

## Slide 3: General issues with latency reduction
RAN4 requirements definition on latency reduction are reliant on RAN1 solutions, which RAN4 needs to discuss after RAN1 has made agreement.
Candidate options:
Analyze factors that impact measurement requirements from RAN4 perspective to identify possible enhancements regarding latency reduction
  Option 1: Yes
  Option 2: TBA

## Slide 4: Latency enhancements in relation to UE measurement time
Candidate options:
Define {N,T} capabilities to indicate measurement/processing time (T) in relation to reference signal duration (T):
  Option 1: Yes
  Option 2: No, not in RAN4 scope
FFS: RAN4 to identify list of side conditions which can lead to enhance requirements

## Slide 5: Latency enhancements in relation to measurement gaps
Wait on outcome of RAN1/2 on gapless measurement. Introducing new measurement gap patterns is FFS and shall be addressed in the next meeting.

## Slide 6: Specify RRM requirements for positioning measurements in RRC_INACTIVE state
Specify measurement delay and accuracy and potential reporting requirements in RAN4 based on outcome of other WGs
Define UE requirements for PRS measurement for DL positioning methods with RRC_INACTIVE and wait for RAN1/RAN2 conclusions on UL/DL+UL positioning methods

## Slide 7: A-GNSS positioning enhancement
Performance requirements for additional BDS and NavIC signals need to be defined based on progress of RAN2 work.

## Slide 8: Impact on existing RAN4 requirements for positioning and other RRM measurements
Wait for RAN1/2 framework agreements on gapless measurements
Impact on existing positioning and RRM requirements can be discussed without RAN1/2 input

## Slide 9: Larger MGL
Candidate options:
Introduction of new measurement gap patterns with larger MGL
  Option 1: Yes
    RAN4 to discuss impact of larger measurement gap length usage on serving cell procedures
  Option 2: No

## Slide 10: Send reply LS to RAN1 on gNB/UE Rx/Tx timing error mitigation
Further study TEG feature feasibility to reach conclusion if reply LS is needed and what to include

## Slide 11: Calibration error/residual timing error after calibration
FFS
Candidate options
  Option 1: The remaining Rx/Tx time delays after the calibration are unknown to the UE/TRP and therefore cannot be provided
  Option 2: TBA

## Slide 12: TEG grouping
FFS
Candidate options
  Option 1:
    UE/TRP may group the timing error (with or without calibration) based on RF chains and antenna panel, such that timing errors in the same group are within certain margin
    UE/TRP may not be able to ensure that timing errors are within the same margin
  Option 2: Discuss and conclude whether UE Rx and UE Tx timing error can be grouped based on antenna panel, RF chain, frequency, baseband sampling rate, SRS antenna switching, etc.
  Option 3: No grouping according to UE Rx and UE Tx timing errors, rather defining association information for which transmission/reception (chain) the timing error difference between transmissions/receptions are within a margin delta
  Other options not precluded

## Slide 13: Time variant behaviour of TEG
FFS: RAN4 to study if TEG appears static, semi-static or dynamic in TX/RX scenarios considering various front-end parameters and conditions
FFS: If time variant behavior has effect on TEG association
FFS: Feasibility study on absolute Tx/Rx timing error estimation in DL-TDOA if TEG changes measurably statically or semi-statically.

## Slide 14: Applicability of TEG with gNB/TRP
FFS
Candidate options
  Option 1: Support TRP to provide association information of DL PRS resources with Tx and Rx TEG to LMF if TRP has multiple TEG (i.e. different antenna panels or arrays)
  Option 2: TRP comprising multiple TEG is unlikely, therefore multiple Rx and Tx TEG is not supported
  Other options not precluded

## Slide 15: Applicability of TEG with UE
FFS
Candidate options
  Option 1: TEG is applicable for UEs
  Option 2: TEG is not applicable for UEs
  Other options not precluded