## Slide 1: WF on frequency bands for testing of A-GNSS Sensitivity requirements in NR and LTE
Apple,
3GPP TSG-RAN WG4#99-e Meeting R4-21xxxxx
Electronic Meeting, May 12 – 20, 2021

## Slide 2: Background
At this meeting, the following contributions are submitted in response to RAN5 LS (R4-2100021).
  R4-2109002 Frequency bands for testing of A-GNSS sensitivity requirements in NR and LTE, Qualcomm
  R4-2109326 Further discussion on testing of A-GNSS Sensitivity requirements in NR and LTE, Apple
  R4-2110199 Discussion on Frequency Bands for testing of A-GNSS Sensitivity requirements in NR and LTE, Xiaomi
  R4-2110959 Discussion on frequency bands for testing of A-GNSS Sensitivity requirements in NR and LTE, Spirent Communications

## Slide 3: Way Forward – LTE and NR bands for testing
There are three options discussed:
  Option 1: only consider E-UTRA/NR bands: Bands 13, 14, 24, 44 (Qualcomm)
  Option 2: LTE Bands 13, 14, 24, 44 and NR Bands n13, n14, n24, n79 and n96. In case of the same LTE and NR band supported by a UE, e.g., 14/n14, it suffices to test either LTE band 14 or NR band n14 because of the same interference mechanism (Apple, Xiaomi, Qualcomm)
  Option 3: all UE supported bands (Spirent, R&S)
Agreements:
  TBD

## Slide 4: Way Forward –EN-DC combinations for testing
When an EN-DC configuration generates second or third order intermodulation distortion (IMD) products falling into the following GNSS L1/E1/G1/B1 typical receiver bands (where supported by the UE), it shall be considered as a candidate for testing:
  GPS L1 C/A : 1574.3970 – 1576.4430 MHz
  Galileo E1 / GPS L1C: 1573.3740 – 1577.4660 MHz
  GLONASS G1: 1597.5515 – 1605.8860 MHz
  BDS B1I: 1559.0520 – 1563.1440 MHz
To further reduce testing, all EN-DC configurations are divided into groups with similar IMD level and risks. For each group, only one of the EN-DC configurations supported by the UE in the group shall be tested. Details can be found at Annex B of reference [1]

## Slide 5: Way Forward
For both LTE/NB bands and EN-DC band combinations, the following details are to be specified as well:
  E-UTRA / NR carrier frequencies
  Carrier bandwidth
  other channel configurations if necessary
As RAN4 continues to introduce new bands or new EN-DC band combinations, RAN4 shall capture the aforementioned rules and maintain the lists for both LTE/NB bands and EN-DC band combinations.

## Slide 6: Plan for Next Meeting
Interested companied are requested to provide more analysis to the next meeting to pick an option in slide 3
Detailed CRs to 38.171 will be agreed.