## Slide 1: [336] FR2_enhTestMethods GTW discussion topics
Apple
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, May 19th – 28th, 2021
Agenda Item: 10.1
R4-21xxxxx

## Slide 2: Polarization mismatch objective
WF on FR2 UL MIMO EVM [R4-2108651]
  Is the WF stable?
  Method 1 and method 2 are baseline for evaluation, refinement on proposed method 1, method 2 not precluded.
TP to TR38.884 v0.3.0 on UL signal demodulation [R4-2108652]
  One company indicated it is not ready to accept the TP based on both methods
  Recommended WF: given the WF recommends further evaluations of simulation results, it seems reasonable to conclude the study and then capture the outcome in the TR
  Include both methods into TR with TP approved in this meeting, and further update on the TR not precluded pending on the evaluation and analysis in future RAN4 meeting.
  Add editor note into TP: RAN4 didn’t confirm the feasibility and the selection on these methods, further update/remove and refinement on these methods not precluded.

## Slide 3: Test time reduction objective
TP to TR38.884 v0.3.0 on testing time reduction [draft R4-2108655] highlights the following potentially open issues:
  “By default, 4x2-based measurement grids can be adopted for FR2 PC3 test cases.” is removed
  The sentence ”For RSRP(B) based Rx beam peak search, the measurement antenna and link antenna are the same one” is removed. Given link antenna is not mentioned in the test procedure, the procedure is clear enough that the direction during link and measurement is the same.
  For step 8, change the sentence to “How to calculate the reported RARPs and RSRPBs is FFS”, given companies are still not clear on how to data processing the measurement results. This step will be added next meeting.
  One note is added: “Note: FFS how to select RSRP-based or RSRPB-based test procedure. FFS whether all the FR2 UEs should support RSRPB or not.”
Is this TP draft stable?

## Slide 4: Environment condition
TP to TR38.884 v0.3.0 on Environment conditions [draft R4-2108658] highlights the following issues:
  Remove the following text: “Whether the RF test cases should be performed with normal condition or extreme conditions should follow the RF requirement applicability defined in TS38.101-2 [2].”
  And add one sentence, “For ETC test system defined in Clause 5.4, the extreme temperature conditions in Table A.2-1 applies.”
Is this TP draft stable?
This TP has no impact on RF core requirements. (Remove the voltage part）

## Slide 5: Extension of permitted methods to band n262
TP to TR38.884 on permitted test methods for demodulation and RRM in band n262 [draft R4-2108657]
  Still available as a draft pending RAN5 LS response (anticipated Wednesday)
  Are there any other comments or inputs which need to be taken into account?

## Slide 6: Others
TP on high DL power and low UL power test cases [R4-2108653]
  Is the TP stable?
TP to TR38.884 v0.3.0 on measurement uncertainty [R4-2108659]
  Is the TP stable?

## Slide 7: Views on concluding the study item
Assuming the previously listed WF/TPs are approved this meeting, the remaining open issues include:
  Objective 1 (test methodology for high DL power and low UL power test cases)
    MU
  Objective 2 (solutions to minimize the impact of polarization basis mismatch)
    EIRP measurement: none minor update still required
    UL signal demodulation: enhancement method and MU
  Objective 3 (enhancements to support the verification of RF requirements for inter-band FR2+FR2 CA)
    None
  Objective 4 (extreme temperature conditions for all applicable FR2 UE RF test cases)
    None
  Objective 5 (testability enhancements to reduce test time)
    Open issues related to the RSRP(B) enhancement and MU for all enhancement methods
  Objective 6 (testability aspects for the introduction of the new band n262)
    RRM/demodulation setup: none, assuming the RAN5 LS can be incorporated into the TP
    RF setup
Others?
It seems reasonable to extend the SI by 1 quarter in order to conclude the open issues