## Slide 1: WF on Rx MU for n262
Nokia, Nokia Shanghai Bell
3GPP TSG-WG RAN4 Meeting #99-e
Electronic meeting, 19th – 27th May, 2021
R4-2108608

## Slide 2: Background
During RAN4#99-e, the following documents on Rx MU for n262 have been submitted:
  R4-2110088; Band n262 - BS conformance - MUs; Ericsson, Nokia, T-Mobile USA, DISH Network
  R4-2110480; 47 GHz band MU and TT for NR BS RF requirement; Keysight Technologies UE Ltd, Rohde & Schwarz
  R4-2111463; Consideration of TR 37.941 and correction of the MU contributors for the FR2 TE; Huawei
  In summary:
Rx test | 38.141-2: 24.25-29.5 GHz [dB] | 38.141-2: 37-43.5 GHz [dB] | R4-2110480 | R4-2110088
Reference sensitivity | 2.4 | 2.4 | 3.6 | [2.5]
ACS | 3.4 | 3.4 | 5.1 | [3.5]
IBB | 3.4 | 3.4 | 5.1 | [3.5]
OOBB | 4.1 | 4.1 | 5.6 | [4.2]
Rx IM | 3.9 | 3.9 | 5.5 | [4.0]
In-channel selectivity | 3.4 | 3.4 | 5.1 | [3.5]

## Slide 3: WF on Rx MU for n262
  It is proposed to agree on [0.1]dB increase of MU (comparing to 43.5GHz) :
  [] are kept until RAN4#100-e for final confirmation
  For Test Equipment MU term, TE vender’s input shall be taken
  It is proposed to further review possible MU value reduction by
  Interested companies are encouraged to contribute on MU values derivation for band n262 in the TR 37.941 (OTA BS testing TR) during RAN4#100-e
  OOBB value may change pending RAN4 agreement on revision of current requirement
  Further review on currently defined mathematics and MU budget in TR37.941 against actual test condition of FR2 Rx test to seek for realistic MU value for possible further value reduction
Rx test | MU for n262
Reference sensitivity | [2.5]
ACS | [3.5]
IBB | [3.5]
OOBB | [4.2]
Rx IM | [4.0]
In-channel selectivity | [3.5]

## Slide 4: Thank you