## Slide 1: 3GPP TSG-RAN WG4 Meeting #99-e R4-210xxxx Electronic Meeting, May. 19th – 27th, 2021
Huawei, HiSilicon
Way forward on PUSCH 256QAM performance requirements

## Slide 2: Background
R4-2106120 Way forward for PUSCH 256QAM performance requirements, Huawei, HiSilicon, RAN4#98bis-e

## Slide 3: Test parameters
MCS
  Option 1: MCS 22
  Option 2: MCS 24
  Option 3: MCS 20 or MCS 21 if there is testability issue for OTA test
Additional DM-RS configuration (dmrsAdditionalPosition): pos1
PT-RS configuration: Not configure PT-RS
Phase noise modelling:
  Not consider explicit phase noise modelling in the alignment results.
  The phase noise impact can be included in the impairment results, but it is left up to companies.
Tx EVM
  Option 1: Consider 3.5%Tx EVM modelling for alignment results
  Option 2: Consider 3.5% Tx EVM impact in the impairment results
    Option 2a: add a certain margin on top of the averaged impairment results
    Option 2b: consider it in the impaired results submitted by companies
  Option 3: Not consider 3.5% Tx EVM impact if the target SNR is 20dB or less
Number of Tx：Only 1Tx
Number of Rx
  Option 1: 2/8 Rx
  Option 2: 2/4/8 Rx
Number of layer: 1 layer

## Slide 4: Test parameters
SCS and Bandwidth combination
  15kHz SCS:
    Option 1: 5MHz and 10MHz
    Option 2: 5MHz, 10MHz and 20MHz
  30kHz SCS:
    Option 1: 10MHz and 40MHz
    Option 2: 10MHz, 20MHz, 40MHz and 100MHz
Test applicability rules for different antenna configuration
  Reusing the existing test applicability rule defined in clause 8.1.2.0 of TS38.141-1?
Test applicability rules for different SCS and bandwidth combination
  Reuse the existing applicability rules defined in 8.1.2.1.1 and 8.1.2.1.2 in TS 38.141-1 for different SCS and bandwidth combination.
MU and TT
  Reuse the existing MU and TT values for PUSCH demodulation test cases defined in TS 38.141-1, but with square brackets for TE vendors’ checking.
Performance requirements for FDD and TDD with different TDD patterns
  One set of performance requirements can be defined for FDD and TDD with different TDD patterns.
Performance requirements for BS type 1-O with 2Rx
  Both conducted and radiated performance requirements need to be defined

## Slide 5: Simulation assumptions
Parameter | Value
Transform precoding | Disabled
CP | Normal CP
Number of Tx | 1, [2]
Number of Rx | 2, [4], 8
Number of layers | 1
TDD pattern | 15kHz SCS: 3D1S1U, S=10D:2G:2U 30kHz SCS: 7D1S2U, S=6D:4G:4U
DM-RS sequence generation | NID=0, nSCID=0
DMRS type | Type 1 with single-symbol DM-RS
Number of DMRS symbols | 1+1
Number of DM-RS CDM groups with data | 2
Ratio of PUSCH EPRE to DM-RS EPRE | -3dB
symbols length | 14
start symbol index | 0
Time domain resource allocation type | type A and B
Frequency domain resource | Full applicable test bandwidth
MCS index | [20, 21, 22, 24]
Carrier frequency (GHz) | 4
Propagation condition | TDLA30-10 Low
SCS and BW | 15kHz: 5MHz, 10MHz, [20MHz]; 30kHz: 10MHz, [20MHz], 40MHz, [100MHz]
SRS | Not configured
PTRS | Not configured
Phase noise modelling | No explicit PN modelling
Tx EVM | FFS
Timing offset, Frequency offset | 0, 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled
Number of HARQ transmissions and RV sequence | 4, {0,2,3,1}
Testing metric | SNR @70% of maximum throughput