## Slide 1: Way forward on NR UE PDSCH demodulation requirements
NTT DOCOMO, Intel Corporation, …
3GPP TSG-RAN WG4 Meeting AH 1807
Montreal, Canada, 2 – 6 July 2018 Agenda Item: 5.4.1.3
R4-1809392

## Slide 2: Performance metrics
Previous agreements
  Test metric
    At least for FR1: Reuse LTE metric as throughput vs. SNR
      Test point: 70% (normal demodulation test cases)
      FFS for other test point(s) of some specific test cases
    FFS for test metric for URLLC specific test cases if any
AH agreements
  No agreements
Proposal
  70% is default test point
    FFS: 30% for additional test cases where maximum HARQ process is configured

## Slide 3: FRCs (1)
AH agreements
  Working assumption: For 64QAM and 256QAM keep both options to further evaluation and pending on the achievable SNR points to decide final options
  Option 1: (baseline)
    QPSK MCS4, 16QAM MCS13, 64QAM MCS 24 (64QAM table)
    256QAM MCS 24 (FR1 only) (256QAM table)
    DMRS configuration for 64QAM and 256QAM will be considered together to achieve feasible SNR points
  Option 2:
    QPSK MCS4, 16QAM MCS13, 64QAM MCS 19 (64QAM table)
    256QAM MCS 20 (FR1 only) (256QM table)
  Working assumption for option 1 need to be confirmed by the analysis for achievable SNR points

## Slide 4: FRCs (2)
Proposal
  Use QPSK MCS4, 16QAM MCS13 (64QAM table)
  64QAM and 256QAM FRCs
    Option 1: (baseline)
      64QAM MCS 24 (64QAM table)
      256QAM MCS 24 (FR1 only) (256QAM table)
    Option 2:
      64QAM MCS 19 (64QAM table)
      256QAM MCS 20 (FR1 only) (256QM table)
    Working assumption: Use option 1 subject to check that operating SNR is testable
      Use option 2 if option 1 is not testable
      Assumption in RAN4: Testable SNR for FR1 is up to 24 dB for 64QAM and 30 dB for 256QAM

## Slide 5: Max number of HARQ process
AH agreements (R4-1809324)
  For FR1 30 kHz
    Apply 8 HARQ processes for REFESNS requirements
    At least some test cases with 16 HARQ processes shall be defined for Rel-15 UE demodulation requirements
  For FR2 120 kHz
    Apply 8 HARQ processes for REFESNS requirements
    At least some test cases with 16 HARQ processes shall be defined for Rel-15 UE demodulation requirements
Proposal
  FDD
    Option 1: 4
    Option 2: 8
  TDD
    Option 1: less than or equal 16 for all test cases with 70% test point, 16 for all test cases with 30% test point
    Option 2:Different HARQ process for each TDD configuration derived under the following assumption on BS processing delay
      Option 2-1: 4 slots for 15kHz, 7 slots for 30kHz, 8 slots for 60kHz, 12 or 13 slots for 120kHz
      Option 2-2: Same processing delay as UE side (N1)
    Other option is not precluded

## Slide 6: RV sequence
AH agreements
  HARQ RV sequence for performance requirements:
    {0, 2, 3,1} for all the modulation orders

## Slide 7: PDSCH scheduling
Previous agreements
  Common test parameters
    For initial simulation alignment purpose: control symbols assumption: 2 symbols with full BW allocation for FR1, 1 symbol with full BW allocation for FR2
    Note: FFS for introducing performance requirements with partial BW PDCCH allocation
  PDSCH scheduling (For initial alignment simulation purpose):
    Full PRB allocation with channel bandwidth
    PDSCH mapping type: both type A and type B
    Further discussion for candidate options this week for PRB bundling size
      2
      FFS for the values of introducing performance requirements
    Random Precoding, per slot, per 2RBs (codebook configuration Single panel Type 1)
  Note: FFS for test set-up for introducing PDSCH performance requirements

## Slide 8: PDSCH scheduling
Proposals for performance requirements
  PDSCH mapping type
    Define requirements for PDSCH Mapping Type A
    FFS whether to define requirements for PDSCH mapping Type B
  PRB bundling
    Baseline: 2 PRB
    Define additional requirements for 4 PRB bundling and WB bundling
  Resource allocation
    Full PRB allocation
  Control symbols assumptions :
    2 symbols with full BW allocation for FR1 (baseline)
    1 symbol with full BW allocation for FR2 (baseline)
    Occupy channel BW as much as possible and start from symbol #0 (baseline)
    Introduce one more requirement with 1 symbol for FR1 FDD with 10MHz and 15kHz SCS (for LTE-NR coexistence scenario)
  Precoding model
    FR1: Random Precoding, per slot , PRB bundling granularity(codebook configuration Single panel Type 1)
    FR2: FFS
    FFS whether to introduce some test cases following PMI report

## Slide 9: Reference Signal (DMRS, PTRS, TRS)
Previous agreements
  DMRS configuration
    Candidate options for defining performance requirements:
      Type 1 or 2, 1 symbol FL DMRS without additional symbol
      Type 1 or 2, 1 symbol FL DMRS 1 additional symbol
      Type 1 or 2, 1 symbol FL DMRS 2 additional symbol
    For initial alignment simulation purpose:
      Type 1, 1 symbol FL DMRS 1 additional symbol for FR1
      Type 2, 1 symbol FL DMRS 2 additional symbol for FR2
      Type 1, 1 symbol FL DMRS 1 additional symbol for FR2
    Note: Detailed test configurations for non-slot test cases if any in FR2 FFS
  PTRS
    PTRS is configured when introducing performance requirements in FR2
    For initial simulation purpose:
      Using Phase noise model in TR 38.803 models for initial simulation purpose
      PTRS configuration (port 1, per 2PRB in frequency domain, per symbol in time domain)
  TRS
    TRS configured when introducing performance requirements for both FR1 and FR2
    FFS for detailed configuration of TRS configuration
      Option 1 for information:
        FR1: periodicity 20 ms , power boosting [6dB], 2 slots
        FR2: periodicity 10 ms , power boosting [6dB], 2 slots
      Other options are not excluded

## Slide 10: Reference Signal (DMRS, PTRS, TRS)
Proposals for requirements definition
  DMRS
    Type: Type 1 DMRS
    Length:
      Option 1: 1 additional DMRS symbol
      Option 2: 2 additional DMRS symbols
      No additional DMRS symbol is not precluded
      3 additional DMRS symbols is not precluded for high speed scenarios
    FDM between DMRS and data
      Option 1: For layer 1 and layer 2 (baseline)
      Option 2: For layer 1 only
      Option 3: For layer 2 only
    DMRS configuration can be different in each test case
  TRS
    2 slots pattern
    periodicity 10ms or 20ms
      Use 20ms for initial simulations for both FR1 and FR2
    Offset 1 slot
    Bandwidth: full BWP
    0 dB boosting.

## Slide 11: Reference Signal (DMRS, PTRS, TRS)
Proposals for requirements definition
  PTRS
    FR1: PTRS is not configured when introducing performance requirements
    FR2: PTRS configuration (port 1, per 2PRB in frequency domain, per symbol in time domain)
    Phase noise model for FR2:
      Using Phase noise model in TR 38.803 models (model #1 and #2) for initial simulation purpose
      For initial alignment:
        Phase noise model: model #2 is baseline for alignment
          Companies are encouraged to provide comparison analysis between model #1 and model #2
        Carrier frequency: 29.55GHz
        Other assumption is not preluded for final requirements
      FFS how to model phase noise for requirements

## Slide 12: Reference Receivers
Previous agreements
  Reference Receiver (For initial alignment purpose):
    Rank1: MMSE-IRC/MMSE
    Layer 2,3,4: MMSE-IRC/MMSE and R-ML
  FFS for the receiver assumptions for performance requirements
Proposals for performance requirements
  Reference Receiver:
    Rank1: MMSE-IRC/MMSE
    Layer 2,3,4:
      MMSE-IRC/MMSE as baseline
      Introduce a limited number of test cases with R-ML receiver.

## Slide 13: SDR Test Methodology
SDR test methodology is FFS