## Slide 1: WF on remaining open issues for UE Demodulation setup
Rohde & Schwarz, Intel, Anritsu, Keysight
3GPP TSG-RAN WG4 Ad-hoc 1807 Montreal, Canada, 2nd – 6th June, 2018
Agenda item: 5.6.2
Draft_R4-1809505

## Slide 2: SNR Reference point
Agreement from the Ad-hoc:
  The reference point for DL SNR and signal/noise power levels is point X in space inside the test chamber
  Point X definition is FFS for UE demodulation setup
  Further discuss on how to handle the mismatch of SNR at the UE baseband and the reference point and methodology how to capture it in the UE performance requirements
Proposal:
  SNR Reference point:
    For Near-Field setup:
      The reference point for SNR is defined as the intersection of the axes of rotation of the positioning system(s).
    For Far-Field (Direct or Indirect) setup:
      The reference point for SNR is defined as the geometrical center of the QZ.
  How to calculate the SNR at the reference point for a wanted SNR at the BB of the UE:
    RAN4 defines a methodology how to calculate the SNR set by the TE at the reference point for a wanted BB SNR
    How to capture the methodology and corresponding SNR value in the specification is FFS

## Slide 3: SNR Accuracy and Range
Agreement from the Ad-hoc for RRM:
  Further capture in the TR the SNR range which can be emulated by the test system with SNR error of [1] dB (note: this value is not expected to be used as MU value)
Proposals:
  In RAN4#88: Identify approximate SNR upper bound to allow RAN4 demod experts to make a prioritization of test cases
    TE Vendors to bring proposals on the max feasible SNR value
  RAN4 UE Demodulation and CSI requirements can be defined for any SNR range
  In case the required SNR is larger than the SNR upper bound, the corresponding requirement can currently not be tested

## Slide 4: Initial MU assessment
Background:
  Identification of MU factors contributing to DL SNR accuracy and range (open issue according to R4-1808541)
Proposal:
  Following parameters have been identified:
    gNB emulator SNR uncertainty
    gNB emulator DL EVM
    gNB emulator Fading model impairments
    RF leakage from measurement antenna to receiver
  The identified parameters shall be captured in TR 38.810. Exact values are to be defined by RAN5.
  Anritsu TP R4-1809511 will capture the proposal.

## Slide 5: Other identified open issues
How to capture different test system applicability in the TR (NF, DFF, IFF)
  Applicability for NF, DFF and IFF to be captured in the TR 38.810
  Proposal:
    Exact wording to be captured in the revised Keysight TP R4-1809512
FR1 link to the UE in case of CA between FR1 and FR2
  Similar as for NSA, the system needs to be able to provide a FR1 Link to the UE in case of CA between FR1 and FR2.
  Proposal:
    Measurement system shall be able to provide an uncalibrated, noise-free link for NR FR1 signals to the DUT.
    No performance verification for joint CA between FR1 + FR2.

## Slide 6: Other identified open issues
Noise-free scenarios support
  For some TCs like SDR the emulation of test condition without additional AWGN is necessary
  Proposal:
    UE demodulation test setup shall support emulation of noise-limited and noise-free test conditions.
TE Tx EVM
  Proposal:
    Reuse the same approach as for LTE. Measurement system shall support TX EVM not worse than [6%] for QPSK/16QAM/64QAM performance requirements
    Tx EVM is defined at the reference point (see slide 2)
    Next step is to identify feasible power levels for the TE

## Slide 7: Other identified open issues
SS-RSRPB measurements
  Background: Side conditions (e.g. SNR) for SS-RSRPB measurements at the UE are undefined and need to be clarified for accuracy analysis
  Proposal:
    SS-RSRPB measurements and reporting are done under noise-free conditions and use static channel conditions.
    The power level at which SS-RSRPB measurement is conducted is FFS.