## Slide 1: WF on NR PUSCH demodulation requirements
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#86bis
Montreal, Canada, July 2nd – 6th 2018
Agenda: 5.4.2.2
R4-1809108
Document for: Approval

## Slide 2: Test scope and performance metric
RAN4 should focus on the basic PUSCH performance in fading channels for BS demodulation requirements.

## Slide 3: PUSCH configurations for the performance tests
PUSCH requirements for CP-OFDM are defined firstly. The requirements for SC-FDM can be defined after the tests for CP-OFDM is finished.
PUSCH performance requirements are only defined for codebook based transmission scheme with 1Tx and 2Tx.
  For 2Tx, requirements are defined for both 1-layer and 2-layer transmission.
RS
  The performance requirements are only defined for DMRS type 1 without additional DMRS.
  PTRS configuration shall be used for defining performance requirements for FR2.
PUSCH performance requirements are defined for both types of time domain resource allocation. RAN4 needs to down-select the symbol lengths to be tested. 14 OFDM symbols for RA type A and 11 OFDM symbols for RA type B can be used for the initial discussion.

## Slide 4: FRC for PUSCH performance tests
SCS
  FR1: 15kHz, 30kHz
  FR2: 60kHz, 120kHz
PUSCH with full cell BW allocation
  15kHz SCS: 5, 10, 15, 20MHz
  30kHz SCS: 10, 20, 40, 80, 100MHz
  60kHz SCS: 50, 100, 200, 400MHz
  120kHz SCS: 50, 100, 200, 400MHz
Modulation orders and code rate
  Pi/2-BPSK (for SC-FDM only): FFS
  QPSK: [4]
  16QAM: [16]
  64QAM: [25]

## Slide 5: Other parameters for PUSCH performance tests
Code block group based PUSCH is disabled
Frequency hopping is disabled
Limited buffer rate matching is disabled
Number of HARQ retransmissions is 4

## Slide 6: Simulation assumptions
Parameter | Value |  | Remarks
 | FR1 | FR2 | 
MCS index | QPSK: [2 or 4] 16QAM: [13 or 16] 64QAM: [25] | QPSK: [2 or 4] 16QAM: [13 or 16] 64QAM: [25] | 
Carrier frequency (GHz) | 4 | 30 | 
Propagation channel | AWGN | AWGN | 
Time offset | Not modelled | Not modelled | 
Freq_offset | Not modelled | Not Modelled | 
Parameter | Value |  | Remarks
 | FR1 | FR2 | 
Transform precoding | Disabled | Disabled | 
Transmission scheme | Codebook based | Codebook based | 
Number of Tx | 1,2 | 1 | no transparent Tx diversity considered
Number of Rx | 2,4,8 | 2 | number of diversity branches in baseband
Number of layers | 1,2(2TX only) | 1 | 
DMRS type | Type-1; | Type-1; | 
Number of DMRS symbols | 1 front-loaded | 1 front-loaded | 
Time domain resource allocation type | Type A | Type A and/or Type B | 
PUSCH symbol length | 14 OFDM symbols | RA Type A: [14 ] OFDM symbols RA Type B: [11] OFDM symbols | 

## Slide 7: Simulation assumptions
Parameter | Value |  | Remarks
 | FR1 | FR2 | 
MCS index | QPSK: [2 or 4] 16QAM: [13 or 16] 64QAM: [25] | QPSK: [2 or 4] 16QAM: [13 or 16] 64QAM: [25] | 
Carrier frequency (GHz) | 4 | 30 | 
Propagation channel | AWGN | AWGN | 
Time offset | Not modelled | Not modelled | 
Freq_offset | Not modelled | Not Modelled |