## Slide 1: 3GPP TSG-RAN WG4 Meeting #87 Busan,Korea, May 21~May 25, 2018
Ericsson
Way forward on NR PRACH demodulation requirements
R4-1809369

## Slide 2: PRACH requirements
There are no test cases for Restricted sets in Rel-15
Preamble Format (For Rel-15)
  For long sequence, requirements are defined for:
    Format 0
    FFS for format 1 and Format 3
  For short sequence, the following formats will be considered, but further down selection is needed:
    A1, A2, A3, B4, C0 and C2
  SCS:
    15kHz
    30kHz
    60KHz (FR2)
    120KHz
Apply the performance requirements based on BS declare

## Slide 3: Simulation Assumption
SCS and bandwidth
  15kHz, 10MHz
  30kHz, 40MHz
  60KHz (FR2), 100 MHz
  120KHz, 100MHz
Channel:
  AWGN
Antenna configuration
  1 Tx, 2 Rx
Ncs
  Format 0: Ncs=[13] and v=22(for simulation alignment)
  Short sequence
    FFS: Ncs, v = [0]