## Slide 1: WF on UE UL transmission after measurement gap
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#86bis
Montreal, Canada, July 2nd – 6th 2018
Agenda: 5.3.2.1
R4-1809406
Document for: Approval

## Slide 2: Background
For LTE, the following UE behavior is specified in 36.133:
In the uplink subframe occurring immediately after the measurement gap, - if the following conditions are met then it is up to UE implementation whether or not the UE can transmit data: - all the serving cells belong to E-UTRAN TDD; - if the subframe occurring immediately before the measurement gap is an uplink subframe. - Otherwise the UE shall not transmit any data. In determining the above UE behaviour in the uplink subframe occurring immediately after the measurement gap the UE shall treat a special subframe as an uplink subframe if the special subframe occurs immediately before the measurement gap
For NR, the corresponding UE behavior has not been agreed.

## Slide 3: WF
RAN4 try to define deterministic UE behavior for UL transmission after measurement gap, i.e. define UE behavior in the way such that network knows whether UE will transmit or not under certain conditions.
Following aspects should be considered when defining the UE behavior:
  UE measurement time and re-tuning time if UE transmits UL after gap
  NR measurement being based on SMTC window
  MGTA (measurement gap timing advance) in NR
  Flexible UL/DL assignment of symbols in NR
  NR symbol length depending on SCS
  UL-DL and DL-UL switching time in NR
Companies are encouraged to bring inputs for RAN4#88.