## Slide 1: RRC - RAN5#87-e (May-20) SA NR (Option 2)
Progress
  Maintenance of 33 RRC Test case CR’s were agreed
  2 NR-DC test cases have been agreed along with 2 other new RRC TC, 1 test was voided.
  Data Path verification procedure has been added for CA tests in 38.508-1, completion status of CA tests has been updated.
  Below is the update of CA Freq addition in TS 38.508-1
    Note 1: No SIG test frequencies for FR2 Intra-Band Non-Contiguous CA introduced in TS 38.508-1 clause 6.2.3.4 yet.
    Note 2: No NR CA FR2 Inter-band configurations defined in TS 38.101-2 yet in Rel-15 or Rel-16.
Open issues for RAN5 attention
  FR2 power levels are missing in certain test cases
  Data path verification needs to be added for several test cases
Frequency range | NR CA Intra-band Contiguous | NR CA Intra-Band Non-Contiguous | NR CA Inter-band
FR1 | Ready | Ready | Ready
FR2 | Ready | Not Ready (Note 1) | Not Ready (Note 2)
FR1+FR2 | N/A | N/A | Ready

## Slide 2: RRC - RAN5#87-e (May-20) EN-DC (Option 3)
Progress
  Maintenance of 15 RRC Test case CR’s were agreed along with 2 new additions
  Data Path verification procedure has been added for CA tests in 38.508-1, completion status of CA tests has been updated.
  Below is the update of CA Freq addition in TS 38.508-1
    Note 1: No SIG test frequencies introduced in TS 38.508-1 clause 6.2.3.4 yet.
    Note 2: No NR CA FR2 Inter-band configurations defined in TS 38.101-2 yet in Rel-15 or Rel-16.
Open issues for RAN5 attention
  FR2 Power levels are missing for few test cases
  Data path verification needs to be added for several test cases
NR Frequency range | EN-DC with 2CC NR CA Intra-band Contiguous | EN-DC with 2CC NR CA Intra-Band Non-Contiguous | EN-DC with 2CC NR CA Inter-band
FR1 | Ready | Not Ready (Note 1) | Ready
FR2 | Ready | Not Ready (Note 1) | Not Ready (Note 2)
FR1+FR2 | N/A | N/A | Ready