## Slide 1: Demod/CSI reporting Performance - RAN5#87-e (May-20) SA NR (Option 2)
Progress – Current WP completion at 90%
  For DEMOD and CSI, SA and NSA test cases are combined in the same test case except for SDR test cases. Same status as NSA applies
Open issues for RAN5 attention
  same as NSA

## Slide 2: Demod/CSI reporting Performance - RAN5#87-e (May-20) EN-DC (Option 3)
Progress - Current WP completion at 91%
  FR1
    CRs with critical corrections/updates impacting already GCF/PTCRB validated test cases were agreed in this meeting.
    1 additional FR1 test case is now 100% complete
    Target for remaining FR1 test cases moved to RAN5#88-e.
  FR2
    The wireless isolation procedure for FR2 UE direction search was updated.
    For mode 1 scenarios with baseband combining, most of the MU element values were finalized.
    For mode 2 scenarios, it was agreed to reuse MU values from REFSENS scenario for some of the MU elements. Further analysis pending for rest of the MU elements.
Open issues for RAN5 attention
  MU/TT for FR2 Demod and CSI test cases