## Slide 1: Way forward on how to handle Option4 (NE-DC) test cases
CMCC, Deutsche Telekom, TIM, Qualcomm, ZTE, CATT, Orange, Spirent
3GPP TSG-RAN5 Meeting #92-e R5-215766
Electronic Meeting, 16 – 27 August 2021
0
0

## Slide 2: Background
Option 4 (NE-DC): Basing on SA (Option2), adding 4G connection as the SCG, while 5G NR connection is used as MCG.
CP
UP
4G LTE
EPC
Option 1
5G NR
5GC
Option 2
4G eLTE
5GC
Option 5
4G eLTE
5GC
Option 7
5G NR
5G NR
5G NR
5GC
Option 4
4G eLTE
4G LTE
EPC
Option 3
5G NR
SA
Observation 1: All the UEs supporting Option 4 also support Option 2 as default.

## Slide 3: Background
For the operators who feel interested in Option 4, almost certainly they own lots of legacy 4G LTE eNBs. These legacy 4G LTE eNBs can support both Option 1 and Option 4 by software upgrading.
Considering the coverage of 5G NR is still growing, 4G LTE coverage is necessary to support both 5G NR/4G LTE UEs and 4G LTE only legacy UEs.
4G LTE is very necessary for the roaming of 5G NR/4G LTE UEs and 4G LTE only UEs.
Observation 2: It is reasonable to assume an Option 4 UE will also support 4G LTE.
Proposal 1: To use the assumption of “an Option 4 UE will also support 4G LTE with EPC” as the premise for the RAN5 test cases defining unless there is justified industry needs to request RAN5 to define test cases for Option 4 ONLY UEs which do not support 4G LTE with EPC.

## Slide 4: Option 4 (NE-DC) RF test cases
Proposal 2: If there is no exception requirements applicable to NR or LTE, no test case details are needed to specified. Separate test cases for Option 4 NE-DC are still needed but only with general descriptions in the test cases to indicate neither NR carrier(s) nor LTE carrier(s) needs to be tested again.
  For NR carrier, the corresponding TS 38.521-1/-2 Option 2 RF test cases apply. i.e. UE is considered to meet the requirements when tested either in Option 2 or Option 4 mode for the same set of NR bands
  For LTE carrier, the corresponding TS 36.521-1 LTE RF test cases apply. i.e. UE is considered to meet requirements when tested either in LTE or Option 3 or Option 4 for the same set of LTE Bands

## Slide 5: Option 4 (NE-DC) RF test cases (Contd.)
Observation 3: “For an inter-band combination between LTE and NR, its EN-DC and NE-DC configuration have the same band combination specific requirements (i.e., ΔTIB,c, ΔRIB,c, Spurious emission, UE co-existence and MSD)” [1]
Proposal 3: If there are exception requirements applicable to NR or LTE, specific Option 4 RF test cases are needed. Noting that UE is considered to meet the exceptional requirements, testing in any one of the modes ( Option 3, Option 2 or Option 4) for the same set of NR and LTE bands
  Test descriptions for EN-DC combinations should be reused/referred for NE-DC combinations as much as possible.

## Slide 6: Option 4 (NE-DC) RRM test cases
Observation 4: The Option 4 RRM core requirements have been completed in TS 38.133.
Observation 5: No Option 4 RRM test cases in TS 38.133 yet.
Observation 6: For Option 3 (EN-DC), there are about 100 RRM test cases in Rel-15 TS 38.133.
Proposal 4: To suspend the kick-off of Option 4 RRM work in RAN5, until there is some reasonable progress in Option 4 RRM test cases in RAN4. LS to RAN4 should be considered to coordinate the Option 4 RRM work between RAN5 and RAN4.

## Slide 7: Option 4 (NE-DC) Demod test cases
Observation 7: The existing NSA test cases can apply to both Option 3 (EN-DC) and Option 4 (NE-DC) Demod tests.
Proposal 5: To make the corresponding rewording to enable the applicability of the existing test cases to both Option 3 (EN-DC) and Option 4 (NE-DC) if necessary. New test cases are needed for SDR (Sustained Data Rate).

## Slide 8: Option 4 (NE-DC) SIG test cases (1/2)
Proposal 6: Quite a few existing Option 2 protocol test cases in TS 38.523-1 can also be applied to Option 4 without any additional wording changes, and NO new separate Option 4 protocol test cases are needed for the following cases
  For protocol Layer 2, the corresponding basic test cases of MAC, RLC and PDCP integrity protection, PDCP Ciphering and deciphering, SDAP etc. in TS 38.523-1 clause 7 are applicable to both Option 4 and Option 2.
  With the configuration of 5GC and NR, the corresponding test cases in TS 38.523-1 clause 6, 9, 10, 11(e.g. 11.3 UAC and 11.4 Emergency Services) are applicable to both Option 4 and Option 2.
Notes: the test case dose not need to be executed for Option 4 if it has been executed for Option 2 already.

## Slide 9: Option 4 (NE-DC) SIG test cases (2/2)
Proposal 7: The separate test cases for NE-DC are needed to capture NE-DC conditions and Option 4 specific message contents, even if they just refer back to the existing Option 2 test cases with different conditions and/or specific message contents.
  For protocol Layer 2, PDCP Uplink Routing / Split DRB and PDCP Handover in TS 38.523-1 clause 7
  For Multi-layer, HO test cases for Option4 are needed in TS 38.523-1 clause 11
Proposal 8: Some complete new specific Option 4 protocol test cases are needed.
  For protocol RRC, the corresponding Option 4 test cases are needed in TS 38.523-1 sub-clause 8.2 (i.e. SCG addition, modification and release; Bearer Modification; Measurement).

## Slide 10: Option 4 (NE-DC) general issues
  Proposal 9: Option 4 Specific IE contents (e.g. 4.6), Generic procedures (e.g. 4.5) and Test states (e.g. 4.4A) are needed in TS 38.508-1.
  Proposal 10: Option 4 Specific UE ICS are needed in TS 38.508-2.
  Observation 8: Quite a few “NSA” in the existing RAN5 specs means “EN-DC only” rather including “NE-DC”.
  Proposal 11: To review the wording of “NSA” in RAN5 specs and to make necessary changes for clarification.

## Slide 11: Option 4 (NE-DC) Positioning test cases
  TS 37.571-1 (Minimum Performance)
    For (old) Rel-15 RAT-dependent technologies: as Proposal 5: To make the corresponding rewording to enable the applicability of the existing test cases to both Option 3 (EN-DC) and Option 4 (NE-DC) if necessary.
    For (new) Rel-16 RAT-dependent technologies: as Proposal 4: To suspend the kick-off of Option 4 work in RAN5.
    For RAT-independent positioning e.g. A-GNSS: as Proposal 5.
  TS 37.571-2 (Signalling)
    Existing test cases apply and are already Option 4-ready. Just need the signalling procedure to be defined in TS 38.508-1.
  TS 37.571-3 (ICS)
    Proposal 12: Specific Option 4 ICS and updates are needed in TS 37.571-3 .

## Slide 12: Reference
[1] R4-2005194 WF on introducing NE-DC combinations into specs, Samsung, RAN4#94-e-bis
[2] RP-210304 Finalization of missing 5G architecture Option 4 work in RAN, Deutsche Telekom, BT, Telecom Italia, RAN#91-e
[3] RP-210305 Additional 5G architecture Option 4 NE-DC combinations
for immediate standardization, Deutsche Telekom, RAN#91-e

## Slide 13: Thank you!