## Slide 1: Updates on SW Implementation on Machine Readable PICS and Applicability​
Qualcomm
3GPP TSG-RAN5 Meeting #104
Maastricht, Netherlands, 19th Aug 2024 - 23rd Aug 2024
R5-244187

## Slide 2
Updates, Agenda for Discussion
Recap: Industry Value and Progress till date
Machine Readable PICS (TS 38.508-2) updates
[New] - Machine Readable Release of Applicability Spec to facilitate automation
Procedural Proposals and overall W/F
Notes: Building Blocks – Code translating Specs into excel

## Slide 3: Background – Overall Industry value
Progress Updates – Key Milestones:
Based on proposal in R5-233200 and outcome in RAN5#99, a separate exploder has been created - 3GPP_TSG_RAN_WG5_APPLICABILITY
Green items above now have Prototype SW Implementation as demonstrated in RAN5#100 - R5-234320
As per outcome of R5-237464 in RAN5#101, it was agreed to explore providing the solution in steps, with initial focus on releasing machine readable PICS
Post RAN5#103, the Machine-Readable PICS derived from the latest TS38.508-2 vi30 released in the draft spec folder
3GPP RAN5 Defined Test Case List
Extracted OEM PICSTS 38.508-2
Extracted Applicability Conditions
TS 38.523-2
Protocol
TS 38.522
RF+Perf (RRM, Demod)
OEM Augments Band, CA and other Information
TS 34.229-2
IMS (5G, 4G)
Output = No. of Applicable Tests per Device Capability
(All Automated in RAN5)
Execution Rules (Cert Industry Logic)
Final List of Test Cases
Notes: Building blocks as an input to the 3rd automation SLIDE

## Slide 4
Machine Readable PICS - Updates
Update towards RAN5 to endorse creation of “machine readable PICS” during every spec release of TS 38.508-2
  Based on the final version of TS38.508-2 post RAN5#103, the machine-readable PICS file is shared with the applicability reflector and in the 3GPP shared site
  No further formatting issues found in spec, both spec and code are now stable.
Logistics of Release
  Location of Release – 3GPP Forge or as attachment to TS 38.508-2
  Ownership - Generation of Machine-Readable PICS – QC shared the code with ETSI
Further improvements to excel translation
  Add Table “Notes” in excel

## Slide 5
Machine Readable Applicability - Proposal
Several Challenges noted in earlier proposed full SW Automation of determining Test Case list – Industry Appetite, reliability, maintenance, development and usage
Strategy change from “RAN5 Specification which are SW implementable shall be provided as a SW” to “RAN5 Specification which are SW implementable shall be provided in Machine Readable form” to facilitate external automation.
This simplified approach enables external automation still providing deterministic test output with reliable implementation of PICS and Applicability spec
RAN5
Machine Readable PICS
(TS 38.508-2)
RAN5
Machine Readable Applicability Spec
(TS 38.523-2, TS 38.522, TS 34.229-2 etc)
External Automation

## Slide 6
Tool generated Column G for easier condition evaluation for both Tool and Human user
Column A, B, C, D and E follows the same format/ Column G is translated to human readable format
Logics in Column D or G can implement to facilitate external automation
Machine Readable Applicability – Example Output TS 38.523-2

## Slide 7
Proposals
Official RAN5 endorsement of Machine-Readable PICS TS38.508-2
Simplified Logistics for ETSI to help with generation of the Machine-Readable PICS TS 38.508-2
New Machine-Readable Applicability proposals limits RAN5 scope to provide clean\implementable excel translations of Applicability specs
Further work to implement Machine Readable Applicability Specifications to be driven by further industry interest and volunteers
Implementation of Applicability Specs to follow TS 38.508-2 Machine Readable process

## Slide 8
References:-
RAN5#99
    R5-233200 SW Implementation of RAN5 Applicability
  RAN5#100
  R5-234320 Progress on Proposal-1 : SW Implementation of NR Applicability Specs
RAN5#101
  R5-237464 - Discussion – Software Implementation of NR Applicability Specifications -SIG - Conclusions and Next Steps
  R5-237465 - Discussion – Software Implementation of NR Applicability Specifications - RF Updates, Conclusions and Next Steps
RAN5#102
  R5-240664 - Way Forward on SW Implementation on Machine Readable PICS and Applicability
RAN5#103
  R5-242560 - Way Forward on SW Implementation on Machine Readable PICS and Applicability

## Slide 9: Supporting Slides

## Slide 10: Tool Generated Machine Readable PICS File (Now Released in RAN5)
Shared with Applicability Reflector
Tool generated Column B for easier condition evaluation for both Tool and Human user
Column C and onward columns exactly follow the 38.508-2 format

## Slide 11: Applicability Translation Steps/Example