## Slide 1: Discussion on allowed power relaxation for different features
ZTE Corporation
3GPP TSG-RAN5 Meeting #104 R5-244935 Maastricht, Netherlands, August 19 – 23, 2024

## Slide 2: Definition for symbol ΔTIB,c
Symbols in TS 38.521-1:
The symbol ΔTIB,c is used for the additional tolerance for serving cell as specified for NR CA, for SUL, or for EN-DC. The UE is allowed to set its configured maximum output power by using the symbol ΔTIB,c..
The following texts have been appeared for the test of transmitter power in many sub-clauses in 38.521-1.
  For the UE which supports inter-band NR CA configuration, inter-band NR-DC configuration, SUL configuration or inter-band EN-DC configuration, ΔTIB,c as specified in 6.2A.4.0.2 for NR CA, 6.2B.4.0.2 for NR-DC, clause 6.2C.2 for SUL, or TS 38.521-3 [14] clause 6.2B.4.2 for EN-DC applies. Unless otherwise stated, ΔTIB,c is set to zero.
  In case the UE supports more than one of band combinations for CA, NR-DC, SUL or EN-DC, and an operating band belongs to more than one band combinations then
    When the operating band frequency range is ≤ 1 GHz, the applicable additional ΔTIB,c shall be the average value for all band combinations defined in clause 6.2A.4.0.2, 6.2B.4.0.2, 6.2C.2 in this specification and 6.2B.4.2 in TS 38.521-3 [14], truncated to one decimal place that apply for that operating band among the supported band combinations. In case there is a harmonic relation between low band UL and high band DL, then the maximum ΔTIB,c among the different supported band combinations involving such band shall be applied.
    When the operating band frequency range is > 1 GHz, the applicable additional ΔTIB,c shall be the maximum value for all band combinations defined in clause 6.2A.4.0.2, 6.2B.4.0.2, 6.2C.2 in this specification and 6.2B.4.2 in TS 38.521-3 [14] for the applicable operating bands..
The same texts also appear in TS 38.101-1 for the configured transmitted power for single carrier and CA in clause 6.2.4 and 6.2A.4.

## Slide 3: ΔTIB,c in TS 38.521-1
The main purpose of introducing the above mentioned texts is how to handle the ΔTIB,c for the cases when the UE supports more than one of band combination, and an operating band belongs to more than one band combination.
However, the same texts appear in different sub-clauses in TS 38.521-1 for more than 41 times when testing the transmitter power for different features on band combinations which is highlighted as below.
Observation 1. The texts for how to handle the ΔTIB,c for the cases when the UE supports more than one of band combination have been duplicated for many times in different sub-clauses in TS 38.521-1.

## Slide 4: Simplify the wordings for ΔTIB,c in TS 38.521-1
It is suggested RAN5 to consider whether so many duplicated text for ΔTIB,c in TS 38.521-1 is really needed. It is observed that if a “General” sub-clause is setup for each feature in RAN5 spec respectively, the structure of the spec will be more clear and less redundant. All common contents under the same feature can move into this “General” sub-clause not only for simplifying the wordings of ΔTIB,c in this proposal but also for the future purpose.
Proposal 1. It is suggested to move the following texts to the “General” sub-clause for each feature for the test of transmitter power in TS 38.521-1.
For the UE which supports inter-band NR CA configuration, inter-band NR-DC configuration, SUL configuration or inter-band EN-DC configuration, ΔTIB,c as specified in 6.2A.4.0.2 for NR CA, 6.2B.4.0.2 for NR-DC, clause 6.2C.2 for SUL, or TS 38.521-3 [14] clause 6.2B.4.2 for EN-DC applies. Unless otherwise stated, ΔTIB,c is set to zero.
In case the UE supports more than one of band combinations for CA, NR-DC, SUL or EN-DC, and an operating band belongs to more than one band combinations then
  When the operating band frequency range is ≤ 1 GHz, the applicable additional ΔTIB,c shall be the average value for all band combinations defined in clause 6.2A.4.0.2, 6.2B.4.0.2, 6.2C.2 in this specification and 6.2B.4.2 in TS 38.521-3 [14], truncated to one decimal place that apply for that operating band among the supported band combinations. In case there is a harmonic relation between low band UL and high band DL, then the maximum ΔTIB,c among the different supported band combinations involving such band shall be applied.
  When the operating band frequency range is > 1 GHz, the applicable additional ΔTIB,c shall be the maximum value for all band combinations defined in clause 6.2A.4.0.2, 6.2B.4.0.2, 6.2C.2 in this specification and 6.2B.4.2 in TS 38.521-3 [14] for the applicable operating bands..
(Opt.1)
(Opt.2)
Proposal 2. To make the description of ΔTIB,c more clear for each feature, it is suggested to select Opt.2 to simplify the test of transmitter power.

## Slide 5: Thank you!