## Slide 1: Introduction of New R16 IDC Test Case
China Mobile
3GPP TSG-RAN5 Meeting #104 R5-245466
Maastricht, NL, Aug 19th - Aug 23th, 2024

## Slide 2: Background of R16 IDC new test case
Observation 1.1: RAN2 introduced a NR IDC solution in R16 to inform network that UE is experiencing IDC problems that cannot be solved by itself. Basing on the IDC assistance information provided by the UE, the network may take some actions to help UE to fix the IDC problem.
Observation 1.2: If UE is configured to provide IDC assistance information, and UE did not transmit a UEAssistanceInformation message, UE transmits UEAssistanceInformation message.
Observation 1.3: If UE is configured to provide IDC assistance information, the UE transmits a UEAssistanceInformation message before, but the current IDC information is different from the one reported previously, UE transmits UEAssistanceInformation message
R16 IDC solution
Notes: RAN2 introduced a NR IDC solution in R16 to inform network that UE is experiencing IDC problems that cannot be solved by itself. Basing on the IDC assistance information provided by the UE, the network may take some actions to help UE to fix the IDC problem.

## Slide 3: Why do we need to introduce R16 IDC new test case now?
Observation 2.1: The earliest NR IDC solutions were introduced by a TEI16 CR into TS 38.331 in R16, and it only focus on NR FDM solution.
Observation 2.2: There was no R17 IDC WI.
Observation 2.3: In R18 IDC WI, enhanced FDM solution was introduced to provide more information of affected frequencies, and also to support NR-DC scenarios. Besides, TDM solution was also introduced to handle which alternative non-interfered frequencies are not available.
Observation 2.4: R18 “NR_IDC_enh-UEConTest” is the first IDC WI in RAN5. To ensure the integrity of the IDC related tests and further support R18 IDC solutions, it is necessary to introduce R16 IDC test case based on the IDC features introduced in R16 core spec.
RAN5 NR_IDC_enh-UEConTest

## Slide 4: Introduction of R16 IDC new test case
Observation 3.1: R16 IDC test case is introduced by R5-244515 with two TPs.
TP1 is for the scenario that UE did not transmit a UEAssistanceInformation message before.
TP2 is for the scenario that UE already transmitted a UEAssistanceInformation message before, and UE transmits a UEAssistanceInformation message again when the current idc-Assistance information is different from the previous one.
TP for R16 IDC solution
Proposal 1: RAN5 agrees to introduce the R16 IDC related TCs into TS 38.523-1 with TEI16_Test WIC to align with RAN2 core spec TS 38.331.
Observation 3.2: RAN2 introduced the R16 IDC solution into TS 38.331 via a TEI16 CR without any specific R2 WI .

## Slide 5: Thank you!