## Slide 1: Discussion on introducing SUL with Inter-band CA configuration in RAN5
Huawei, HiSilicon
3GPP TSG-RAN5 Meeting #104 R5-245813
Maastricht, Netherlands, Aug 19-23, 2024

## Slide 2: Applicable configurations
This discussion paper is focused on how to introduce Inter-band CA+SUL configurations into RAN5 specification and what updates are needed in RF test aspects.
Example configurations (ongoing in PRD21):
Observation 1:
  The UL configuration of inter-band CA+SUL band combo can be classified into two categories:
  1) NUL band + SUL band combination; 2) NUL band(s) UL CA
Observation 2:
  For Category 2 in Observation 1：Considering SUL band has no downlink, when the UL configuration consists of NUL band(s) UL CA, the Tx requirements could be covered by testing corresponding UL CA test cases.
Conclusion 1:
  Only Need to check if existing SUL test cases are applicable for inter-band CA+SUL band combo with UL SUL configuration, i.e. CA_n41C_n79A-n83A (UL: SUL_n79A-n83A)
SUL band combination with CA | UL configuration | Type | Number of CCs
CA_n28A_n41A-n83A | SUL_n41A-n83A | Inter-band CA + SUL | 3
CA_n41C_n79A-n83A | SUL_n79A-n83A CA_n41C CA_n41A-n79A | Intra-band + Inter-band CA + SUL | 4

## Slide 3: Tx requirements - Transmitter power for SUL (6.2C)
Minimum requirements in TS 38.101-1
6.2C.1 Configured transmitted power for SUL
When a UE is configured with both NR UL and NR SUL carriers in a serving cell with active transmission either on the UL carrier(s) or SUL carrier, the configured transmit power requirements specified in clause 6.2.4 and 6.2A.4 are applicable for the UL carrier(s) and the SUL carrier, respectively.
Current RAN5 test case in TS 38.521-1
clause | title | Applicable for the SUL carrier in CA+SUL configuration
6.2C.1 | Configured transmitted power for SUL | Yes
6.2C.3 | UE maximum output power for SUL | Yes
6.2C.4 | UE maximum output power reduction for SUL | Yes
6.2C.5 | UE additional maximum output power reduction for SUL | Yes
Observation 3:
The minimum requirements are referred back to clause 6.2.4 for SUL carrier. No config-specific requirements are defined for inter-band CA+SUL configurations.
Observation 4:
The downlink configurations in test cases in 6.2C for SUL test cases are N/A. And they are applicable for inter-band CA+SUL configurations when the uplink config is NUL band + SUL band combination.
Conclusion 2:
No need to introduce new test case in clause 6.2C.

## Slide 4: Tx requirements - Output power dynamics for SUL (6.3C)
Minimum requirements in TS 38.101-1 (for CA+SUL configuration)
Current RAN5 test case in TS 38.521-1
clause | title | Applicable for the SUL carrier in CA+SUL configuration
6.3C.1 | Minimum output power for SUL | Yes
6.3C.3.1 | General transmit ON/OFF time mask for SUL | Yes
6.3C.3.4 | General transmit ON/OFF time mask for switching between one uplink band with one transmit antenna connector and one uplink band with two transmit antenna connectors | Yes
6.3C.3.5 | General transmit ON/OFF time mask for switching between two uplink bands with two transmit antenna connectors | Yes
6.3C.3.6 | Time mask for switching across three uplink bands | Yes
6.3C.3.7 | Time mask for switching across four uplink bands | No applicable configurations in RAN5
6.3C.4 | Power control for SUL | Yes ,but single downlink carrier is configured in PUCCH subtest in 6.3C.4.3
Observation 5:
No band-combo specific requirements in this clause.
Observation 6:
The downlink configurations in test cases in 6.3C are N/A except PUCCH subtest in 6.3C.4.3 where single DL carrier is configured.
Configuring single DL carrier is enough for testing PUCCH on SUL carrier for SUL + inter-band CA configuration.
Conclusion 3:
Existing test cases in 6.3C well covered the requirements specified in TS 38.101-1.
No need to introduce new test case in clause 6.3C
6.3C.3.3 | Time mask for switching between one uplink band with one transmit antenna connector and one uplink band with two transmit antenna connectors
6.3C.3.4 | Time mask for switching between two uplink bands with two transmit antenna connectors
6.3C.3.5 | Time mask for switching across up to four uplink bands
6.3C.3.5a | Additional requirements for three-band switching with dual TAG

## Slide 5: Tx requirements - Transmit signal quality for SUL (6.4C)
Minimum requirements in TS 38.101-1
For the UE which is configured with both NR UL and NR SUL carriers in a serving cell with active transmission either on the UL carrier(s) or SUL carrier, the transmit signal quality requirements specified in clause 6.4.2 are applicable for the UL carrier(s) and the SUL carrier, respectively.
Current RAN5 test case in TS 38.521-1
Observation 7:
The minimum requirements are referred back to clause 6.4.2 for SUL carrier. No config-specific requirements are defined for CA+SUL configurations.
Observation 8:
The downlink configurations in test cases in 6.4C are N/A except test case 6.4C.1, 6.4C.2.1 and 6.4C.2.3 where single DL carrier is configured;
Configuring single DL carrier is enough for testing PUCCH on SUL carrier for SUL + inter-band CA configuration
Conclusion 4:
Existing test cases in 6.3C well covered the requirements specified in TS 38.101-1. No need to introduce new test case in clause 6.4C.
clause | title | Applicable for the SUL carrier in CA+SUL configuration
6.4C.1 | Frequency error for SUL | Yes, but single downlink carrier is configured in test case 6.4C.1
6.4C.2.1 | Error Vector Magnitude for SUL | Yes, but single downlink carrier is configured in test case 6.4C.2.1
6.4C.2.2 | Carrier leakage for SUL | Yes
6.4C.2.3 | In-band emissions for SUL | Yes, but single downlink carrier is configured in test case 6.4C.2.3
6.4C.2.4 | EVM equalizer spectrum flatness for SUL | Yes
6.4C.2.5 | EVM equalizer spectrum flatness for Pi/2 BPSK for SUL | Yes

## Slide 6: Rx requirements - Reference sensitivity for SUL (7.3C)
Minimum requirements in TS 38.101-1
REFSENS without exception: For SUL operation with downlink CA, the reference receive sensitivity (REFSENS) requirement for downlink bands specified in clause 7.3A.2 shall be met for an uplink transmission bandwidth less than or equal to that specified in Table 7.3.2-3 or supplementary uplink transmission bandwidth less than or equal to that specified in Table 7.3C.2-1 with reference measurement channels as specified in Annexes A.2.2.2, A.3.2, and A.3.3 (with one sided dynamic OCNG Pattern OP.1 FDD/TDD for the DL-signal as described in Annex A.5.1.1/A.5.2.1), unless sensitivity degradation is allowed in this clause of this specification. These exceptions also apply to any higher order CA or DC combination containing one of the exception combinations in this clause as subset.
MSD due to uplink harmonic: For the UE that supports any of the SUL operation given in Table 7.3C.2-2, exceptions to the requirements specified in Table 7.3.2-1a and Table 7.3.2-1b are allowed for different combinations of UL configurations and DL channel bandwidths when the uplink is active in a lower frequency band and is within a specified frequency range such that transmitter harmonics fall within the downlink transmission bandwidth assigned in a higher band as noted in Table 7.3C.2-2. For these exceptions, only the listed test points in Table 7.3C.2-2 are needed to be tested.
MSD due to cross band isolation: For the UE that supports any of the SUL operation given in Table 7.3C.2-4, reference sensitivity degradation is allowed for different combinations of UL configurations and DL channel bandwidths when a DL band is impacted by UL band due to cross band isolation issues. For these exceptions, only the listed test points in Table 7.3C.2-4 are needed to be tested.
Current RAN5 test case in TS 38.521-1
Observation 9:
In TS 38.101-1: the REFSENS without exceptions for DL CA bands are referred back to clause 7.3A.2.
MSD requirements defined in Table 7.3C.2-2 and 7.3C.2-4 are for two-band SUL configuration.
Basically, REFSENS testing for inter-band CA+SUL configuration can be covered by testing 7.3.2 / 7.3A.1 and 7.3C.2
Observation 10:
No applicable clause for 4CC inter-band CA+SUL configurations. (i.e CA_n41C_n79A-n83A).
A new test case 7.3C.4 Reference sensitivity power level for SUL (4CC) need to be introduced into TS 38.521-1.
clause | title | Applicable for the SUL carrier in CA+SUL configuration
7.3C.3 | Reference sensitivity power level for SUL (3CC) | Yes, but only for 3CC configuration Note: testing is covered by 7.3.2 and 7.3C.2

## Slide 7: Rx requirements - Blocking characteristics for SUL (7.6C)
Minimum requirements in TS 38.101-1
In-band blocking: For SUL operation with downlink CA, the in-band blocking requirement for downlink bands specified in clause 7.6A.2 shall be met.
Out-of-band blocking: For SUL operation with downlink CA, the out-of-band blocking requirement for downlink bands specified in clause 7.6A.3 shall be met.
Current RAN5 test case in TS 38.521-1
clause | title | Applicable for the SUL carrier in CA+SUL configuration
7.6C.2_1.1 | Inband Blocking for SUL with 2 DL CA | Yes, but only for 3CC configuration
7.6C.3_1.1 | Out-of-band Blocking for SUL with 2 DL CA | Yes, but only for 3CC configuration
Observation 11:
In TS 38.101-1: the Blocking requirements for inter-band CA+SUL configuration are referred back to clause 7.6A.2 or 7.6A.3 for DL CA part.
Observation 12:
No applicable clause for 4CC inter-band CA+SUL configurations. (i.e. CA_n41C_n79A-n83A).
New test case 7.6C.2_1.2 - Inband Blocking for SUL with 3 DL CA and 7.6C.3_1.2 - Out-of-band Blocking for SUL with 3 DL CA need to be introduced into TS 38.521-1.

## Slide 8: Necessary updates when introducing new CA+SUL combo
Based on above observations, following proposals are submitted:
Proposal 1：(implement in R5-244866)
For SUL with inter-band CA combination, the testing of Tx requirements can be covered by testing corresponding UL CA configuration or SUL configuration. Updating reference table numbers in existing SUL test cases to be applicable for SUL combinations with inter-band CA
Proposal 2：(implement in R5-244867)
Adding new test case 7.3C.4 Reference sensitivity power level for SUL with 3DL CA in TS 38.521-1
Proposal 3：(implement in R5-244868)
Adding new test case 7.6C.2_1.2 - Inband Blocking for SUL with 3 DL CA in TS 38.521-1
Proposal 4：(implement in R5-244869)
Adding new test case 7.6C.3_1.2 - Out-of-band Blocking for SUL with 3 DL CA in TS 38.521-1
Proposal 5:
A new SUL configuration with inter-band CA can be declared completed in PRD21 when following conditions are met:
  PICS introducing new configuration are updated in TS 38.508-2
  New configuration is introduced into TS 38.521-1 following clauses:
  All fallback configurations are marked as completed in PRD21
CA_nX_nY-nZ (3CC) | CA_nX_nY-nZ (4CC)
clauses 5.5C | 
6.2C.2 (ΔTIB,c) | 
7.3C.0.3 (ΔRIB,c) | 
7.3C.3 REFSENS for SUL (2DL CA) | 7.3C.4 REFSENS for SUL (3 DL CA) (new test case)
7.6C.2_1.1 IBB for SUL (2DL CA) | 7.6C.2_1.2 IBB for SUL (3DL CA) (new test case)
7.6C.3_1.1 OOBB for SUL (2DL CA) | 7.6C.3_1.2 OOBB for SUL (3DL CA) (new test case)

## Slide 9: THANK YOU