## Slide 1: Discussion on simplifying RF testing among different features
Huawei, HiSilicon
3GPP TSG-RAN5 Meeting #104 R5-244881r1
Maastricht, Netherlands, Aug 19-23, 2024

## Slide 2: Background
RAN4 SI: Study on simplification of band combination specification for NR and LTE (FS_SimBC, UID 950067, closed in RAN4#109)
TR 38.846 captured the RAN4 agreements on Test burden reduction for band combinations in clause 7. The general guidelines could be summarized as below:
RAN5#103: discussion paper R5-243305, prop1 is noted with comments below:
  This discussion paper is to:
    Provide more background and details for discussing test burden reductions
    Discuss the specific approach to implement test burden reduction in RAN5
Proposal 1 | Conlcusion/comments
RAN5 to consider if there is a need to develop a common test method for different features with the same frequency band combination. | prop1 needs more specific examples from ran5 spec and background for change
  Band combo specific RF requirements mainly include: MOP, Spurious emission for UE co-ex, general REFSENS and MSD
  RF implementations are similar and RF architectures can be reused for different features on the same band combination. i.e. CA_nA-nB (NR CA), DC_nA-nB (NR-DC), DC_A_nB (EN-DC), DC_B_nA (EN-DC), DC_nB_A (NE-DC), DC_nA_B (NE-DC) (different features on same band combination) can use same RF implementation
  The final decision whether to reduce testing burden should be taken by RAN5 based on the industry certification testing needs

## Slide 3: Test burden reduction for MOP – RAN4 guideline
MOP requirement for the same frequency range with different features
Part of table 7.2.1-1 in TR 38.346 :
  TR 38.346 cl.7.2.1: Taking PC3 MOP requirements for all the UL NR CA, UL NR DC, EN-DC and NE-DC band combinations in table 7.2.1-1 based on the TS 38.101-1-h60 and TS 38.101-3-h60 as an example. One band combination may be chosen to verify MOP testing for some band combinations in same row.
Uplink NR CA Configuration | Uplink NR DC Configuration | Uplink EN-DC Configuration | Uplink NE-DC Configuration | Class 3 (dBm) | Tolerance (dB)
CA_n1A-n3A | DC_n1A-n3A | DC_1A_n3A DC_3A_n1A DC_1A_n80A DC_3A_n84A | DC_n3A_1A | 23 | +2/-3
CA_n1A-n5A |  | DC_1A_n5A |  | 23 | +2/-3
CA_n1A-n7A | DC_n1A-n7A | DC_1A_n7A DC_7A_n1A |  | 23 | +2/-3
CA_n1A-n8A |  | DC_1A_n8A DC_8A_n1A | DC_n8A_1A | 23 | +2/-3
CA_n1A-n18A |  |  |  | 23 | +2/-3
CA_n1A-n20A |  | DC_1A_n20A DC_20A_n1A |  | 23 | +2/-3
CA_n1A-n28A | DC_n1A-n28A | DC_1A_n28A DC_28A_n1A | DC_n1A_28A | 23 | +2/-3

## Slide 4: Test burden reduction for MOP – RAN5 testing
MOP testing for same band combination among different features in RAN5:
  * MU/TT for the E-UTRA carrier and NR carrier are the same when the FC and CBW for E-UTRA carrier and NR carrier are same.
Observation 1:
  RAN4 guildline: different features on the same band combination have same MOP minimum requirements
  RAN5 testing aspects: except for the EN(NE)-DC configurations requiring singleUL-Transmission, MOP testing for same band combination among different features have same measurement procedure, requirements and MU/TT value.
Proposal 1: When UE supports different features on the same band combination, the measured MOP for one configuration is applicable to other remaining configurations in the group. This rule doesn’t apply when UE supporting singleUL-Transmission on certain EN-DC (NE-DC) configuration. This rule only apply to same power class for all involved configurations.
Features | NR CA | NR-DC | EN-DC | NE-DC
UL configuration type | CA_nXA-nYA | DC_nXA-nYA | DC_XA-nYA | DC_nXA-YA
Test case No. | 38.521-1 6.2A.1 | 38.521-1 6.2B.1 | 38.521-3 6.2B.1.3 | 38.521-3 6.2B.1.3a
Measured by | sum of mean transmitted power over all component carriers | sum of mean transmitted power over all component carriers | not supporting UE singleUL-Transmission: sum of mean transmitted power over all EN-DC component carriers supporting UE singleUL-Transmission: mean transmitted power over E-UTRA carrier or NR carrier | 
MU | MAX (MUCC1, MUCC2) | MAX (MUCC1, MUCC2) | MAX (MULTE, MUSA) | MAX (MULTE, MUSA)
TT | MAX (TTCC1, TTCC2) | MAX (TTCC1, TTCC2) | MAX (TTLTE, TTSA) | MAX (TTLTE, TTSA)

## Slide 5: Test burden reduction for Spurious UE co-ex – RAN4 guideline
Spurious emission UE co-existence requirement for the same frequency range with different features
Analysis of minimum requirements: The requirements are consist of…
Observation 2a:
  For a specific configuration, the protected frequency range (known as “additional requirements”) requirement is same across different releases
  Spurious UE co-ex requirements are same for the band combination among difference features , except EN-DC testing for R15 UE and NE-DC configurations without corresponding defined EN-DC.
  It’s better to ask RAN4 group to confirm that the spurious UE co-existence requirements in the future will keep in alignment across different features and releases.
  TR 38.346 cl.7.2.2: Generally, if CA_nA-nB, DC_A_nB, DC_B_nA, DC_nB_A, DC_nA_B have same spurious emission requirements for UE to UE coexistence, it may not be needed to test the spurious emission requirements for UE to UE coexistence for each UL configuration again and again. Once one of these UL configurations is verified, the other UL configurations for different feature in same band combination can be considered as being capable of meeting these requirements.
Uplink NR CA | Uplink NR DC | Uplink EN-DC | Uplink NE-DC
Intersection of requirements for the individual bands + additional protected frequency range |  | R15: defined protected band and protected frequency range | WITH corresponding defined EN-DC: same as EN-DC
 |  | R16-R18: Intersection of requirements for the individual bands + additional protected frequency range | WITHOUT corresponding defined EN-DC: defined protected band and protected frequency range

## Slide 6: Test burden reduction for Spurious UE co-ex – RAN5 testing
MOP testing for same band combination among different features in RAN5:
  * NSA only capable UE is not involved in this discussion
Observation 2b:
  RAN5 testing aspects: NE-DC spurious UE co-ex testing hasn’t been defined in RAN5. The testing results for NR CA testing applies for the same band combination of NR-DC
Proposal 2: When UE supports different features on the same band combination, the measured Spurious UE co-existence for one configuration is applicable to other remaining configurations in the group. This rule doesn’t apply to EN-DC testing for R15 UE.
Features | NR CA | NR-DC | EN-DC | NE-DC
UL configuration type | CA_nXA-nYA | DC_nXA-nYA | DC_XA-nYA | DC_nXA-YA
Test case No. | 6.5A.3.2.1 | 6.5B.3 | 6.5B.3.3.2 | 6.5B.3.3a.2
Measured by | Step by step measuring spurious emission as per the test requirement for both PCC and SCC; During measurement the spectrum analyser shall be set to 'Detector' = RMS. |  | Step by step measuring spurious emission as per the test requirement for both E-UTRA CC and NR CC; During measurement the spectrum analyser shall be set to 'Detector' = RMS. | FFS
MU | inter-band CA: same as 6.5.3.2 for each CC |  | Same as 6.5.3.2 in TS 38.521-1 | FFS
TT | 0 dB |  | 0 dB | FFS

## Slide 7: Test burden reduction for REFSENS – RAN4 guideline
Generally speaking, REFSENS requirement for a combination includes:
  general REFSENS without exceptions
  REFSENS exceptions due to 1) harmonic/harmonic mixing; 2) inter-modulation distortion; 3) cross band isolation interference
REFSENS without exception requirement for different features (inter-band):
However, the single-band REFSENS requirements are not exactly the same for E-UTRA and NR. For example:
  TR 38.346 cl.7.3.4: For band combinations DL_nA-nB_UL_nA-nB / DL_B_nA_UL_B_nA / DL_A_nB_UL_A_nB / DL_nB_A_UL_nB_A / DL_nA_B_UL_nA_B which doesn’t have any MSD requirements, it’s suggested to test one of them in order to reduce the test burden for REFSENS requirements and final decision is up to RAN5. The reason is that the same Rx RF implementation is used to achieve these band combinations.
NR CA | NR DC | EN-DC | NE-DC
Same as single-band requirements for each component carrier uplink is assigned to one NR |  | Same as single-band requirements for each E-UTRA carrier and NR carrier | NA: only REFSENS exception requirements defined
FDD E-UTRA | FDD NR | TDD E-UTRA | TDD NR
Band 3, 20MHz@15kHz: REFSENS = -91 | n3, 20MHz@15kHz: REFSENS = -90.8 | Band 41, 20MHz@15kHz: REFSENS = -92 | n41, 20MHz@15kHz: REFSENS = -91.7
Band 66, 10MHz@15kHz: REFSENS = -96.5 | Band 66, 10MHz@15kHz: REFSENS = -96.3 | Band 39, 10MHz@15kHz: REFSENS= -97 | n39, 10MHz@15kHz: REFSENS= -96.8

## Slide 8: Test burden reduction for REFSENS – RAN4 guideline
As for the REFSEN exception requirements, there’s some slight difference for NR-CA and EN-DC for the same band combination. For example:
Observation 3:
  REFSENS requirements for different features are not exactly the same. The general REFSENS for some same bands in LTE and in NR have a difference at +/- 0.2dB. Some MSD requirements are defined under different condition for NR CA and EN-DC. And some MSD requirements have different values under same condition for NR CA and EN-DC.
Proposal 3: Ask for RAN4 group to clarify the inconsistency of REFSENS requirements for the same band combinations in NR CA and EN-DC
NR CA
EN-DC

## Slide 9: Summary of Proposals
Based on above analyses, proposals for simplification on RF testing among different features can be summarized as below:
Proposal 1:
  When UE supports different features on the same band combination, the measured MOP for one configuration is applicable to other remaining configurations in the group. This rule doesn’t apply when UE supporting singleUL-Transmission on certain EN-DC (NE-DC) configuration. This rule only apply to same power class for all involved configurations.
Proposal 2:
  When UE supports different features on the same band combination, the measured Spurious UE co-existence for for one configuration is applicable to other remaining configurations in the group. This rule doesn’t apply to EN-DC testing for R15 UE.
Proposal 3:
  Ask for RAN4 group to:
    Confirm the spurious UE co-existence requirements are aligned across different features and releases
    Clarify the inconsistency for the same band combinations in NR CA and EN-DC

## Slide 10: Thank you!