## Slide 1: Discussion on handling of RAN5 AI
China Mobile, CAICT, MediaTek, ZTE, Telecom Italia, Huawei, AT&T
3GPP TSG-RAN5 Meeting #104 R5-244507
Maastricht, Netherlands, August 19 – 23, 2024

## Slide 2: Background Information
Proposal 1: RAN5 leadership to coordinate meeting TimeTables to enable RAN5 delegates with an interest in AI/ML to participate in RAN4 AI/ML discussions.
Observation 1.1: As per the approved R19 WID “NR_AIML_Air” RP-240774 [1] for the “Testability and interoperability” topic, RAN5 aspects related to testability and interoperability to be addressed on a request basis.
Observation 1.2: AIML has totally new requirements for RAN5. RAN5 needs to keep abreast of the AIML WI progress in RAN4 and do early contributions when necessary.
RP-240774

## Slide 3: “General Issues” for RAN4 AIML topics that may impact RAN5 (1/2)
As per [2], the “General issues” for RAN4 AIML topic is as below.
R4-2410570
Issue 1-1: Post deployment testing
Interested companies are invited to bring analysis on the feasibility of the options proposed so far.
Issue 1-4: Inference latency handling
Agreement:
Use the following as the starting point
n Inference latency can be implicitly captured in the delay of corresponding procedures (e.g. reporting delay) and/or performance requirements.
n Inference latency is part of delay of the corresponding procedure and no separate requirement will be specified for inference latency.
Check the above bullets based on per use case, and if other WGs define the inference latency, RAN4 can revisit the above bullets.
Observation 2: Being quite different from the traditional UEs, considering AIML models will be constantly updated after the devices are officially announced, AIML UEs will need a brand new conformance testing/certification methodology. RAN5 has rich experiences in UE conformance testing/certification, which will probably be very helpful to devise a new scheme to test/certify AIML models before and/or after the AIML devices hit the market.

## Slide 4: “General Issues” for RAN4 AIML topics that may impact RAN5 (2/2)
Proposal 2: RAN5 should consider to join RAN4 discussion on Issue 1-1.
Issue 1-5: LCM Requirements
Agreement:
n RAN4 considers defining RRM requirements for LCM procedures based on the specific use cases (beam management and positioning), and candidates are:
· identification
· selection
· activation
· deactivation
· switching
· fallback to non-AI operation
· performance monitoring
· Others are not precluded
Issue 1-6: Legacy RRM requirements handling
Agreement:
UE shall meet all legacy RRM requirements (non-AI/ML) even during the AI/ML operation mode.
R4-2410570

## Slide 5: “Testability and interoperability issues for beam management” for RAN4 AIML topics that might impact RAN5 (1/2)
As per [2], the “Testability and interoperability issues for beam management” for RAN4 AIML topic is as below.
Issue 2-3: Reported measurements and ground truth
Agreement:
n The ground truth for the predicted RSRP is the ideal measurement of RSRP on the predicted Tx beam
n In RAN4, the ground truth is the approximate as the reported RSRP measurement under the certain SNR on the predicted Tx beam
u FFS on SNR level to ensure that SNR is high enough for sufficient accuracy of reported RSRP
u FFS on impact of multiple-AoA test setup
u FFS on the channel condition
u FFS on whether the ground truth will be changing or not
Other solutions are not precluded
R4-2410570
Observation 3.1: It deserves RAN5’s early attention on the following items to avoid potential testability issues, including
  SNR power level is high enough
  impact of multiple-AoA test setup
  the channel condition
  whether the ground truth will be changing

## Slide 6: “Testability and interoperability issues for beam management” for RAN4 AIML topics that might impact RAN5 (2/2)
Issue 2-5: Test setup needs
Agreement:
maximum number of set B Tx beams that test system should be able to emulate: [8-16]
maximum number of set A Tx beams that test system should be able to emulate: [64-128]
FFS on AoAs
UE rotation during the test: FFS
UE rotation/repositioning between different tests: Yes
Issue 2-6: Datasets for training/testing
Agreement:
l Vendors may take into account the test environment/conditions defined by RAN4 when training the UE
Ø sufficient test environment/conditions should be defined to enable vendors to create the data needed for training
l FFS on proposals to augment training data to avoid overfitting of UE models to the test environment
l RAN4 to strive to make the test conditions similar to field deployment conditions
Proposal 3: RAN5 should consider to join RAN4 discussions on Issue 2-3, 2-5 and 2-6.
R4-2410570
Observation 3.2: It deserves RAN5’s early attention on the following items to avoid potential testability issues, including how to implement AoAs during the test, whether/how to implement UE rotation during the test, how similar we can make the test conditions to field deployment conditions.

## Slide 7: “Testability and interoperability issues for positioning accuracy enhancement” for RAN4 AIML topics that may impact RAN5 (1/2)
As per [2], the “Testability and interoperability issues for positioning accuracy enhancement” for RAN4 AIML topic is as below.
Issue 3-2: Requirements for case 2a
Agreement:
No requirements on LMF for positioning accuracy
FFS on RAN4 requirements for any UE reported measurements defined by other groups
Issue 3-3: Requirements for case 2b
Agreement:
No requirements on LMF for positioning accuracy
FFS on RAN4 requirements for any UE reported measurements defined by other groups
Case 1: UE-based positioning with UE-side model, direct AI/ML or AI/ML assisted positioning
Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning
R4-2410570
Notes: Case 1: UE-based positioning with UE-side model, direct AI/ML or AI/ML assisted positioning
Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning

## Slide 8: “Testability and interoperability issues for positioning accuracy enhancement” for RAN4 AIML topics that may impact RAN5 (2/2)
Proposal 4: RAN5 does NOT need to directly participate in RAN4 discussions on Issue 3-2 or 3-3, and only monitor progress and conclusions.
Observation 4: There seems to be no test plans/needs on the table for positioning accuracy enhancements at the moment.
Notes: Case 1: UE-based positioning with UE-side model, direct AI/ML or AI/ML assisted positioning
Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning

## Slide 9: “Testability and interoperability issues for CSI compression and CSI prediction” for RAN4 AIML topics that may impact RAN5 (1/2)
As per [2], the “Testability and interoperability issues for CSI compression and CSI prediction” for RAN4 AIML topic is as below.
Issue 4-1: Reference encoder/decoder
Agreement:
Reference encoder:
The reference encoder is used in RAN4 discussions at least for simulation alignment/requirement derivation, test decoder derivation and/or test decoder verification. It could be documented (in TR, WF, etc) or captured in the specifications as necessary.
Reference decoder:
The reference decoder is used in RAN4 discussions at least for simulation alignment/requirement derivation and/or verification of the decoder implemented by the TE. It could be documented (in TR, WF, etc) or captured in the specifications as necessary.
For Option 3, for each test, a test decoder needs to be captured in the specs, a reference encoder might be needed to derive the test decoder and/or requirements and/or to validate the test decoder implementation in the TE. The same decoder might be used in multiple tests or each test could have a difference decoder.
In Option 3 the Reference decoder is the test decoder.
For Option 4, there might be a need to have reference encoder and/or reference decoder.
R4-2410570
Notes: Option3：To define specific encoder/decoder models for testing in 3GPP TS/TR/WF, etc.
Option 4：Only some guidance on how to implement the encoder/decoder models for testing, without any specific encoder/decoder models for testing in 3GPP TS/TR/WF, etc.

## Slide 10: “Testability and interoperability issues for CSI compression and CSI prediction” for RAN4 AIML topics that may impact RAN5 (2/2)
Observation 5: RAN5 needs to consider how to apply the encoder and decoder in the conformance testing. Inputs from TF160 might also be needed to make sure the conformance among the different encoders/decoders implemented by different TE vendors.
Proposal 5: RAN5 should consider to join RAN4 discussion on Issue 4-1.
Option1: DUT provides the decoder;
Option2: Infra vendor provides the decoder[3]
Option3: Full decoder specification in standard. Option 3 target is that a single decoder defined in the specifications for at least a single test for any DUTs.[3]
Option4: TE vendor provides the decoder. Option 4 target is that a single decoder implemented by each TE vendor will be enough for at least a single test for any DUTs. TE vendor should be able to implement the test decoder for Option 4 without any involvement from another party.[3]
Notes: Option3：To define specific encoder/decoder models for testing in 3GPP TS/TR/WF, etc.
Option 4：Only some guidance on how to implement the encoder/decoder models for testing, without any specific encoder/decoder models for testing in 3GPP TS/TR/WF, etc.

## Slide 11: “Testability and interoperability issues for CSI compression and CSI prediction” for RAN4 AIML topics that may impact RAN5
Observation 6.1: As per [2], agreements about the parameters used in the simulations for checking the feasibility of testing options for CSI compression and prediction is as below.
Agreement:
Parameters agreed are just for the feasibility study of testing options.
If/when RAN4 discusses requirement definition, RAN4 will define a new test decoder which may or may not reuse any of the parameters agreed in the feasibility study.
Proposal 6: RAN5 does NOT need to directly participate in RAN4 discussions on “Test decoder derivation procedure” and only monitor progress and conclusions.
Observation 6.2: As per [2], agreements regarding the process for checking the feasibility of deriving a test decoder for Option 3 is as below.
Test decoder derivation procedure:
Option 1
companies bring encoder + decoder set based on agreed parameters. RAN4 chooses one of the decoders and interested companies further check if an encoder can be trained with this decoder to obtain similar performance/complexity (or other evaluation criteria)
Option 2
companies bring training data for encoder + decoder pair, interested companies train an encoder + decoder pair based on the aggregated dataset from all companies to check decoder derivation feasibility and performance/complexity (or other evaluation criteria)
RAN4 agrees to work on Option 1.
Interested companies are invited to bring further feasibility analysis for Option 2
R4-2410570
R4-2410570

## Slide 12: Reference
[1] RP-240774, Revised WID on Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface, 3GPP TSG RAN Meeting #103; Maastricht, NL, March 18-21, 2024.
[2] R4-2410570, WF on AI/ML, 3GPP TSG-RAN WG4 Meeting #111; Fukuoka city, Japan , May 20th – 24th, 2024
[3] TR 38.843, Study on Artificial Intelligence (AI)/Machine Learning (ML) for NR air interface
Notes: Study on Artificial Intelligence (AI)/Machine Learning (ML) for NR air interface

## Slide 13: Thank you!