## Slide 1: Discussion on handling of AI/ML in RAN5
China Mobile, AT&T, CAICT, Ericsson, Huawei, MediaTek, Nokia, ZTE
3GPP TSG-RAN5 Meeting #105 R5-247647
Orlando, Florida, USA, 18 – 22 November 2024

## Slide 2: Background
Observation 0: During RAN5#104, Proposal 1.2 and Proposal 1.3 in R5-245606 are accepted. Accordigly, the dedicated RAN5 AIML reflector and Agenda Item are well implemented before RAN5#105 already.
R5-245606

## Slide 3: Ongoing RAN4 AIML discussion on “Issue 1-2: Post deployment testing”
Observation 1: During RAN4#112bis, “how to conduct the validation of a change in functionality in already deployed UEs” was discussed under “Issue 1-2: Post deployment testing” with the following agreements captured in R4-2417212 [1].
R4-2417212

## Slide 4: When/How to deal with Changes in certified Products in GCF (1/3)
Observation 2.0: GCF-AP[2] Section 7.7 covers the scenario of “how to deal with the changes in Product’s Hardware and/or Software Configuration”, which addresses the scenario of “how to conduct the validation of a change in functionality in already deployed UEs” from a methodology perspective.
It is feasible to handle this for the changes in already certified/deployed UEs.
Observation 2.1: For the UE which already supports AI functionality/features when it is certified, and the certified AI-UE is subsequently modified with updated AI models, as long as the changes in the AI models do not add new functionality/features, this scenario is aligned with: “do not add new functionality or features” described in GCF-AP[2] Section 7.7.
Evidence of continued compliance with the applicable Certification Criteria shall be provided and recorded by the certification bodies.
Observation 2.2: The scenarios below are addressed by “add new functionality or features” described in GCF-AP[2] Section 7.7.
  The UE does not support AI functionality/features when it is certified, and the certified UE is subsequently modified with addition of AI functionality/features
  The UE already supports AI functionality/features when it is certified, and the certified UE is subsequently modified with updated AI models which enable the certified UE with new functionality/features
Evidence for compliance to the Certification Criteria applicable to the new functionality for feature shall be provided and recorded by the certification bodies.

## Slide 5: When/How to deal with Changes in certified Products in GCF (2/3)
Observation 2.3: For the change that requires a modification to the information within the declaration, the certification bodies shall be notified in time, including both the scenarios below described in GCF-AP[2] Section 7.7
  “do not add new functionality or features”: The UE already supports AI functionality/features when it is certified, and the certified AI-UE is subsequently modified with updated AI models. However, the changes in the AI models do not add new functionality/features
  “add new functionality or features”:
    The UE does not support AI functionality/features when it is certified, and the certified UE is subsequently modified with addition of AI functionality/features
    The UE already supports AI functionality/features when it is certified, and the certified UE is subsequently modified with updated AI models which enable the certified UE with new functionality/features

## Slide 6: When/How to deal with Changes in certified Products in GCF (3/3)
Observation 3.1: There are a few cases tagged with “Updated” can be found in GCF website. For an updated device, some manufacturers may choose to make a new certification rather than updating the original.
Observation 3.2: In GCF, there is no additional fee for doing a new certification or updating a certification. But Recognised Test Organisation (RTO) may still charge for doing a new certification or updating a certification.

## Slide 7: Proposals
Proposal 1: Considering RAN5 is familiar with the existing certification/validation methodology/processes in the certification bodies (quite a few RAN5 delegates attend both RAN5 and GCF), RAN5 should discuss methods to address how to conduct the validation of changes in functionality in already deployed UEs relevant to “Issue 1-2: Post deployment testing” as part of “AI/ML Testability and Interoperability”.
Proposal 2: RAN5 take into consideration the methodology of “how to deal with the changes in already deployed UEs in GCF” as a starting point with necessary adaptions when discussing “how to conduct the validation of a change in functionality in already deployed UEs” under “Issue 1-2: Post deployment testing”.
Notes: It is strongly recommended contributions are focussed/targeted on RAN5 aspects of ‘AI/ML Testability and Interoperability’

## Slide 8: How to identify AI UE in UE certification?
Observation 4: RAN4 is disucssing about how to identify which UEs shall follow the non-AI UE requirements during the UE tests, while which UEs shall follow the AI UE requirements during the UE tests.
Observation 5: As per the existing UE certification process in certification bodies, the UE capability/type identification is counted on UE declaration.
Observation 6: In RAN2#127, it was agreed in R2-2409202[3] to define UECapablityInformation message to indicate UEs’ AI/ML supported functionalities
Proposal 3: Consider to use “UE declaration” as the reference when discuss “how to indentify AI-UE in UE certification”. e.g. If the UE declares itself as an AI UE, it shall follow the AI UE requirements during the UE tests. Otherwise, the UE shall follow the non-AI UE requirements during the UE tests.
RAN2#127 Chair Notes (R2-2409202) cl. 8.1.2.2

## Slide 9: Reference
[1] R4-2417212 WF on requirements for AI/ML air interface, 3GPP TSG-RAN WG4 Meeting #112bis, Hefei, Anhui, China, 14th – 18th October, 2024;
[2] GLOBAL CERTIFICATION FORUM (GCF) Ltd Application Procedures (GCF-AP), Version 3.79.0, 26 September 2024;
[3] R2-2409202 RAN2 ChairNotes, 3GPP TSG-RAN WG2 Meeting #127, Maastricht, Netherlands, Aug 19th – 23rd, 2024

## Slide 10: Thank you!