## Slide 1: Rel-17 5G_ProSe: Way Forward on Sidelink Relays
MediaTek Inc., Apple, China Unicom, China Telecom, Convida Wireless, Futurewei, Huawei, HiSilicon, Interdigital, KPN, Lenovo, Philips, Sony, TNO, Xiaomi, ZTE
3GPP TSG SA#91E SP-210122
March 2021 Agenda Item 5.3

## Slide 2: Status RAN2, SA2, SA3
SA 5G_ProSe WI SP-200972 | SA2: FS_5G_ProSe feasibility , proceed  | RAN2: FS_SL_Relay feasibility , proceed  | SA3: FS_5G_ProSe_sec ongoing
Approved 5G_ProSe WI includes U2N Relay U2U Relay Support of L2 and/or L3 U2N, U2U subject to RAN2/SA3 feedback | SA2#143e TR23.752 v1.1.0: No showstopper for L2, L3 U2N, U2U Recommend to proceed to normative work for L2, L3 U2N, U2U subject to RAN2/SA3 feedback Status Report S2-2101125 No outstanding technical issues Controversial issue: Support of L2 and/or L3 U2N, U2U to be determined at TSGs#91e (RAN, SA) | RAN2#133e: R2-2101955 L2, L3 are both feasible for U2N and U2U [AT113-e][605][Relay] Continuation of L2 architecture issues: [16/16 companies] Proposal 3.3.1: Capture in the conclusion section for L2: “L2 Relay Meets all of the objectives of the SID.” (16/16 companies) [16/16 companies] Proposal 3.3.2: Capture in a common conclusion section for L2 and L3: “RAN2 recommends both L2 and L3 UE to NW and UE to UE relay can proceed to normative work” (16/16 companies) | Work ongoing TR33.847 Sol#14 L2 U2N (self)evaluation: TS33.501 security mechanisms can be reused No self-evaluation for L2/L3 U2U and L3 U2N
 |  No outstanding SA2/RAN2 technical dependencies  |  | 

## Slide 3: U2N Relay approaches
 | L2 | L3 basic | L3+N3IWF | Comment
AS and RAN impact | Yes | Yes | Yes | 
Data communication | Yes | Yes | Yes | Some latency and overhead concern with N3IWF resulting in performance degradation (more network hops, additional headers)
QoS Support | Full | Partial | Partial | PDB split is handled differently in L2 and L3 architectures L2 QoS can be flexibly tailored to the AS conditions on sidelink and Uu, but L3 cannot N3IWF delays not accounted for
End-to-end security | Yes (PDCP) | No | Yes (IPsec) | Relay UE is deemed not trusted, esp. in commercial use cases
Service continuity (3GPP) | Yes (handover) Network controlled (radio criteria) | No 3GPP support* | Session continuity only (IP@ preserv.) No lossless HO UE controlled (higher UE complexity) AS/Radio aspects cannot be ignored | L3+N3IWF mobility requires UE radio link establishment prior transfer * except commercial IMS services (23.737)
L2 approach is the ONLY solution providing full network control, full QoS control, full security, full service continuity,
with minimum overhead, minimum latency and minimum system complexity

## Slide 4: U2U Relay approaches
 | L2 | L3 | Comment
Data communication | Yes | Yes | 
QoS Support | Yes | Yes | U2U Relay QoS splitting
End-to-end security | Yes (PDCP) | No | Use of IPSec unclear. IPSec not available for non-IP traffic
L2 approach is the ONLY solution fulfilling all requirements

## Slide 5: Way Forward
Proceed only with L2 U2N Relay and L2 U2U Relay in normative work.