## Slide 1: 5G-SOLUTIONS: Feedback from Verticals on 5G performance on Project’s use cases Telecom Italia A.i. 8: Other technical contributions Document for: Discussion
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under Grant Agreement No. 856691
S1-223024
3GPP TSG SA1#100
Tolouse, November 14-18, 2022
Notes: Per cambiare l'immagine in questa diapositiva, selezionarla ed eliminarla. Quindi fare clic sull'icona Immagini nel segnaposto per inserire l'immagine desiderata.

## Slide 2: Background
The European Commission Horizon 2020 5G-SOLUTIONS (5G - Solutions for European Citizens) is aiming to demonstrate the capabilities of 5G for Verticals’ applications through five Living Labs.
The experience acquired in the labs is a driver to identify requirements, standardization gaps and drive the work in relevant Standard Development Organizations (SDOs).
At the end of the Project, each Living Lab was interviewed to collect feedbacks on how 5G (*) fulfilled their requirements
(*) Since the Living Labs are running their experiments on live commercial networks or on prototype platforms developed by other EU funded projects (5G-EVE, https://www.5g-eve.eu/, and 5G-VINNI, https://www.5g-vinni.eu/ ), the baseline for the experiments is 3GPP Release 15

## Slide 3: Living Labs
Five different living labs will be trialed
Smart Factories
Smart Energy
Smart City / Ports
Media & Entertainment
Multi-living lab

## Slide 4: Living Lab 1: Factories of the Future (FoF)
Use Case 1.1: Time-critical process optimisation inside digital factories
Use Case 1.2: Non-time-critical communication inside factories
Use Case 1.3: Remotely controlling digital factories
Use Case 1.4: Connected goods
Use Case 1.5: Rapid deployment, auto/re-configuration and testing of new robots
Use Case |  | KPIs |  |  |  |  |  | 
 | Data Rate (Mbps) | Mobility (km/h) | Latency (ms) | Density (devices/m2) | Reliability (%) | Positioning Accuracy (m) | Coverage (%) | Autonomy (days)
UC 1.1 | >100 | <10 | <5 | >0.1 | >99.999 | <0.5 | >99 | -
UC 1.2 | >10 | <10 | <100 | >0.1 | >99.99 | <0.5 | >99 | >30
UC 1.3 | >500 | <10 | <5 | >10-2 | >99.99 | <0.5 | >99 | -
UC 1.4 | >10 | >30 | <10 | >10-4 | >95 | <10 | >99.9 | >30
UC 1.5 | >100 | <50 | <1 | >1 | >99.999 | <0.1 | >99.9 | >30

## Slide 5: Living Lab 2: Smart Energy
Use case 2.1 – Industrial Demand Side Management
Use case 2.2 – Electrical Vehicle Smart Charging
Use case 2.3 – Electricity Network Frequency Stability
Use Case | Indicative KPIs |  |  | 
 | Data Rate (kbps) | Latency (ms) | Reliability (%) | Coverage
UC 2.1 | Not critical | <10 | >99.999 | >99.9% Indoor
UC 2.2 | Not critical | <10 | >99.999 | >99.9% Outdoor
UC 2.3 | Not critical | <10 | >99.999 | >99.9% Outdoor

## Slide 6: Living Lab 3: Smart Cities & Ports
Use Case 3.1: Intelligent street lighting
Use Case 3.2: Smart parking
Use Case 3.3: Smart city co-creation
Use Case 3.4: Smart buildings – smart campus
Use Case 3.5: Autonomous assets & logistics for smart port
Use Case 3.6: Port safety: monitor & detect irregular sounds
Use Case | KPIs |  |  |  |  |  |  | 
 | Data Rate (Mbps) | Mobility (km/h) | Latency (ms) | Density (devices/m2) | Reliability (%) | Positioning Accuracy (m) | Coverage (%) | Service provisioning time (minutes)
UC 3.1 | - | - | <100 | >1 | >99 | - | >99 | -
UC 3.2 | - | <100 | <100 | >0.1 | >95 | <10 | >95 | -
UC 3.3 | >10 | <50 | <10 | >1 | >99.99 | <1 | >95 | <90
UC 3.4 | >100 | - | <10 | >1 | >99.99 | <1 | >99.9 | -
UC 3.5 | >100 | <50 | <10 | >1 | >99.99 | <0.5 | >99.9 | -
UC 3.6 | >100 | <10 | <10 | >0.1 | >99.99 | <10 | >99.9 | -

## Slide 7: Living Lab 4: Media & Entertainment (M&E)
Use Case 4.1: Ultra High-Fidelity Media;
Use Case 4.2: Multi CDN selection;
Use Case 4.3: On-site Live Event Experience;
Use Case 4.4: User & Machine Generated Content;
Use Case 4.5: Immersive and Integrated Media and Gaming
Use Case 4.6: Cooperative Media Production.
Use Case | KPIs |  |  |  |  |  | 
 | Data Rate (Mbps) | Mobility (Km/h) | Latency (ms) | Density (Devices per m²) | Reliability (%) | Coverage (%) | QoE (MOS)
UC 4.1 | <1000 | <100 | <100 | >1 | >99.99 | >99.9 | >4.3
UC 4.2 | >100 | <1 | <50 | >10-2 | >99 | >99 | >4.3
UC 4.3 | <1000 | <1 | <50 | >1 | >99 | >95 | >4.3
UC 4.4 | >100 | <100 | <100 | >1 | >95 | >99.9 | >4.3
UC 4.5 | <200 | <1 | <10 | >0.1 | >99 | >99 | >4.3
UC 4.6 | <1000 | <100 | <50 | >0.1 | >99.99 | >95 | >4.3

## Slide 8: Questionnaire submitted to the four Living Labs
Questionnaire to be filled by each living labs
Vote can be provided in a scale from 1 to 5; free text can be also used
How to score your experience with 5G and the communication system in general
  What are the key positive aspects?
  What are the key negative aspects?
  Major difficulties experienced in integrating the communication system.
Grade the download speed vs the requirements of your use cases (1 poor – 5 excellent)
Grade the upload speed vs the requirements of your use cases (1 poor – 5 excellent)
Grade the latency vs the requirements of your use cases (1 poor – 5 excellent)
Grade the reliability vs the requirements of your use cases (1 poor – 5 excellent)
Grade the complexity to integrate the communication system in your use case (1 very difficult – 5 easy)
Grade the complexity to operate the communication system in your use case (1 very difficult – 5 easy)
Grade the complexity to overview/monitor the communication system in your use case (1 very difficult – 5 easy).
Security
  Did you envisage any security issue?
  Was the security provided by the communication network in line with your expectations (1 not at all – 5 absolutely)
3GPP provides incremental updates of the specifications. Usually, the first release provides the basic functions, and the following releases are used to improve/upgrade the features
  Is it acceptable to start deploying the communication system and then upgrade it (on the basis of the following releases)? Each release is expected 1-2 years after the previous one
Any suggestion on how to improve the communication system?

## Slide 9: Answers
How to score your experience with 5G and the communication system in general
  What are the key positive aspects?
    Factories of the Future: 3 - Testing with Innovative Technologies
    Smart Energy: 4 – The 5G transmission environment allows the possibility to offer performance enabling the smart energy use cases with specific focus on Demand Side Management program, in particular referring to device density, latency and coverage (reliability + availability).
    Smart Cities & Ports: 4 - the experience overall is positive. 5G brings major improvements compared to 4G; Various innovative solutions in the smart cities and ports sectors enabled by 5G
    Media & Entertainment: 4.25 - Bandwidth and slicing; latency, downlink potential; Improved network characteristics, the ability to dynamically deploy, adapt and terminate network services and VNFs on demand; Fast internet access
  What are the key negative aspects?
    Factories of the Future: 3 - Network performance far from the industry needs
    Smart Energy: 4 – It would be necessary to improve the availability and the management of the Vertical Service deployment procedure related to the Vertical VNF deployment in the virtualized environment in the MEC of the service provider.
    Smart Cities & Ports: 4 - 5G performs differently in different scenarios (indoor, outdoor, small-scale deployment, commercial deployment…), expected performances not always met
    Media & Entertainment: 4.25 - Upload can be better sometimes; Integration difficulties, infrastructure availability
  Major difficulties experienced in integrating the communication system.
    Factories of the Future: 3 - Adaptation to the Industrial plants
    Smart Energy: The 5G technologies is still under definition and the commercial availability only in specific areas
    Smart Cities & Ports: 4 Difficulties related to testbed set up and deployment (technological blockers, administrative issues - frequency bands licenses)
    Media & Entertainment: No answer

## Slide 10: Questionnaire submitted to the four Living Labs
Grade the download speed vs the requirements of your use cases (1 poor – 5 excellent)
    Factories of the Future: 2
    Smart Energy: 4 – but it is not a key relevant performance for smart energy
    Smart Cities & Ports: 4 – download speed targets achieved in some LL3 UCs, thanks to mmWave.
    Media & Entertainment: 4.5
Grade the upload speed vs the requirements of your use cases (1 poor – 5 excellent)
    Factories of the Future: 2
    Smart Energy: 4 – but it is not a key relevant performance for smart energy
    Smart Cities & Ports: 2 – upload speeds only partially achieved, due to hardware limitations and the bands used
    Media & Entertainment: 25% - 3, 50% - 4, 25% - 5
Grade the latency vs the requirements of your use cases (1 poor – 5 excellent)
    Factories of the Future: 2
    Smart Energy: 3 – it should represent the key for 5G success. Thinking to 26 GHz for better latency performances
    Smart Cities & Ports: 2 – latency only partially achieved, mainly due to hardware limitations
    Media & Entertainment: 25% - 3, 25% - 4, 50% - 5

## Slide 11: Questionnaire submitted to the four Living Labs
Grade the reliability vs the requirements of your use cases (1 poor – 5 excellent)
    Factories of the Future: 4
    Smart Energy: 4 - it should represent the key for 5G success. Important to be maintained in large scale 5G deployment
    Smart Cities & Ports: 5 – reliability measurements in LL3 show a good reliability score (~99.99% successful transmissions)
    Media & Entertainment: 25% - 3, 50% - 4, 25% - 5
Grade the complexity to integrate the communication system in your use case (1 very difficult – 5 easy)
    Factories of the Future: 4
    Smart Energy: 3 – using a “user-friendly” platform, e.g. 5G-EVE it is easy. Perhaps in a commercial environment, it will be hard to convince service providers to use (and to pay for) MEC capabilities
    Smart Cities & Ports: 3 – some custom connectors needed to be built as the barebone 5G does not provide support for the specific use cases
    Media & Entertainment: 25% - 2, 25% - 3, 50% - 4
Grade the complexity to operate the communication system in your use case (1 very difficult – 5 easy)
    Factories of the Future: 4
    Smart Energy: 3- medium complexity
    Smart Cities & Ports: 4 – the integration was seamless enough, some issues were encountered, related to the availability of User Equipment (UEs) with full support for the functionalities tested
    Media & Entertainment: 33% - 2, 33% - 3, 33% - 5

## Slide 12: Questionnaire submitted to the four Living Labs
Grade the complexity to overview/monitor the communication system in your use case (1 very difficult – 5 easy).
    Factories of the Future: 4
    Smart Energy: 4
    Smart Cities & Ports: 4 – generic network monitoring tools can be used with the 5G systems
    Media & Entertainment: 50% - 4, 50% - 5
Security
  Did you envisage any security issue?
      Factories of the Future: Open access to outside 5G Infrastructure not always possible
      Smart Energy: Yes, security is a crucial point. Not at all about customer information; critical related to DoS for vital services
      Smart Cities & Ports: Remote orchestration may raise security concerns. Some compliance issues were encountered for some UCs but this is not specific to 5G (it is only due to the way the testbed is deployed)
      Media & Entertainment: no answer
  Was the security provided by the communication network in line with your expectations (1 not at all – 5 absolutely)
      Factories of the Future: 2
      Smart Energy: 4
      Smart Cities & Ports: 4 – the provided security was enough for the purpose of the smart cities & ports living lab
      Media & Entertainment: 33% - 4, 67% - 5

## Slide 13: Questionnaire submitted to the four Living Labs
3GPP provides incremental updates of the specifications. Usually, the first release provides the basic functions, and the following releases are used to improve/upgrade the features
  Is it acceptable to start deploying the communication system and then upgrade it (on the basis of the following releases)? Each release is expected 1-2 years after the previous one
      Factories of the Future: no answer
      Smart Energy: no answer
      Smart Cities & Ports: It depends on the use case. Some use cases have stringent requirements in terms of network performances (such as the case of Port Safety), in which case it is not an option to deploy an early version with limited support to functionalities and performances.
      Media & Entertainment: no answer
Any suggestion on how to improve the communication system?
    Factories of the Future: no answer
    Smart Energy: Open as much as possible the possibility that Telecommunications and Vertical can integrate solutions. Open environment can help. The standardization too, especially in the Vertical Service Deployment and in Network Resource Orchestration
    Smart Cities & Ports: More seamless integration of 5G technology with the vertical applications, through the development of intent-based APIs
    Media & Entertainment: Ability to configure automatically the experiment through the portal

## Slide 14: Conclusions
Wide range of feedbacks also on the same question
  Due to different requirements / use cases
  Overall positive feedbacks but there are a number of critical aspects
Critical aspects
  Latency: score 2 for Factories of the Future and Smart Cities & Ports
  Upload speed: score 2 for Factories of the Future and Smart Cities & Ports
  Security: score 2 for Factories of the Future
Suggested improvements:
  seamless integration and automatic configuration
Considerations:
Some of the feedbacks can be linked to the use of experimental platforms or early commercial networks (mainly Rel 15)
  But it is clear that in many real-world implementations, especially when using macro networks, the limitations of a fixed frame structure (often mandated by the Regulators to avoid inter-operators interference) is limiting the radio performance
However, the feedbacks provided by the Verticals involved in the Living Labs, even if partial, can be considered a good indicator on what are the expectations on 5G

## Slide 15: Recommendations
It is recommended to take into account the feedbacks indicated in this document to ensure Verticals’ expectations are met in real world deployments