## Slide 1: PIN Management – Validity duration of the PIN
Document type: Discussion Document for: Discussion
Source: Samsung, vivo

## Slide 2: Outline
PIN Management
Interpreting the validity duration of PIN
Allowing the suspension of PIN (temporary state)

## Slide 3: PIN Management(1/2)
3GPP TS 22.261 listed the requirements for PIN Management in clause 6.38.2.9
  PIN Management includes configuration of PIN, Creation of PIN and Removal of PIN
  PIN configuration provides a mechanism for the 5GS to manage the authorization/de-authorization of PINE, PEMC and PEGC
  Information related to the PIN are configured at the 5GS by authorized 3rd party or PLMN
The configuration information helps the 5GS, PEMC and PEGC to manage the functionality of the PIN.
  (From a stage 2 perspective) The configuration information of PIN is retained till the PIN is deleted.

## Slide 4: Duration of the PIN
3GPP TR 22.261 has the following requirement :
  The 5G system shall support mechanisms for a network operator or authorized 3rd party (e.g., a PIN User) to create, remove and manage a PIN, including:
    Authorizing/deauthorizing PIN Elements;
    Authorizing/deauthorizing PIN Elements with Management Capability;
    Authorizing/deauthorizing PIN Elements with Gateway Capability;
    Establishing duration of the PIN;
    …
The requirement is currently not specific. This has invited debate in SA6.

## Slide 5: Duration of the PIN
It should be possible for the PIN Owner or PLMN to configure or reconfigure the duration of the PIN as below :
  One time use, e.g. valid for 2 hrs
  Recurring like 2 hrs per day
  Valid on a particular calendar day in a month
  NOT valid for 5 minutes, temporarily interrupting an existing PIN
Validity duration need not be restricted to one time e.g. 2hrs, because
  Establishing a PIN requires communication with all elements, authorization, etc. which is a significant amount of data and computation.
  A known temporary interruption could allow devices to save power, etc.
  If a PIN is deleted, elements may join some other PIN, etc. and no longer be available when needed.

## Slide 6: Scenario – a PIN must be interrupted
The PIN Admin must suspend the PIN.
Option 1 wastes resources, may result in not being able to continue.
Option 2 allows continuity despite temporary interruptions and is efficient.

## Slide 7: Summary
The duration can be configured as a one-time event, or as recurring. This is flexible to many scenarios, is efficient and allows more continuity of service in a consistent manner.
The duration can be changed to support unforeseen events, such as the need to temporarily use the PIN gateway for some other purpose.