## Slide 1: Discussion on Positioning Services for UEs connecting via dual 3GPP access
CATT
S1 - 223209
Motivation, Use cases, Proposals

## Slide 2: Motivation(1/2)
Location Service and associated service requirements have been introduced to TS 22.071 since 3G. As positioning becomes a critical feature to serve use cases of different verticals (e.g. smart factories, V2X) in 5G, more requirements for high accuracy positioning services are included in TS 22.261.
However, the existing requirements are defined based on an assumption that, in the location determining process, UE uses only one 3GPP access of the network, with or without non-3GPP access involved, which has excluded the possibility to well study the scenarios of UE connecting to two 3GPP access simultaneously.

## Slide 3: Motivation(2/2)
The system enhancement in positioning services for UE using dual 3GPP accesses will benefit the utilization of radio and network resources, as well as improve the service performance like increasing the availability, reducing the latency, etc.
The possible scenarios to be addressed will include but not limited to:
    UE using two 3GPP access networks(e.g. E-UTRAN&NG-RAN, two NTNs) from one PLMN;
    UE using two 3GPP access networks from different PLMNs or a PLMN and an NPN;
    Note: it’s assumed the mentioned networks are managed by one operator, while UE may have one subscription or two subscriptions.

## Slide 4: Use Cases
Potential new use cases possible to be considered for the enhancement positioning services in Rel-19:
High accuracy positioning in warehouse
Access selection for cruise ships at near sea
High accuracy positioning in the automated factory
Access selection for UE to send positioning message
UE location information sharing between PLMNs

## Slide 5: Use Case I High accuracy positioning in Warehouse
Many (semi-) stationary objects exist in the surrounding like high shelters in warehouse, blocking the radio signals. UE location accuracy cannot be fulfilled by the measurements form one access network.
The RAN nodes of two access networks are deployed in different locations. So the network requests UE to perform positioning measurements by the signals of two access networks simultaneously, and then report to the network for location calculation.
With the help of LCS over dual accesses, the network can provide location information fulfilling the accuracy requirements.

## Slide 6: Use Case II Access Selection for cruise-ships at near sea
UE enters into the area with the coverage of both terrestrial access and satellite access network. Due to satellite propagation delay as shown, it is hard to meet the positioning service latency requirements e.g. 10ms, 15ms via single satellite access.
 | UE to satellite Delay [ms] |  | One-Way Max propagation delay [ms]
 | Min | Max | 
LEO | 3 | 15 | 30
MEO | 27 | 43 | 90
GEO | 120 | 140 | 280
The network steers UE to select one access or two accesses together to reduce the transmit latency.

## Slide 7: Use Case III High accuracy positioning in the automated factory
The automated factory is installed in remote area, at the edge of 5G terrestrial access network, and covered by satellite access. All the materials are transported between different workspaces via trucks with autonomous driving. The trucks are tracked with the required horizontal positioning accuracy better than 5m.
The number of the deployed RAN nodes limits the horizontal positioning accuracy to lower than 10m. Satellite access can be selected to facilitate the positioning procedure to fulfil the required horizontal accuracy.

## Slide 8: Use Case IV Access selection to send positioning message
UE registers to PLMN via 3GPP Access1 and 3GPP Access2 separately. 3GPP Access 1 and 3GPP Access 2 support different latency and congestion status.
The positioning message can be transferred in either 3GPP Access to improve location service availability and network resource utilization.

## Slide 9: Use Case V UE location info. sharing between PLMNs
UE registers PLMN1 and PLMN2 over different 3GPP access networks, the location information obtained via positioning procedure is stored in PLMN1 and PLMN2 separately.
With the help of LCS over dual accesses, the network resource utilization, UE power consumption, positioning latency can be optimized.
With location information exposure between PLMN1 and PLMN2, PLMN2 can avoid UE positioning at 10:05, and reuse the existing UE location stored in PLMN1 at 10:00am.

## Slide 10: Proposals
This documents proposes to add several new requirements in TS 22.071 and TS 22.261 for enhancing positioning services when UE is using dual 3GPP accesses.
TS 22.071
Clause4.1
The location determining process should be able to combine diverse location information from the networks, diverse positioning techniques and local knowledge when considering quality of service parameters to provide an optimal positioning request response.
Clause5.4
It shall be possible for the location determining process to make use of several sources of information from more than one networks simultaneously on an on-demand in determining the location. …… The LCS shall be capable of making use of more than one network and/or the restricted or the extra information as appropriate for the service being requested.

## Slide 11: Proposal
TS 22.261
Clause 6.27.2
The 5G system shall provide different 5G positioning services, supported by different location information from the networks, different single and hybrid positioning methods to supply absolute and relative positioning.
NOTE X: The networks refer to 3GPP networks of single PLMN, or one PLMN and one SNPN, or two PLMNs with the same RAT or different RATs, e.g. E-UTRA, NR, Satellite access.

## Slide 12
Thank you!