## Slide 1: Discussion for Information Exposure to Application in UE
OPPO, Xiaomi, Tencent, Toyota, vivo, Bosch, Huawei
3GPP TSG-SA1 Meeting #100 S1-223281 (was 3181)
Toulouse, France, 14 – 18 November 2022

## Slide 2: 5GAA Usecase-1: The Infrastructure stops transmitting data and informs the Application Server and Vehicle
Example Flow Chart for Infrastructure Assisted Environment Reaction,
Scenario #7: The Infrastructure stops transmitting data and informs the Application Server and Vehicle
(Reference: 5GAA_T-220058_WI-PRESA-Technical-Report)
1. The Infrastructure is notified about expected QoS degradation and initiates its reaction (500 ms)
2. The Infrastructure’s sensor app intends to stop sending any data to Application Server and Vehicle, and the Infrastructure informs the Application Server and Vehicle its intention in advance (500 ms)
3. The Vehicle’s AD Application changes the automated driving algorithm based on its local sensor, or stops safely, or hand over to the safety driver (7000 ms)
4. The Vehicle hands over feedback to the Infrastructure that it has finished reacting (500 ms)
5. The Infrastructure’s sensor app stops sending data to the Application Server and Vehicle (200 ms)

## Slide 3: 5GAA Usecase-2: The AV (RV1) stops safely and releases the automated driving system
Example Flow Chart for Cooperative Lane Merge Reaction, Scenario #3: The AV (RV1) stops safely and releases the automated driving system
1. The Vehicle’s AD app is notified about expected QoS degradation or Coverage Loss and initiates its reaction (500ms)
2. The Vehicle stops safely (7000ms)
3. The vehicle deactivates the automated driving system (500ms)
(Reference: 5GAA_T-220058_WI-PRESA-Technical-Report)

## Slide 4: Use case-3: QoS prediction for HD map downloading for intelligent driving
HD Map
Area-1
HD Map
Area-2
HD Map
Area-3
HD Map
Area-4
Download the static layer HD Map when it is going to the area-2
Precondition: The car can only download the static information of HD map in the current location, due to regulatory requirement, changing of HD map, storage capacity.
Service flow:
The car performs LaneGCN model based inference for auto-driving (see the picture on top-right);
When a car is getting close to an area boundary, it needs to download the HD map of the next area from the server. Since the HD map data size is large (~100MB covering an area about 5-12 square KM, reference: https://www.argoverse.org/).
A QoS prediction helps UE to determine whether the HD map can be downloaded in time so that the Auto-driving can continue, otherwise some reaction is needed such as speeding down or turn to Manual driving
Requirement: the UE needs to get the QoS prediction information from 5G system directly, since no regular connection with a application server
LaneGCN model based AI inference for auto-driving
(Reference: https://www.argoverse.org/)
Fusion of HD Map
Dynamic layer inference
Static layer inference
Notes: HD Map data is much more precise than a navigation map
The size of the Vector HD Map provided by the Argoverse dataset is on the order of 100 megabytes, covering an area of ​​about 5 or 12 square kilometers;

## Slide 5: Summary: requirements and proposal
Requirements:
  QoS prediction time horizon (time before the QoS change happens): in several seconds (6-18 sec) in 5GAA Technical Report;
  QoS prediction notification time (from 5GS to application in UE): 0.5 sec (mostly) – 2 sec
  Some use cases clarify the notification time is even less than 0.5sec (500ms) in 5GAA Technical Report
  The user plane connection may not always be available
  “deliver information on potential QoS change to the UE-side of the application are needed especially for the time horizons in the order of a few seconds and become particularly important under critical radio conditions, since the user plane may not always be available, while control plane radio resources are expected to be available in most cases even when user plane resources have been deallocated” (from 5GAA Technical report)
  The implementation complexity for the interface between each 3rd party’s Application server and 5G core is considerable. It is not ideal to assume the 5G core can always find the application server and UEs in a short time.
Proposal: To approve A R19 miniWID and draft CR (S1-223178, S1-223189) to clarify the requirements for letting 5G network expose information to the 3rd party application in UE

## Slide 6: Thanks

## Slide 7: 5GAA LSin (LS on QoS Sustainability analytics and V2X service adaptations)
  Q.1.3: In the context of Requirement 6 “Investigate harmonization of QoS change notifications for V2X application (e.g., QoS change notification sent to the UE)” and 3GPP study item [3], KI#2, some of the proposed solutions include the possibility to share QoS Sustainability with the UE directly:
    Q.1.3.1: Will [3], KI#2 will conclude and select solution in the scope of Release 18?
    Q.1.3.2: Does 3GPP envision that for the above KI#2 3GPP can select a solution that can deliver QoS Sustainability to the UE via NAS or other control plane protocol?
    Q.1.3.3: Does 3GPP envision that above solution may be used also for non-AIML specific applications, and specifically support also V2X use cases?
Q2: whether additional clarifications are needed by 3GPP in order to cover those requirements in Release 18 or later releases.
Notes: TS 22.261 clause 6.40
Based on operator policy, the 5G system shall be able to provide an indication about a planned change of bitrate, latency, or reliability for a QoS flow to an authorized 3rd party so that the 3rd party AI/ML application is able to adjust the application layer behaviour if time allows. The indication shall provide the anticipated time and location of the change, as well as the target QoS parameters.
Based on operator policy, 5G system shall be able to provide means to predict and expose predicted network condition changes (i.e. bitrate, latency, reliability) per UE, to an authorized third party.
Subject to user consent, operator policy and regulatory constraints, the 5G system shall be able to support a mechanism to expose monitoring and status information of an AI-ML session to a 3rd party AI/ML application.
5G system shall be able to provide event alerting to an authorized 3rd party, together with a predicted time of the event (e.g., alerting about traffic congestion or UE moving into/out of a different geographical area).

## Slide 8: Proposal
A R19 miniWID and draft CR with the following objectives:
This work item proposes requirement to let 5G network expose information directly to the 3rd party application running on UE, including:
- Define the specific information (e.g. QoS prediction) which is allowed to be exposed to the application running on UE
- Authorize/deauthorize the 5G network to expose information directly to an application running on UE;
- Authorize/deauthorize which 3rd party application running on UE to acquire the 5GC information;

## Slide 9: 5GAA Usecase-2 The AV ignores Infrastructure’s data and drives only with its own sensor observations
Example Flow Chart for Infrastructure Assisted Environment Reaction, Scenario #2: The AV ignores Infrastructure’s data and drives only with its own sensor observations
1. The Vehicle’s AD Application is notified about expected QoS degradation or Coverage Loss and initiates its reaction
2. The Vehicle’s AD Application changes automated driving algorithm based on its local sensor
3. The Vehicle drives with adapted algorithm
4. The Vehicle informs the Application Server

## Slide 10: AECC: AI inference with/without real time interaction
Pattern A: AI Inference without real time interaction with AS (Application Server)
- Local AI inference is performed e.g. for auto-driving on the right picture
- Multiple factors for the AI inference including static Map, dynamic road condition, computation capability, speed, etc.
Pattern B: AI inference with real time interaction with AS
- real-time reporting of Sensor data for UL, result message for DL (a round trip transmission)
- Model splitting for AI inference may be applied (TR 22.874, intermediate data reporting)
Processing pattern A (no real time reporting) and pattern B (Real time reporting)
Reference: AECC WP “ Operational Behavior of a High Definition Map Application “

## Slide 11: AECC: creating HD map with dynamic and static layer information (with no real-time interaction with AS)
For pattern A (no real-time reporting): a vehicle system has the HD Map data (static) about its current location and traveling route, which includes data for an area smaller than several dozen square miles, while the MSP edge server has the HD Map data for one or more areas of a country. The MSP center server could have the HD Map data for the whole country.
(Reference: AECC WP “ Operational Behavior of a High Definition Map Application “)
Static layer information of HD map is downloaded from application server. (such as road information, traffic control, construction, car accident)
Dynamic layer information around the vehicle, the vehicle performs AI inference itself (real-time moving of pedestrian and vehicle)

## Slide 12: Reference
5GAA technical report “Predictive QoS and V2X Service Adaptation”
5GAA Technical Report A-200055, ‘5GS Enhancements for Providing Predictive QoS’ in C-V2X
AECC WP “ Operational Behavior of a High Definition Map Application “
https://www.argoverse.org/
5GAA LS on QoS Sustainability analytics and V2X service adaptations
3GPP TR22.874 Study on AIML Model Transfer