## Slide 1
Introduction to Support WBA OpenRoaming Framework for the Interconnect between SNPN & Credentials Holder (CH)
Intel, Cisco
Contact: Suresh Srinivasan / suresh.srinivasan@intel.com
Supporting companies: HPE, BT Group, Broadcom, SaankhyaLab, IITB
SA WG1 Meeting #S1-100
14- 18 November, 2022, Toulouse, France
S1-223085, S1-223086, S1-223087

## Slide 2
OpenRoaming Architecture
OpenRoaming is a cloud-based federation framework that opens WiFi roaming to IDPs and APNs.
Wireless Broadband Alliance (WBA) Specifies and operates OpenRoaming.
Industry Solution to enable scalable, seamless, and secure authentication between IDPs and users with OpenRoaming profile.
OpenRoaming defines a legal framework – for secure signaling between ANPs and IDPs.
SA WG1 Meeting #S1-100
14- 18 November, 2022, Toulouse, France
S1-223085, S1-223086, S1-223087

## Slide 3
Issues with Release-17 SNPN and CH (N32)
Interconnections
3GPP (Release-17) has introduced a new capability to enable NPN deployments of 5G system
Release-17 Architecture issues with SNPN and IDP/CH:
    Signaling are between SNPN and IDP/CH are short lived.
    Failure of HTTP connection between IDP/CH and SNPN with today’s architecture.
SA WG1 Meeting #S1-100
14- 18 November, 2022, Toulouse, France
S1-223085, S1-223086, S1-223087

## Slide 4
Background
SA has discussed WBA OpenRoaming Technical Standards Task Group’s request and concluded that the most appropriate way for initiating related work in 3GPP is via the SA1 WG by company contributions. Namely, the proponents of this work should bring a Release 19 proposal in the SA1 WG following the 3GPP working procedures.
WBA OpenRoaming Technical Standards Task Group have renewed their request by sending an LS directly to SA1 (S1-22xxxx): “WBA kindly asks 3GPP SA1 to consider defining, in the release 19 timeframe, service requirements for facilitating interconnect between SNPN and CH, in particular, considering the issues described above.”
  The WBA LS points to the following issues of interconnection between SNPN and Credentials Holder:
    There may be SNPN and CH deployments where IP address information of endpoints is not available in advance of signalling establishment, e.g.,
      1) where the SNPN is operated behind a NAT,
      2) where a CH instance is operated using a cloud provider using dynamic IP address assignment,
      3) where the interconnect is delivered as part of a third party defined confederation which does not operate a centralized database of IP addresses.
    Infosec policies of the enterprise operating the SNPN may prohibit accepting inbound socket connections from unknown IP addresses.
SA WG1 Meeting #S1-100
14- 18 November, 2022, Toulouse, France
S1-223085, S1-223086, S1-223087

## Slide 5
miniWID: Justification and Objective
Justification:
  N32 reference point is currently designed to support tens of millions of subscribers using a long-lived connection between VPLMN and HPLMN.
  The requirements on the N32 reference points are increased due to a couple of complementary factors:
    The need to support thousand times more networks
    Subscribers use short lived forwarding connections between VPLMNS and HPLMNs.
Objective:
  How to enable support for N32 functionality between SNPN and CH (which can be either a PLMN or another SNPN or AAA server) that does not require long-lived persistent connectivity on N32.
  How to enable support for N32 functionality that facilitates firewall and border GW configuration on the SNPN side of N32.
  How to scale the N32 design to support a three order of magnitude increase in the number of subscribers.
SA WG1 Meeting #S1-100
14- 18 November, 2022, Toulouse, France
S1-223085, S1-223086, S1-223087

## Slide 6
Change Request to TS 22.261
Specific to the 5G system for standalone operation of a non-public network the following additional requirements apply:
  The 5G system for standalone operation of a non-public network shall be able to interconnect with a large number (e.g. 1,000,000) of entities that authenticate and authorize access to the non-public network.
  The 5G system for standalone operation of a non-public network shall be able to interconnect with an entity that authenticates and authorizes access to the non-public network in deployments where the IP address information of the entity’s endpoints is not available in advance of signalling establishment, e.g.,
  where the 5G system for standalone operation of a non-public network is operated behind a NAT device.
  where the entity that authenticates and authorizes access to the non-public network is operated using a cloud provider using dynamic IP address assignment.
  where the interconnect is delivered as part of a third party defined confederation (e.g. WBA OpenRoaming) which does not operate a centralized database of IP addresses.
NOTE: Infosec policies of the enterprise operating the 5G system for standalone operation of a non-public network can prohibit accepting inbound socket connections from unknown IP addresses.
SA WG1 Meeting #S1-100
14- 18 November, 2022, Toulouse, France
S1-223085, S1-223086, S1-223087