## Slide 1: Discussion on the sensing definitions
Source: Huawei
S1-230221
3GPP TSG SA WG 1 Meeting #101
Athens, Greece, 20 - 24 February 2023

## Slide 2: Current definitions in FS_Sensing
sensing measurement data: data collected about radio/wireless signals impacted (e.g. reflected, refracted, diffracted) by an object or environment of interest for sensing purposes.
sensing measurement process: process of collecting sensing measurement data.
sensing result: the information derived from processing sensing measurement data.
NOTE: Examples of sensing result are characteristics of an object or environment, etc.

## Slide 3: How to differentiate sensing measurement data and sensing result
Principles:
The 3GPP sensing measurement data is to be processed inside 5G system.
The sensing result is intended to be used outside 5G system for sensing service.
3GPP sensing measurement data
sensing result

## Slide 4: Different data sources for sensing result
3GPP sensing measurement data
N3GPP sensing measurement data
Processing
Sensing result
Input
Input
processed 3GPP sensing measurement data
Input
processed N3GPP sensing measurement data
Input
Processing
Processing
Inside 5G system
3GPP sensing measurement data
sensing result
processed 3GPP sensing measurement data

## Slide 5: Proposal of definitions
3GPP sensing measurement:
  Option#1:
  data collected obtained from 5G system about radio/wireless signals impacted (e.g. reflected, refracted, diffracted) by an object or environment of interest for sensing purposes by using 5G Wireless sensing and to be processed inside 5G system.
  Option#2(a new simplified definition considering the current definition of 5G Wireless sensing):
  data obtained by using 5G Wireless sensing and to be processed inside 5G system.
Non-3GPP sensing measurement data: data obtained from non-3GPP sensors (e.g. video, LiDAR, sonar) directed at an object or environment of interest for sensing purposes.
sensing measurement process: process of collecting 3GPP sensing measurement data.
sensing result: the information derived from processing 3GPP sensing measurement data and/or Non-3GPP sensing measurement data, which is intended to be used outside 5G system for sensing service.
NOTE: Examples of sensing result are characteristics of an object or environment, etc.