## Slide 1: Proposal on human readable name for network slice / service
3GPP TSG-SA1 Meeting #102 S1-231200
Berlin, May 2023

## Slide 2: Introduction
There can be different levels at which 5GS network services can be provided.
These can be identified by means of e.g. S-NSSAI (slice), DNN (connectivity), QoS parameters or can be associated with a URSP (e.g. a S-NSSAI+DNN of a Route selector Descriptor) or specific data bearers that are provided to a UE.
For the above, it would be beneficial if the operator could provide the end user with human readable information associated to those specific slice identifiers or QoS/connectivity settings, to help user awareness of available NW services that the operator is providing, i.e. better user experience.

## Slide 3: Use Case 1
Each enterprise has its own S-NSSAI
Slices are available over the entire PLMN
Each slice (S-NSSAI) is isolated from each other and gives access to services belonging to a specific enterprise
Problem
  How does the user know to which S-NSSAI is connected at a given time?
    And other NSSAIs (not)available?
One PLMN (or NPN), two isolated slices
UE
RAN
5GC
S-NSSAI-1
S-NSSAI-2
Which S-NSSAI is the user connected to?

## Slide 4: Use Case 2
Large business campus with multiple buildings each belonging to different enterprise functions (e.g. logistics, Stock warehousing)
Building has its own PNI-NPN (from the same PLMN)
Each slice is isolated from each other and gives access to a network belonging to a specific enterprise (PNI-NPN)
There is overlapping between NPNs
Problem
  How does the user know to which S-NSSAI is connected at a certain time?
    And other NSSAIs (not)available?
One PLMN, two NPNs, two Isolated Slices
NPN-1
NPN-2
UE
RAN-1
RAN-2
5GC
S-NSSAI-1
Logistics
S-NSSAI-2
Stock
Warehousing
Which S-NSSAI is the user connected to?

## Slide 5: Use Case 3
One PLMN (or PNI-NPN)
Enhancements for Gaming support are provided by means of a specific gaming slice, DNN and QoS (possibly including a certain GBR value)
Gaming slice and DNN not available in some part of PLMN
Problem
  How does the user know when the enhanced network service for gaming (subscribed to) is available?
  How can the operator communicate to end user the deployment/availability of such enhancement in their network?
One PLMN (or NPN)
RAN
5GC
Where is gaming enhancement available?
S-NSSAI +DNN + QoS
(gaming)
DNN Gaming (LBO)
UE
UE

## Slide 6: Human readable name per Slice/Service
High-level Service Flow:
  Serving NW can provide S-NSSAI(s) to the UE together with associated human-readable service name(s), e.g. during UE registration, if they are available
    service names may be part of subscription information.
  HPLMN may provide the UE with information on how to map specific S-NSSAIs (or DNN, QoS or URSP info) with service names
    This can also include whether /how the information should be displayed to the user
  UE can display the human readable service name in the user interface (device display/screen), in addition to PLMN/NPN Network name.
  UE may also display human readable name of services that cannot be established, to inform the user if/where certain application or set of applications cannot run

## Slide 7: Human readable name per slice/S-NSSAI - Example
Examples of User’s display (1/3)
OPERATOR A
Logistics
App1
App2
App3
Derived from PLMN-id
Derived from name(s) of service, received from network, associated to a S-NSSAI
OPERATOR A
Stock warehousing
App1
App2
App3
UE moves to new NW/ Slice Area of service
Access to logistics not possible
Derived from rejected S-NSSAI, and associated readable name(s)
App2
See another example in next slide…

## Slide 8: Human readable name per slice/S-NSSAI - Example
Examples of User’s display (2/3)
OPERATOR A
Stock warehousing
App1
App2
App3
Example#2: when user presses e.g. App2 and UE tries to establish PDU session to the associated S-NSSAI, if UE knows that is not allowed to use the logistics apps, UI can pop up a message indicating the human readable name of the non-allowed S-NSSAI.
App related to Logistics not allowed here
Access to logistics not possible

## Slide 9: Human readable name per slice/service/QoS - Example
Examples of User’s display (3/3)
OPERATOR A
GAMING enhanced support AVAILABLE
App1
App2
App3
Derived from PLMN-id
Derived from name of service, received from network, associated to a combination of S-NSSAI, DNN, QoS
OPERATOR A
App1
App2
App3
UE Moves to area outside Enhanced gaming deployment
App2
GAMING enhanced support AVAILABLE

## Slide 10: Existing requirements and gaps
Existing requirements
22.261 includes a requirement on broadcasting HRNN for NPNs (sec.6.25):
The 5G system may broadcast a human readable network name that a UE may display for manual selection of a non-public network.
There are also other reqs on displaying PLMN network name, in 22.101 and 22.042
  Including different mechanisms to derive NW name, e.g. broadcast, USIM/UE based, NITZ
Gap: existing requirements do not cover the ability to associate human readable names to specific NW slices (or QoS or DNN) for a certain UE

## Slide 11: Proposal for SA1: New service requirements
See associated WID (S1-23xxxx) and CR to 22.261 (S1-23xxxx)

## Slide 12: Proposal for SA1
Add a new requirement, in TS 22.261:
Subject to HPLMN policy and control, the 5G system shall support mechanisms for the network (PLMN or NPN) to provide UEs with human readable name(s) associated to network slices, connectivity/QoS settings or a combination of these, e.g., to be displayed to the user.
See CR in S1-231202