## Slide 1: Discussion on missed detection and false alarm
Huawei
S1-232151

## Slide 2: Conventional understanding of Missed Detection and False Alarm
The Missed Detection rate is the False Negative rate:
Examples:
True Positive (TP): the highway intrusion happens, and the sensing result accurately reports this.
True Negative (TN): the highway intrusion doesn’t happen, and the sensing result accurately reports this.
False Negative (FN): , the highway intrusion happens, but the sensing result inaccurately reports that there are no intruders.
False Positive (FP): the highway intrusion doesn’t happen, and the sensing result inaccurately reports that there are intruders.
False alarm rate
The False Alarm rate is the False Positive rate:
Missed detection rate
 | Positive | Negative
Positive | True Positive (TP) | False Negative (FN)
Negative | True Negative (TN) | False Positive (FP)
Measured Values
Actual Values

## Slide 3: Conventional understanding of Missed Detection and False Alarm
Truth = positive
Truth = negative
Measurement = negative
Measurement = positive
MD =
FA =

## Slide 4: Current definitions of TR 22.837
Missed detection probability denotes the ratio of missing event to acquire a sensing result over all events during any predetermined period when the 5G system attempts to acquire a sensing result. It applies only to binary sensing results.
False alarm probability denotes the ratio of detecting an event that does not represent the characteristics of a target object or environment over all events during any predetermined period when the 5G system attempts to acquire a sensing result. It applies only to binary sensing results.
The current definition of missed detection probability specifies the probability of the missing event (false negative event) over all events:
The current definition of false alarm probability specifies the probability of the false positive event over all events:

## Slide 5: Discussions
Missed detection rate
False alarm rate
Conventional understanding:
Definitions of TR 22.837:
Missed detection rate
False alarm rate
True Positive(TP) | False Positive(FP)
False Negative(FN) | True Negative(TN)
To provide slightly supplementary examples, for illustration purpose, there are two examples as follows:
Missed detection for intruder detection at home:
  Consider a faulty system design which always report negative (i.e. no intruder), assuming 10,000 detection events in total, and only 1 intrusion event which is actually occurs (but it is detected as being negative in this example). For intruder detection, we do not want to miss any true event ideally.
  In this example, we will have TN=9999, FN=1, TP=0, FP=0. Unfortunately this faulty system seems to be perfect, as MD=0.01%/FA=0, according to the latest SA1 understanding.
  In summary, TN and FP events, which never occur, shall not be a part of denominator for statistical KPI of missing detection rate.
False alarm for parking space for detecting the presence of car in a given parking spot,
  Consider a faulty system design which always report positive (i.e. being occupied 100%), assuming 10,000 detection events in total, and 9900 events which actually occur (they are detected as being positive in this example) during the peak time. This system will give rise to less efficient usage of car park.
  In this example, we will have TP=9900, FP=100, TN=0, FN=0. Unfortunately this faulty system seems to be fine, as FA= 100/10000=1%/MD=0, according to the latest SA1 understanding.
  In summary, FN and TP events, which do occur, shall not be a part of denominator for statistical KPI of false alarm rate.

## Slide 6: Proposals
  Missed detection probability denotes the probability of an event is missed from detection but the event representing the characteristics of a target object or environment occurs actually. It applies only to binary sensing results.
  False alarm probability denotes the probability of an event is detected but the detected event representing the characteristics of a target object or environment does NOT occur actually It applies only to binary sensing results.
Three alternatives to update the definitions: :
Option 1
Option 2
  Missed detection probability denotes the ratio of number of events falsely detected to be negative about the presence of the characteristics of a target object or environment, over the number of events which are falsely detected as being negative presence or truly detected as being positive presence It applies only to binary sensing results.
  False alarm probability denotes the ratio of the number of events falsely detected to be positive about the presence of the characteristics of a target object or environment, over the number of events which are falsely detected as being positive presence or truly detected as being negative presence.It applies only to binary sensing results.
Option 3
Missed detection probability is the conditional probability of not detecting the presence of an target object/environement when the target object/environment is present. This probability is denoted by the ratio of the number of events falsely identified as negative, over the total number of events with a positive state. It applies only to binary sensing results.
  Note: An event with a positive state refers to the presence of the characteristics of a target object or environment, including the event falsely identified as being negative and truly identified as being positive.
  False alarm probability is the conditional probability of falsely detecting the the presence of target object/environement when the target object/environment is not present. This probability is denoted by the ratio of the number of events falsely identified as being positive, over the total number of events with a negative state. It applies only to binary sensing results. It applies only to binary sensing results.
  Note: An event with a negative state refers to the non-presence of the characteristics of a target object or environment, including the event falsely identified as being positive and truly identified as being negative.

## Slide 7: Proposals
It is proposed to update the definitions of TR 22.837 using Option 3.

## Slide 8
Thank you