## Slide 1
China Telecom
Discussion on Edge Computing Considering the Operational Needs of Service Hosting Environment

## Slide 2
  Background and use case
Cloud phone has the features of cost saving, quick setup and flexible scalability. Cloud phone is a phone that deeply integrated with Internet service. It only has interaction and display functions, and the network is responsible for storage and processing.
Cloud phones are more and more popular with the advantages of meeting the requirement of high performance with low device capability.
For example, the cloud phone could provide service for immersive VR highlights and replays on site during concert or matches in the stadium.

## Slide 3
  Background and use case
For example, there could be immersive highlights and replays service for people in a stadium to have immersive experience on the football game through cloud phones. The traffic of the users could be offloaded to meet the user experience with low latency and low bandwidth pressure. In that situation, the closest Service Hosting Environment might be overloaded or highly-loaded, which cannot provide the expected user experience. The user plane paths could be selected or changed to another Service Hosting Environment with lower load.
In order to meet the expected requirement of low latency and low bandwidth, the user plane paths could be selected or changed to Service Hosting Environment with a lower load offering the Hosted Service for Cloud phone.

## Slide 4
  Existing requirements and observation
In TS 22.261, there are existing requirements on selecting and/or changing the user plane paths with the consideration on the location of the UE or application in the Service Hosting Environment.
6.5 Efficient user plane
6.5.1 Description
5G is designed to meet diverse services with different and enhanced performances (e.g. high throughput, low latency and massive connections) and data traffic model (e.g. IP data traffic, non-IP data traffic, short data bursts and high throughput data transmissions).
User plane should be more efficient for 5G to support differentiated requirements. On one hand, a Service Hosting Environment located inside of operator's network can offer Hosted Services closer to the end user to meet localization requirement like low latency, low bandwidth pressure. These Hosted Services contain applications provided by operators and/or trusted 3rd parties. On the other hand, user plane paths can be selected or changed to improve the user experience or reduce the bandwidth pressure, when a UE or application changes location during an active communication.
The 5G network can also support multiple wireless backhaul connections (e.g. satellites and/or terrestrial), and efficiently route and/or bundle traffic among them.
6.10 Network capability exposure
Based on operator policy, a 5G network shall provide suitable APIs to allow one type of traffic (from trusted third-party owned applications in the operator's Service Hosting Environment) to/from a UE to be offloaded to a Service Hosting Environment close to the UE's location.

## Slide 5
  Proposal
Considering the lack of requirements on offloading the data traffic to the Service Hosting Environment based on the usage information, e.g. load condition.
Please find the detailed changes to TS 22.261 in the attached CR.

## Slide 6
THANKS
感 谢 聆 听