## Slide 1: Discussion on System vs Network Control
Daniel Lönnblad
Ericsson, Deutsche Telekom AG, Nokia, BMWK

## Slide 2: General
In SA1 normative requirements there are some ways to differentiate what parts of the system that is involved in specific functionality.
  “The 5G system shall” used for service requirement that the 3GPP system as whole should support. Examples of this is
    The 5G system shall be able to provide 5G wireless sensing service in a sensing service area location using sensing transmitters and sensing receivers.
    The 5G system shall be able to support IMS as part of a network slice.

## Slide 3: General cont’
  “5G network shall” is used for service requirements applicable to the 5G network (excluding the Ues).
  “5G network is often used for functionality related to configuration or authorization. Examples are:
      Based on operator policy, a 5G network shall provide suitable means to allow a trusted and authorized third-party to create and modify network slices used for the third-party with appropriate security policies (e.g. user data privacy handling, slices isolation, enhanced logging). (TS 22.261 8.2)
      Based on the HPLMN operator preference, the 3GPP network shall be able to authorize the ability of an Evolved ProSe Remote UE to access the 3GPP network via an Indirect 3GPP Communication (TS 22.278 9.5)
      The 5G network shall ensure that only member UEs of the same 5G LAN-VN are able to establish or maintain private communications among each other using 5G LAN-type service. (TS 22.261 6.26.2.2)
      The 5G network shall enable the network operator to remove one or more UEs from an existing 5G LAN-VN. (TS 22.261 6.26.2.3)
      The 5G network shall enable the network operator to create, manage, and remove 5G LAN-VN including their related functionality (subscription data, routing and addressing functionality). (TS 22.261 6.26.2.3)
      The 3GPP network shall be able to control (i.e. block and/or prioritize) traffic from UEs to an application on a third-party server or the third-party server itself without affecting traffic to other applications on the third-party server or to other third-party servers. (TS 22.101 31.2.1)

## Slide 4: Reasons for using 5G network for sensing requirement
The 5G network has control over geographical areas that are allowed and not allowed to do sensing due to regulation. The UE’s may not.
The configuration of sensing service can include many users and many different service levels. The network therefore needs to have control to allow for reuse spectrum/sensing signals in best possible way.
Sensing operation can require a huge amount of spectrum. This needs to be managed together with requests of other services (e.g. data communication). The 5G network has this overall responsibility.
If the 5G UE (included in 5G system) can authorize sensing receivers and transmitters this could allow UE’s to authorize other UE’s, which is not acceptable.
Sensing opens up for new usage and new obligations around security and specifically bystander privacy and it is important to minimize the risk for unintended exposure. Regulations are expected in this area.
If configuration is left to the UE to do (i.e. via policy) there is a lack of mechanism to ensure this is followed unless it is managed in an MNO controlled security domain (fraudulent UE’s can misbehave)

## Slide 5: Motivation about 5G network exposure
The UE is not a trusted entity and can be a weak point where 3GPP sensing data and sensing results can be faked for fraud purposes .
There are general requirements for UE exposure present in section 6.10 of TS 22.261 which require secure access from UE side to network APIs where the third-party service authorization is included.
Northbound solution is available in Rel18 (CAPIF) and based on these requirements the UE has access to network APIs via CAPIF.
UE policy cannot cover security and privacy aspects related to direct UE exposure in general for all services.
Any service exposure via NW API would potentially create a value and business opportunity for operators.
Direct access from UE application towards the UE seems to be only applicable for V2X and public safety where operations are often outside of network coverage or with partial coverage.

## Slide 6: Why it is important to keep full control in network
Sensing is a completely new feature which can be used to track objects behind walls and also track for instance people without any easy way to get consent.
  In home environment it is natural that you are allowed to do sensing in your flat but certainly not in your neighbours.
  In many ways this can be seen as setting up a camera and in some occasions even beyond that.
  Regulations will be expected similar to setting up cameras.
  Network control can improve consumers’ confidence in this new technology.
  The resolution of sensing is critical since high resolution may reveal information to enable identification of persons.
  Some concrete examples where network control could be of special importance include: military installations; public buildings like schools or police stations; public restrooms; neighbouring apartments or hotel rooms e.g. with drywall or sheetrock.