## Slide 1: Discussion on the requirements for slice-based PLMN selection
Huawei

## Slide 2: Background
S1-233012/C1-236565 “LS on the requirements for slice-based PLMN selection”
Related SA1 service requirements:
  SMARTER (R15) – TR 22.864 (clause 5.1) / TS 22.261
  The 5G system shall support a mechanism for the VPLMN, as authorized by the HPLMN, to assign a UE to a network slice with the needed services or to a default network slice.
  EASNS (R18) - TR 22.835 (clause 5.5) / TS 22.261(CR 0505)
  For a roaming UE activating a service/application requiring a network slice not offered by the serving network but available in the area from other network(s), the HPLMN shall be able to provide the UE with prioritization information of the VPLMNs with which the UE may register for the network slice.
These requirements are aligned with the basic principle as stated in TR 22.864 clause 5.1:
To guarantee a consistent user experience and support of services in case of roaming, slices composed of the same network functions should be available for the user in the VPLMN. Configuration of network slices and provisioning of proprietary functions will be based on agreements between operators.

## Slide 3: Question 1
Question 1: Would SA1 be able to provide any additional guidance regarding Scenario 1? In particular:
Whether the "prioritization information" defines priorities between the PLMNs or between the slices?
If the answer to a) is “between the slices”, should the prioritization of slices be determined by the network or by the UE?
Observation #1:
  This is particularly related to R18 EASNS - TR 22.835 (clause 5.5) / TS 22.261(CR 0505)
  For a roaming UE activating a service/application requiring a network slice not offered by the serving network but available in the area from other network(s), the HPLMN shall be able to provide the UE with prioritization information of the VPLMNs with which the UE may register for the network slice.
and the "prioritization information" is intended for the priorities between the PLMNs.
Proposal #1:
Answer 1:
a) The prioritization information is about the priorities between the PLMNs.
b) n/a

## Slide 4: Question 2
Question 2: Should a slice determined according to Scenario 2 be considered as being offered by the serving network or not? If yes, then is the slice determined from the non-default URSP rule to be considered as higher priority than the slice determined from the default URSP rule?
Observation #2:
  This is particularly related to R15 SMARTER – TR 22.864 (clause 5.1) / TS 22.261
  The 5G system shall support a mechanism for the VPLMN, as authorized by the HPLMN, to assign a UE to a network slice with the needed services or to a default network slice.
and a slice determined according to Scenario 2 should be considered as being provided by the serving network, as authorized by the HPLMN.
Proposal #2:
Answer 2: A slice determined according to Scenario 2 can be considered as being provided by the serving network, as authorized by the HPLMN. SA1 has no specific requirement regarding the priority between the slice determined from the non-default URSP rule and the one from the default URSP rule. However, SA1 believes it is down to HPLMN’s authorisation, as stated in the following requirement in TS 22.261:
The 5G system shall support a mechanism for the VPLMN, as authorized by the HPLMN, to assign a UE to a network slice with the needed services or to a default network slice.

## Slide 5: Question 3
Question 3: Would SA1 be able to provide any additional guidance regarding the interaction between legacy PLMN selection prioritization and new prioritization information for slice based PLMN selection? In particular:
which list has a higher priority while performing PLMN selection?;
does the trigger to perform SOR apply when the UE uses slice-based PLMN selection?
Observation #3:
  To minimize the impact on the legacy UEs, it is preferred to decouple the slice-based PLMN selection from the legacy PLMN selection. Note this is generally agreed in CT1 discussion on this topic.
  Slice-based PLMN selection is triggered when an application needs a specific slice, during which the corresponding list has higher priority. When the specific slice is not needed, the list associated with the legacy PLMN selection takes higher priority.
Proposal #3:
Answer 3: Slice-based PLMN selection is triggered when an application needs a specific slice, during which the corresponding list has higher priority. When the specific slice is not needed, the list associated with the legacy PLMN selection takes higher priority.
When the slice-based VPLMN selection is enabled, the corresponding list has higher priority.
Slice-based PLMN selection is triggered only when an application needs a specific slice. Therefore the trigger to perform SOR does not apply.

## Slide 6: Proposed way forward
LS on Slice based PLMN selection:
- The reply is essential for CT1 to be able to continue this work.
- SA asked SA1 to exceptionally take any action needed to speed up the discussion.
Basic Principle: It is important for SA1 to provide sufficient clarity for other WGs to get on with their work, while focusing on SA1 level aspects.
Proposed way forward: There are clear SA1 service requirements on the related aspects. The reply LS would provide information to confirm SA1’s service requirements. The following answers can be considered as baseline for the reply.
Answer 1: a) The prioritization information is about the priorities between the PLMNs. b) n/a
Answer 2: A slice determined according to Scenario 2 can be considered as being provided by the serving network, as authorized by the HPLMN. SA1 has no specific requirement regarding the priority between the slice determined from the non-default URSP rule and the one from the default URSP rule. However, SA1 believes it is down to HPLMN’s authorisation, as stated in the following requirement in TS 22.261:
The 5G system shall support a mechanism for the VPLMN, as authorized by the HPLMN, to assign a UE to a network slice with the needed services or to a default network slice.
Answer 3: Slice-based PLMN selection is triggered when an application needs a specific slice, during which the corresponding list has higher priority. When the specific slice is not needed, the list associated with the legacy PLMN selection takes higher priority.
When the slice-based VPLMN selection is enabled, the corresponding list has higher priority.
Slice-based PLMN selection is triggered only when an application needs a specific slice. Therefore the trigger to perform SOR does not apply.