## Slide 1
S1-233027, 3GPP TSG SA1#104, 13-17 November 2023
Motivation for study on distributed device and user-centric trust
InterDigital

## Slide 2: Motivations of distributed device and user trust
5GS lacks distributed and user-centric trust
  Wireless system evolution toward 6G will feature increasingly distributed networks and services.
  Such distributed networks and services may be from different organizations (administrative domains) and may not have pre-established mutual trust relationships.
  5GS primary authentication is based on the shared root key stored at SIM card and the core network. It does not reflect any trust on the user or device behavior. User-centric trust can provide another level of trustworthiness.
  ProSe in 5GS assumes relay UEs are trustable. However, relay UEs and remote UEs may be from different organizations and may not trust each other.
Distributed device and user-centric trust will bring multitude benefits to 5GS and beyond
  Increased system resiliency:
    Distributed trust removes the strict need for a centralized party such as home networks and avoids single point of failure.
  Improve system performance:
    Distributed trust enables direct interactions between devices and local networks without relying home networks.
    Local interactions are more efficient in terms of communication overhead.
  Support dynamic trust monitoring, evaluation and assessment:
    The context of devices and networks changes dynamically.
    As such, dynamic trust monitoring, evaluation and assessment are required.
  Enable new service models in 5GS and beyond:
    Dynamic and direct network access services between & across devices/users, visited networks and NPNs, which helps extend network coverage and improve user experience.
    Distributed and trustworthy services among devices, between devices and networks, and between different networks.
3GPP needs a unified study and solutions for trustworthy 5GS and beyond

## Slide 3: Clarifications on some concepts
Distributed Trust
  Trust relationship built without fully relying on a centralized party (but such a centralized party may be used to facilitate to build distributed trust relationship).
  Distributed trust can be established among devices, between devices and networks (home, visited, or NPNs), or between networks.
  Distributed trust can enable trustworthy services, such as:
    1) services that a device can provide to another device;
    2) services that a network can provide to a device or vice versa; and
    3) services that a network can provide to another network.
User-Centric Trust
  Trust relationship relying on user credentials instead of fully relying on or in addition to SIM-based primary authentication in current 5GS.
  User-centric trust can be established among devices, and between devices and networks.
  User-centric trust can enable user-centric trustworthiness expanding or beyond existing SIM-based authentication and trust.
There are existing technologies, such as distributed ledgers, Self-Sovereign Identity (SSI), Decentralized Identifiers (DID) and verifiable credentials, that can enable distributed device and user-centric trust.

## Slide 4: Use cases
Mutual trust needs to be established between a Roaming UE and a Visited Network (VN)
Three scenarios in future 3GPP systems
  Scenario 1: Roaming UE-1 needs to access to VN 1, however the Home Network (HN) becomes unreachable.
  Scenario 2: Roaming UE-2 requests dynamic services from VN 2, which is a distributed network like NPN. No HN.
  Scenario 3: Roaming UE-3 has no Subscriber Identity Module (SIM) card. Roaming UE-3 needs to access to VN 3. No HN.
Source: NextG Alliance TWG Report on 6G Technologies for Wide Area Cloud Evolution (March 2023)
In 6G wide area cloud environment, system nodes, such as client devices and infrastructure servers, must make independent decisions about the trustworthiness of the system nodes they are interacting with.
  For example, client devices must establish the trustworthiness of the servers to whom they entrust to provide computation and storage services. In turn, the computing platforms used to provide these services must be able to determine the trustworthiness of the clients that request their services to avoid attacks on the infrastructure

## Slide 5: Objectives
Study use cases and potential service requirements for 5GS to support distributed device and user-centric trust:
  New service scenarios which demand and/or can be built upon distributed trust.
  New service scenarios which demand and/or can be built upon user-centric trust.
  Study the impact of distributed and user-centric trust on existing functionality in 5GS, e.g., security, authentication, and charging.
  Gap analysis of existing 5GS functionalities in contrast to identified new service scenarios.
  Study of potential technologies to enable distributed and user-centric trust for 5GS and beyond.
  Potential new requirements in enabling distributed and user-centric trust between devices and networks in 5GS and beyond.
  Potential new requirements in enabling distributed and user-centric trust among devices in 5GS and beyond.
  Potential new requirements in enabling distributed and user-centric trust between networks in 5GS and beyond.
Some Relevant Activities
SWS-230027 (MITRE): Identified distributed authentication architecture based on non-centralized infrastructure network in the context of Non-public networks (August 2023)
S1-203219 (China Unicom): Discussion on New SID: Study on Distributed AIoT Network (August 2020)
S1-202053 (Spread Communications): Motivation for R18 SID proposal of Blockchain for mobile communication system (July 2020)
ETSI PDL-021: PDL Use Cases in 3GPP Networks (August 2023)
  “Decentralized certificate management, decentralized credential management, decentralized identity management”
  PDL: Permissioned Distributed Ledger

## Slide 6
Thank you!