## Slide 1: New Study on NetShare phase 2
China Unicom
weiqun5@chinaunicom.cn

## Slide 2: The existing requirements in R19
The requirements on Indirect Network Sharing have been specified in clause 6.21 of TS 22.261 under the following aspects:
General
Mobility
Network access control
Regulatory services
Charging
NOTE : Requirements of Indirect Network Sharing assume no impact on UE.
Notes: 绿色的区域是低密度，但是需要与粉色保持连续性的地区。
这一页主要是 OP2在没有合适覆盖时，可以使用OP1的低密度覆盖区域的5G网络。OP1还可以提高低密度区域网络利用率。
两个重要的好处，
1、如果粉色和绿色需要开网络共享，只需要考虑边界2块的连续性和无线参数修改。而不需要考虑其他4块的改变。
2、绿色可以是已经建设好的5G覆盖、粉色可以自行建设和扩容等。商务、建设和维护的捆绑性小。减少多个运营商人为参与。尤其在运维方面。

## Slide 3
Potential Scenario in R20: shared satellite network
Shared satellite network ?
①
②
③
Figure ① : Satellite network is not only an effective complement to terrestrial networks, but can also play an important role in network access in areas or scenarios that are inaccessible to terrestrial networks.
Figure ② : The use case described in clause 5.7 of TR 22.851 has involved the “satellite network sharing” in some special scenarios, e.g. desert, islands, forests, and etc. However, the Indirect Network Sharing considering to share satellite network has not been investigated fully in R19 item.
Figure ③ : illustrates the example to share the satellite network using the mechanism of Indirect Network Sharing.
Notes: 5G 覆盖范围为500米， 比4G密度增加50%。铁路建设成本提升大幅度；
分区域合作建设可能是有效办法之一。
铁路沿线在国家内需要显示统一网号，但是支持铁路沿线服务连续性。
该场景特点是高铁使用高速业务比较多
其他类似的场景都在场景附件中

## Slide 4
Gaps compared with the existing requirements
Hosting satellite OP1
Participating terrestrial OP3
Hosting terrestrial OP2
Question: how to perform network selection in the overlapping area?
Potential scenario: The coverage of OP1’s shared satellite network may overlap with OP2’s shared 5G network.
If the UE of participating operator moves into this shared area, the network selection needs to be performed considering lots of factors, e.g., charging, regulation, service.
Potential scenario: Currently, LEO satellites are being used more widely. And 3GPP SA2 R19 also began to study the satellite network of regenerative payload generic architecture.
Since the LEO satellite is always moving relative to the ground, if the LEO satellite network is used as a hosting operator network in Indirect Network Sharing scenario, when the LEO satellite moves to a shared area, it can broadcast the information of the corresponding participating operator to provide access service, but if the LEO satellite moves to other non-shared areas, in order to reduce interference and consider other factors, it should not broadcast the information of the corresponding participating operator temporarily.
The existing requirement as specified in clause 6.21 of TS 22.261 “A 5G satellite access network shall support NG-RAN sharing” is too general and not enough.
Notes: 对于MOCN RAN连接到每个HPLMN核心网
对于GWCN RAN可以连接到一个MSC/SGSN，但可以查询多个网络的用户数据。
UE接入HPLMN
网络共享场景中
RAN连接到的是拜访网络中，属于OP1
RAN与HPLMN之间存在拜访网络
UE的用户数据并不在OP1
UE接入拜访网络
能需要明确定义。如果是SNPN方式的可能不是基于roaming的。如果是否要基于一些SNPN的参数做。
这个片子的价值在于澄清对于网络共享的概念属于漫游场景。
另外就是RAN可以广播多个PLMN，其中可以有OP1和OP2.
到了AMF（OP1），实际上是作为VPLMN来接入的。并不会直接接入HPLMN。
challenge1: AMF 需要区分，哪些从OP1 PLMN接入，哪些从OP2 PLMN接入。
challenge2: 移动性原来是网内，现在出现网间。

## Slide 5
Potential Scenario in R20: minimization of service interruption
?
Disaster condition
Potential scenario: Normally, in some area, the UE of OP2 will access the OP2’s RAN and core network to use the service and the UE of OP1 will access the OP1’s RAN and core network to use the service separately. When arising the disaster condition, the OP2’s RAN or OP2’s core network or both broke down, we hope that the UE of OP2 will access to the OP1’s network using the mechanism of Indirect Network Sharing to minimize the service interruption.
Gap analysis: Compared with the existing requirements of minimization of service interruption specified in clause 6.31 of TS 22.261. Using Indirect Network Sharing to achieve the minimization of service interruption can be transparent to UE.
This mechanism needs to consider when and how to trigger the NG-RAN of hosting operator to broadcast the participating operator’s information and how to select the core network of participating operator if the core network of participating operator in this disaster area has broken.
?
?
PLMN ID of OP2
Notes: 5G 覆盖范围为500米， 比4G密度增加50%。铁路建设成本提升大幅度；
分区域合作建设可能是有效办法之一。
铁路沿线在国家内需要显示统一网号，但是支持铁路沿线服务连续性。
该场景特点是高铁使用高速业务比较多
其他类似的场景都在场景附件中

## Slide 6: Thank you