## Slide 1
S1-221073, 3GPP TSG SA1#98e, 9 - 19 May 2022, e-meeting
China Mobile
Motivation of Study on Energy Efficiency as Service Criteria Ph2

## Slide 2: Motivation
  Follow the study and work on Energy Efficiency as service criteria in R19, more scenarios can be studied to further address the improvement of energy saving and energy efficiency from end-to-end perspectives.
  For example, for services served by multiple PLMNs (i.e. roaming case), different energy consideration and different capabilities of the networks need to be considered, related information exchange and other functional requirements may needed.
  For low-orbit satellite, energy is usually limited, the limitation of total energy consumption of RAN or 5GC NF on satellite will need to be consider as a prerequisite when considering the communication service.
  In the previous study, only service with best effort was considered with policy to limit energy consumption. In this release, with user preference, services with QoS requirement can also consider this kind of policy control and adjustment.
  Besides, study on network supporting for UE energy saving is also needed.
  The studies of SA, SA2, SA5 and RAN and especially ongoing work on energy efficiency will be taken into account as the starting point and cooperation of this study in SA1.

## Slide 3
  For services served by multiple PLMNs (i.e. roaming case), there may exist the following issues:
  HPLMN and VPLMN may have different energy related capabilities. For example, In HR roaming, HPLMN makes energy related decision (e.g. NF re-selection based on energy status), which is beyong the capability of VPLMN.
  HPLMN and VPLMN may have different consideration on energy and experience trade-off. For example, for a service, HPLMN takes priority to energy efficiency while VPLMN considers user experience more important. This requires inter-PLMN negotiation.
Use case 1: network energy saving involving different PLMNs
VPLMN Core
DN
App
HPLMN Core
Network capability&consideration negotiation

## Slide 4
  UE may have energy related requirement, e.g. keeping certain services with as low as possible energy consumption. Except for UE behavior (e.g. turning on energy saving mode), there are also operations can be performed by network. For example,
  Reducing paging frequency or improving periodic update time may reduce UE energy consumption.
  Degrading QoS level for ongoing services may reduce UE energy consumption.
Use case 2: network supporting UE energy saving requirement
Core Network
DN
App
Paging frequency reduction
QoS level degradation

## Slide 5: Objectives:
The objectives include:
  Support energy efficiency in 5G through new approaches to delivering services (e.g. adding energy efficiency as a selection criteria).
  Support energy consumption framework to optimally use different communication capabilities of the 5G system taking into account energy consumption along with efficiency, latency, and data rate.
  Interaction between network and application on UE/application energy consumption statues for network condition modification.
  Note: There’s no implication on 3GPP will provide energy efficiency as a trade-off to service quality.
Other aspects include security, charging and privacy.

## Slide 6
Thank you!