## Slide 1: Discussion on PS Data Off exemption for services over IMS DC
Huawei, China Mobile

## Slide 2: Background
S2-2311881 “LS to clarify PS Data Off exemption for services over IMS DC”
SA2 kindly asks SA1 to clarify how the term “Services” in “Services over IMS Data Channel” needs to be interpreted, and whether applications using IMS Data Channel should be configurable separately for PS data off exempt or all applications over IMS Data Channel should be treated in the same way.
Related SA1 service requirement: TS 22.011 CR 0348
  Each of the following operator services shall be configurable by the HPLMN operator to be part of the 3GPP PS Data Off Exempt Services:
  - MMTel Voice;
  - SMS over IMS;
  - USSD over IMS (USSI);
  - MMTel Video;
  - Services over IMS Data Channel;
  - Particular IMS services not defined by 3GPP, where each such IMS service is identified by an IMS communication service identifier;
  - Device Management over PS
  - Management of USIM files over PS (e.g. via Bearer Independent Protocol); and
  - IMS Supplementary Service configuration via the Ut interface using XCAP.
  NOTE 1a: IMS Data Channel is defined in 3GPP TS 26.114[20].

## Slide 3: SA1 agreement in TS 22.011 CR0348
Observation:
  In the related SA1 discussion, companies expressed different views on how this feature would be used. Depending on business models and network deployment, some might require applications using IMS Data Channel be configurable separately for PS data off exempt while some might need all applications over IMS Data Channel be treated in the same way.
  This requirement is therefore agreed to allow flexibility for operators to configure the intended services over IMS data channel as part of the 3GPP PS Data Off Exempt Services.
Reason for change: | The LS (S1-230045/S2-2301827) from SA2 asks SA1 to investigate whether IMS data channel should be considered as a feature to be exempted when PS Data Off is activated. By adding services over IMS data channel to the list of 3GPP PS Data Off Exempt Services, operators can configure whether the services over IMS data channel will still be enabled when the user sets the UE to PS Data Off.
Summary of change: | Define services over IMS Data Channel as part of the 3GPP PS Data Off Exempt Services.
Consequences if not approved: | When PS Data Off is activated, applications relying on IMS Data Channel will not be available and part of IMS multimedia telephony service will be impacted.

## Slide 4: Proposed way forward
  It is proposed the following answer to SA2’s question, and a CR to provide the clarity.
Proposal:
Answer -
In the related SA1 discussion, companies expressed different views on how this feature would be used. Depending on business models and network deployment, some might require applications using IMS Data Channel be configurable separately for PS data off exempt while some might need all applications over IMS Data Channel be treated in the same way.
This requirement is to allow flexibility for operators, according to business models and/or network deployment, to configure the intended services over IMS data channel as part of the 3GPP PS Data Off Exempt Services.
The corresponding update to the requirement –
  Each of the following operator services shall be configurable by the HPLMN operator to be part of the 3GPP PS Data Off Exempt Services:
  - MMTel Voice;
  - SMS over IMS;
  - USSD over IMS (USSI);
  - MMTel Video;
  - Services over IMS Data Channel;
  - Particular IMS services not defined by 3GPP, where each such IMS service is identified by an IMS communication service identifier;
  - Device Management over PS
  - Management of USIM files over PS (e.g. via Bearer Independent Protocol); and
  - IMS Supplementary Service configuration via the Ut interface using XCAP.
  NOTE 1a: IMS Data Channel is defined in 3GPP TS 26.114[20].
  NOTE 1b: It is to allow flexibility for operators, according to business models and/or network deployment, to configure the intended services over IMS data channel as part of the 3GPP PS Data Off Exempt Services.