## Slide 1
S1-233151, 3GPP TSG #104, 13 - 17 November 2023, Chicago, USA
Discussion on Multi-network Interoperability Enhancement
China Unicom
Chenyi Li, licy1036@chinaunicom.cn

## Slide 2
The early deployments are adopting NSA as a means of fast launching 5G and may gradually evoluting to SA. Based on operators’ different network development progress and deployment strategies, SA networks and NSA networks will coexist and interact in same PLMN or different PLMNs for a long period of time.
However, those are not suffient enough that data service offering is remain undefined where 5G network subscribers cannot be provided 5G data service in current SA and NSA coexisting situation in some cases.
Standard capabilities to enable 5G data service offerings to all 5G subscribers are essential to guarantee the user service experience and extend service area.
To reduce excessive investment and save cost by avoiding implememt 5GC network elements at once in network evolution from EPC based NSA to 5GC based SA.
Background & Motivation
Notes: 22.261 The 5G system shall support a UE with a 5G subscription roaming into a 5G Visited Mobile Network which has a roaming agreement with the UE's 5G Home Mobile Network.

## Slide 3: Gap Analysis
Existing reqs and specs
  TS 22.261 specified requirements of supporting interworking between 5G systems and interoperability with legacy 3GPP systems
  TS 23.501 defined architectures for interworking between 5GS and EPC via dedicated entities (i.e. SMF+PGW-C, UPF+PGW-U, UDM+HSS), and interworking procedures are described in TS 23.502
  TS 23.292 defined the interworking architecture, reference points and procedures between CS and IMS domain to enable IMS service to be controlled via IMS rather than via CS mechanisms
Proposal: Enable 5G data service to be provided for all subscribers of a 5G network and for inbound roamers
Gaps
  Does not cover non-roaming case, e.g. a UE with a 5G(NSA) subscription moves to SA only area
  Does not cover core networks without the dedicated entities
  Data service offering capability and mechanisms between 5GC and EPC are remain undefined
Notes: Proposal: Enable 5G data service to be provided for all subscribers of a 5G network and for inbound roamers

## Slide 4
Roaming scenario: when subscribers of a 5G network roaming from a NSA network to a SA network, there is no roaming specified when HPLMN deploys NSA by supporting EPC only and VPLMN deploys SA by supporting 5GC only.
Non-roaming scenario: subscribers of EPC based NSA networks move from NSA area to SA only area.
Potential Scenario
NSA area
subcriber of 5G service
5G SA gNB
5G NSA gNB
SA 5GC
EPC
SA area
×
VPLMN
HPLMN NSA
Inbound roamer (subscriber of 5G network)
5G SA gNB
eNB
SA 5GC
EPC
×
EPC
EPC roaming
5G NSA gNB
subscriber of the 5G network

## Slide 5: Proposal
Investigate use cases which enable 5G system (e.g. 5G SA network) to provide data service for pre-R15 network (e.g. 5G NSA option 3) users.
Derive potential requirements from those use cases regarding the following aspects:
  Network access control
  Subscription data retrievement & generation
  Service continuity
  Idnetify user’s subscription type (i.e., subscription 5G SA network or NSA network if those networks are coexisting)

## Slide 6
Thank you!