## Slide 1: About KPIs related to “5G-enabled Traffic Flow Simulation and Situational Awareness”
LW Goix
Nokia, Nokia Shanghai Bell

## Slide 2: Background
At SA1#103, it was agreed in S1-232412 to put area traffic capacity of the “5G-enabled Traffic Flow Simulation and Situational Awareness” use case in TS22.156 “[TBD]”
This document discusses the current values for calculation and proposes a new set of values
The newly proposed values heavily rely on the 5G Automobile Association White Paper "C-V2X Use Cases Volume II: Examples and Service Level Requirements“ document (TS22.156, reference [8])

## Slide 3: Current status
TS22.156, table 6.2.1
Use Cases | Characteristic parameter (KPI) |  |  |  | Influence quantity |  |  |  |  | Remarks
 | Max allowed end-to-end latency | Service bit rate: user-experienced data rate | Reliability | Area Traffic capacity | Message size (byte) | Transfer Interval | Positioning accuracy | UE Speed | Service Area | 
5G-enabled Traffic Flow Simulation and Situational Awareness (NOTE 2) | [5-20] ms (NOTE 1) | [10~100] Mbit/s [8] (NOTE 6) | > 99.9% | [TBD] Tbit/s/km2 (NOTE 5) | - | 20~100 ms (NOTE 3) | - | < 250 km/h | City or Country wide (NOTE 4) | UL
NOTE 1: The mobile metaverse server receives the data from various sensors, performs data processing, rendering and provide feedback to the vehicles and users. NOTE 2: Examples of typical data volume including 1) camera: 10 Mbit/s per sensor (unstructured), 2) LiDAR: 90 Mbit/s per sensor (unstructured), 3) radar: 10 Mbit/s per sensor (unstructured), and 4) real-time Status information including Telemetry data: [< 50 kbit/s] per sensor/vehicle/VRU (structured). This is to support at least 80 vehicles and 1600 users present at the same location (e.g. in an area of 40m*250m) to actively enjoy immersive metaverse services for traffic simulation and traffic awareness, the area traffic capacity is calculated considering 2 cameras, 2 Radars, 2 LiDARs on road side, 1600 user’s smart phones and 80 vehicles with 7 cameras, 4 radar and 2 LiDAR for each vehicle. NOTE 3: The frequency considers different sensor types such as Radar/LiDAR (10Hz) and camera (10~50Hz). NOTE 4: The service area for traffic flow simulation and situational awareness depends on the actual deployment, for example, it can be deployed for a city or a district within a city or even countrywide. In some cases a local approach (e.g. the application servers are hosted at the network edge) is preferred in order to satisfy the requirements of low latency and high reliability. NOTE 5: The calculation is this table is done per one 5G network, in case of N 5G networks to be involved for such use case in the same area, this value can be divided by N. NOTE 6: User experienced data rate refers to the data rate needed for the vehicle or human, the value is observed from industrial practice.

## Slide 4: Current status
TS22.156, table 6.2.1 / Main current assumptions
[“typical data volume” extracted from NOTE 2]
1) camera: 10 Mbit/s per sensor (unstructured),
2) LiDAR: 90 Mbit/s per sensor (unstructured),
3) radar: 10 Mbit/s per sensor (unstructured),
4) real-time Status information including Telemetry data: [< 50 kbit/s] per sensor/vehicle/VRU (structured).
This is to support at least 80 vehicles and 1600 users present at the same location (e.g. in an area of 40m*250m) to actively enjoy immersive metaverse services for traffic simulation and traffic awareness.
The area traffic capacity is calculated considering:
2 cameras, 2 Radars, 2 LiDARs on road side,
1600 user’s smart phones
80 vehicles with 7 cameras, 4 radar and 2 LiDAR for each vehicle.
Such an area is equivalent to 10m*1km. 1km2 (capacity metric) corresponds to 100 of such areas
Number of road side in this area not precised : assumption is 1 camera/radar/lidar per road direction
Note: 2.36 is 17x lower than current value in TR22.856 cl 7.2 (was 39.6Tb/s/km2 before TBD)
CURRENT | bitrate | vehicle | user | road |  | 
 | Mb/s | 80 | 1600 | 1 |  | 
camera | 10 | 7 |  | 2 |  | 
lidar | 90 | 2 |  | 2 |  | 
radar | 10 | 4 |  | 2 |  | 
status | 0.05 | 13 | 1 | 6 |  | 
 | per item | 290.65 | 0.05 | 220.3 |  | 
 | total | 23252 | 84 | 220.3 | 23556.30 | Mb/s
 |  |  |  | x100 | 2.36 | Tb/s/km2

## Slide 5: Current status
TS22.156, table 6.2.1 / Proposal and motivations
[“typical data volume” extracted from NOTE 2]
1) camera: 10 Mbit/s per sensor (unstructured),
2) LiDAR: 90 Mbit/s per sensor (unstructured),
3) radar: 10 Mbit/s per sensor (unstructured),
4) real-time Status information including Telemetry data: [< 50 kbit/s] per sensor/vehicle/VRU (structured).
This is to support at least 80 vehicles and 1600 users present at the same location (e.g. in an area of 40m*250m) to actively enjoy immersive metaverse services for traffic simulation and traffic awareness.
The area traffic capacity is calculated considering:
2 cameras, 2 Radars, 2 LiDARs on road side,
1600 user’s smart phones
80 vehicles with 7 cameras, 4 radar and 2 LiDAR for each vehicle.
From 5GAA “Infrastructure Assisted Environment Perception” use case:
Assumes RADAR sensors already generate object lists for observed vehicles […] From RADAR to local compute unit for sensor fusion 80-160 Kbps.
Assuming each LIDAR sensor creates point clouds and not object lists. […] From LIDAR sensors to local compute unit: 35Mbps per sensor
From cameras to local compute unit 5-8 Mbps per camera
From 5GAA “HD map collecting/sharing” use case:
Case 1: Unprocessed but compressed sensor data sent to the HD map provider. 47 Mbps is derived from: H.265/ HEVC HD camera ~8 Mbps + LIDAR ~35 Mbps + other sensor data.
Case 2: Processed sensor data (interpreted objects) sent to the HD map provider. Assumed 1 kB/Object/100 ms x 50 objects per car: 4 Mbps.
New proposed values:
1) camera: 8 Mbit/s per sensor (unstructured),
2) LiDAR: 35 Mbit/s per sensor (unstructured),
3) radar: 160 Kbit/s per sensor (unstructured),
4) real-time Status information including Telemetry data: [< 50 kbit/s] per sensor/vehicle/VRU (structured).
Based on 5GAA "C-V2X Use Cases Volume II: Examples and Service Level Requirements", 5G Automobile Association White Paper (TS22.156, reference [8])

## Slide 6: Current status
TS22.156, table 6.2.1 / Proposal and motivations
[“typical data volume” extracted from NOTE 2]
1) camera: 10 Mbit/s per sensor (unstructured),
2) LiDAR: 90 Mbit/s per sensor (unstructured),
3) radar: 10 Mbit/s per sensor (unstructured),
4) real-time Status information including Telemetry data: [< 50 kbit/s] per sensor/vehicle/VRU (structured).
This is to support at least 80 vehicles and 1600 users present at the same location (e.g. in an area of 40m*250m) to actively enjoy immersive metaverse services for traffic simulation and traffic awareness.
The area traffic capacity is calculated considering:
2 cameras, 2 Radars, 2 LiDARs on road side,
1600 user’s smart phones
80 vehicles with 7 cameras, 4 radar and 2 LiDAR for each vehicle.
Based on 5GAA "C-V2X Use Cases Volume II: Examples and Service Level Requirements", 5G Automobile Association White Paper (TS22.156, reference [8])
Current assumption is realistic, although more accurately we propose:
8 radars (4x per each bumper)
1 LiDAR (front) – pricing reason
Current assumption means (x100, see prev. slide):
8k vehicles/km2
160k users/km2
However, from TS22.261, cl 7.1.1
4k-10k vehicles/km2
100-50k users/km2 [10.000 “urban macro users”/km2]
From 5GAA, “maximum assumed density in urban situation” is 12.000 vehicles/km2
Current assumption is realistic. From 5GAA:
Each edge node is responsible for a certain section of highway, for example 1-2 km in length. Sensors on this section of the road are connected to at least one edge node which is then generating an environmental map for this 1-2 km road section.
Connecting more than two cameras to a state-of-the-art (edge) server is currently unlikely.
The first edge node transmits the information about all observed objects to the next node in line. [proposal : x2 of the traffic generated by the road side equipments towards the first node – to receive AND retransmit the data]
Assumption for “lane width” is 3m (for the two directions with 3 lanes in each direction, around 20m)

## Slide 7: Current vs proposed values
CURRENT | bitrate | vehicle | user | road |  |  |  | PROPOSED | bitrate | vehicle | user | road |  | 
 | Mb/s | 80 | 1600 | 1 |  |  |  |  | Mb/s | 120 | 100 | 2 |  | 
camera | 10 | 7 |  | 2 |  |  |  | camera | 8 | 7 |  | 2 |  | 
lidar | 90 | 2 |  | 2 |  |  |  | lidar | 35 | 1 |  | 2 |  | 
radar | 10 | 4 |  | 2 |  |  |  | radar | 0.16 | 8 |  | 2 |  | 
status | 0.05 | 13 | 1 | 6 |  |  |  | status | 0.05 | 16 | 1 | 6 |  | 
 | per item | 290.65 | 0.05 | 220.3 |  |  |  |  | per item | 93.08 | 0.05 | 86.62 |  | 
 | total | 23252 | 84 | 220.3 | 23556.30 | Mb/s |  |  | total | 11169.6 | 11 | 173.24 | 11353.84 | Mb/s
 |  |  |  | x100 | 2.36 | Tb/s/km2 |  |  |  |  |  | x100 | 1.14 | Tb/s/km2

## Slide 8: Proposed change
TS22.156, table 6.2.1, NOTE 2
Current
Examples of typical data volume including 1) camera: 10 Mbit/s per sensor (unstructured), 2) LiDAR: 90 Mbit/s per sensor (unstructured), 3) radar: 10 Mbit/s per sensor (unstructured), and 4) real-time Status information including Telemetry data: [< 50 kbit/s] per sensor/vehicle/VRU (structured). This is to support at least 80 vehicles and 1600 users present at the same location (e.g. in an area of 40m*250m) to actively enjoy immersive metaverse services for traffic simulation and traffic awareness, the area traffic capacity is calculated considering 2 cameras, 2 Radars, 2 LiDARs on road side, 1600 user’s smart phones and 80 vehicles with 7 cameras, 4 radar and 2 LiDAR for each vehicle.
Proposed
Based on [8] and 3GPP TS22.261 [7], typical data volume include 1) camera: 8 Mbit/s per sensor (unstructured), 2) LiDAR: 35 Mbit/s per sensor (unstructured), 3) radar: 160 Kbit/s per sensor (unstructured), and 4) real-time Status information including Telemetry data: [< 50 kbit/s] per sensor/vehicle/VRU (structured). Typical urban density [8] considers 120 vehicles and 220 users/smartphones (120 drivers + 100 VRU) present in an area of 40m*250m to actively enjoy immersive metaverse services for traffic simulation and traffic awareness. This further considers 2 cameras, 2 Radars, 2 LiDARs on road side per direction, which communicate with the same equipments at previous road side infrastructure node. Estimated vehicle equipments are 7 cameras, 8 radar and 1 LiDAR for each vehicle.

## Slide 9: Proposed change
TS22.156, table 6.2.1
Use Cases | Characteristic parameter (KPI) |  |  |  | Influence quantity |  |  |  |  | Remarks
 | Max allowed end-to-end latency | Service bit rate: user-experienced data rate | Reliability | Area Traffic capacity | Message size (byte) | Transfer Interval | Positioning accuracy | UE Speed | Service Area | 
5G-enabled Traffic Flow Simulation and Situational Awareness (NOTE 2) | [5-20] ms (NOTE 1) | [10~100] Mbit/s [8] (NOTE 6) | > 99.9% | 1.14 Tbit/s/km2 (NOTE 5) | - | 20~100 ms (NOTE 3) | - | < 250 km/h | City or Country wide (NOTE 4) | UL
NOTE 1: The mobile metaverse server receives the data from various sensors, performs data processing, rendering and provide feedback to the vehicles and users. NOTE 2: Based on [8] and 3GPP TS22.261 [7], typical data volume include 1) camera: 8 Mbit/s per sensor (unstructured), 2) LiDAR: 35 Mbit/s per sensor (unstructured), 3) radar: 160 Kbit/s per sensor (unstructured), and 4) real-time Status information including Telemetry data: [< 50 kbit/s] per sensor/vehicle/VRU (structured). Typical urban density [8] considers 120 vehicles and 220 users/smartphones (120 drivers + 100 VRU) present in an area of 40m*250m to actively enjoy immersive metaverse services for traffic simulation and traffic awareness. This further considers 2 cameras, 2 Radars, 2 LiDARs on road side per direction, which communicate with the same equipments at previous road side infrastructure node. Estimated vehicle equipments are 7 cameras, 8 radar and 1 LiDAR for each vehicle. NOTE 3: The frequency considers different sensor types such as Radar/LiDAR (10Hz) and camera (10~50Hz). NOTE 4: The service area for traffic flow simulation and situational awareness depends on the actual deployment, for example, it can be deployed for a city or a district within a city or even countrywide. In some cases a local approach (e.g. the application servers are hosted at the network edge) is preferred in order to satisfy the requirements of low latency and high reliability. NOTE 5: The calculation is this table is done per one 5G network, in case of N 5G networks to be involved for such use case in the same area, this value can be divided by N. NOTE 6: User experienced data rate refers to the data rate needed for the vehicle or human, the value is observed from industrial practice.

## Slide 10: Thank you