## Slide 1: Study on Mobile Base Station Relay Phase2
S1 - 233161
CATT
Qing Wan (wanqing1@cictmobile.com)

## Slide 2: Motivation(1/2)
Existing 3GPP Requirements
SA1 Spec. | Requirements
TS 22.261 (SMARTER) | Capabilities of wireless self-backhaul (sec. 6.12) The scenarios of the user in vehicles connecting the network via onboard base station, and perf. KPIs (sec. 7.1)
TR 22.829 TS 22.125 (R17 EAV) | Use cases of radio access nodes on-board UAV (UxNB) Operational requirements e.g. reduce interference(sec. 6.4)
TR 22.839 TS 22.261 (R18 VMR) | Use cases of terrestrial VMR serving users inside/nearby the vehicle Reqs of efficient operation, multi-link connectivity, mobility, charging(sec. 6.42)
UxNB
VMR
The enhancement of network operation on satellite access, satellite backhaul, network slicing, and non-public network were performed in parallel, which introduced new options for network deployment.

## Slide 3: Motivation(2/2)
Potential Use Cases and Gap Analysis
Use Case #1 E2E QoS Harmonization
Use Case #2 Relay Link Selection
As the UE moves from Area B to Area A, the UAV relay targeted to the UE flies together. The donor gNB linked to the relay has switched from one terrestrial gNB to onee satellite gNB or terrestrial gNB via satellite backhaul.
Gap Analysis: The impact(e.g. latency, bandwidth) of satellite access or multi-hops including satellite backhaul is not taken into account for UE QoS control using mobile base station relay.
UE#1(SST3: MIoT) and UE#2(SST1: eMBB) are served by the same UAV relay. The traffic from UE#1 can be transmitted to the network via donor gNB#1 due to the nearest geographic location. The traffic from UE#2 can be transmitted to the application service via donor gNB#2 for the more efficient content delivery.
Gap Analysis: The optimization of network behaviors for the data delivery has not considered the factor of traffic QoS.
Use Case #3 AN node selection between the vehicle relay(NR-Uu) with satellite gNB and terrestrial E-UTRAN macro base station
Gap Analysis: The interworking with E-UTRAN node is not considered in the previous study item.

## Slide 4
Identify additional use cases and potential new service requirements to improve 5GS support of mobile base station relays mounted on vehicle (e.g. UAV, train), using various wireless backhauling to connect to donor gNB and 5GC, including but not limited to the following aspects:
End-to-End QoS control for different mobility scenarios, e.g. the UE changes the mobile base station relay using different type of backhaul (e.g. NR, or satellite), the fixed relay of the UE switches the link to donor gNB of terrestrial access network to that of satellite access network.
Provisioning of the relay link to donor gNB for delivering the user traffic with different QoS, or different services(e.g. emergency services, MPS)
Interworking with E-UTRAN macro base station, e.g access control, mobility, QoS.
Aspects related to the operation impacted by power restriction, charging, regulatory requirements and etc.
Proposed Objectives

## Slide 5
Thank you!