## Slide 1: Study on High-availability IoT Services via Dual 3GPP Access
S1 - 233163
CATT
Hui Xu (xuhui@catt.cn)

## Slide 2: Motivation – Problems
Problem: MTC/Cellular IoT devices mainly rely on CP based services (e.g. SMS over NAS, NIDD) optimized for the upper-layer applications to save energy.
MR-DC with 5GC
C-Plane Connectivity
U-Plane Connectivity
X
Multi-USIM
X
5GC
E-UTRA
NR
Problem: Due to the restriction of BOM cost and form factor, the MTC devices will not support multiple USIMs embedded.
Only the master node(MN) has CP connection with 5GC
Both the master node(MN) and secondary node(SN) has UP connection with CN (see TS 37.340 and TS 23.501)
For some scenarios (e.g. medical monitoring, remote metering) with high demand on the service availability and reliability, the existing features of 3GPP system cannot cater to all use cases.

## Slide 3: Motivation – Typical use cases
Use Case #1 Last Gasp Message of Smart Meter
Use Case #2 Remote wakeup by MT SMS
Use Case #3 Positioning by inter-RAT Combination
Use Case #4 Positioning by CN Coordination
The “last gasp” message shall be delivered out to the application server before the device runs out of energy and powers off
Smart Meters
Remote Platform
5GC
E-UTRA
NR
Paging Strategy
When MT SMS arrives at the 5GC, which access path to page UE shall be handled by 5GC e.g. based on the status of reachability.
Positioning based on the measurement data from hybrid RAT nodes in different radio conditions, in order to improve the service availability and accuracy.
Existing location information of the same UE can be reused between two PLMNs when QoS fulfills the new request, in case of unavailable LCS in any CN.
Support high-availability IoT service via dual 3GPP access of the same or different CNs

## Slide 4
This study item intends to investigate the use cases and potential service requirements to improve 5GS for supporting IoT devices in high demand of service availability to obtain services via dual 3GPP access (e.g. NR& NR, NR & E-UTRA, terrestrial & satellite) of one or two core networks belonging to the same or different MNOs.
Include but not be limited to the following aspects:
Handling of control plane based services (e.g. SMS over NAS, Non-IP data delivery)
Handling of positioning service with the coordination of different RAT nodes.
Aspects related to roaming, security, regulatory services (e.g. PWS), charging, etc
NOTE 1: It’s assumed UE may have one subscription.
Proposed Objectives

## Slide 5
Thank you!