## Slide 1: Supplemental Network Extension (SUPNet)
Qualcomm
3GPP TSG SA WG 1 Meeting #104 S1-233224
Chicago, USA, 13 - 17 November 2023

## Slide 2: Motivations
Reducing MNO CAPEX/OPEX or cost vs price/GB for RAN deployment is a constant and increasing issue
  Especially challenging for densified/small cells, indoor coverage, remote areas, ad-hoc hotspots
An independent entity (e.g., premises/real-estate owner, 3rd party small cells provider) can deploy RAN nodes providing supplemental coverage/capacity extension for MNOs’ services
  The entity deploying the NW can be incentivized, by the MNO, for contributing to the MNO’s extended coverage & connectivity
  The supplemental NW can also provide specific CN functions, services or local breakout data connectivity
  Spectrum can be licensed/unlicensed, and can be owned by the MNO or the SUPNet provider
Some example target scenarios are:
  Indoor venues, e.g. shopping malls, commercial/enterprise buildings
  Remote areas with no/limited MNOs coverage
  Ad-hoc events / venues (e.g., music festival, sport venues)

## Slide 3: High-level concepts
Coverage & capacity extension service (to MNO / PLMNs)
Proof of Coverage / Usage and rewarding
SUPNet Provider
SUPNet RAN
PoC participants
(Assisting UE)
Normal UEs (using SUPNet RAN)
Reward for PoC operation
Reward for Proof of usage
$
PLMN A
PLMN B
PLMN C
$
Biz deal with MNO
for coverage/capacity extension
$
SUPNet Provider
SUPNet RAN nodes/cells

## Slide 4: High-level concepts (cont.)
SUPNet provider should manage:
  Onboarding, status reporting, other configuration functions related to the SUPNet RAN
  Proof-of-Coverage, authentication of inbound roaming session, policy enforcement, data recording and charging
  Coordination with MNOs, settlement of data offloading cost and reward
Assisting UE (A-UE) is a UE with new functionality performing Proof-of-Coverage/Usage
  It can be normal UE served by another PLMN or a dedicated UE for PoC purpose
SUPNet RAN
UE
SUPNet provider
Data Network
MNO
Core Network
Data connectivity
Control plane connection
Internet
[Legend]
A-UE
PoC

## Slide 5: Proposal for SA1
Study, in Rel-20, use cases and requirements covering the following areas:
Coordination/Exposure for coverage/capacity extension service to MNO, e.g.:
  To negotiate area/time for coverage/capacity extension, how much traffic/UEs are expected
  To determine/select candidates SUPNet nodes, update the configuration to serve the request from the MNO
Authorization and configuration of the SUPNet network, e.g.:
  How to support authorization and onboarding of SUPNet nodes
  How to configure SUPNet networks
  How to enforce a policy that MNO requires
Proof of Coverage, e.g.:
  How to verify the location & coverage of the SUPNet nodes
  How to verity the operation time of SUPNet nodes (e.. To verify availability of the network –24 hrs, part time, etc.)
  How to authenticate/authorize the participants and the transactions for Proof of Coverage operation
Proof of Usage, e.g.:
  How to authenticate the UE accessing the SUPNet NW (UE with MNO credential)
  Monitoring RAN/CN performance, and the amount of data offloaded

## Slide 6: ANNEX (Background information)

## Slide 7: Motivation – Business drivers
MNO
NW/UE vendor
SUPNet
Provider
Network Participant
(SUPNet owner, UE)
Gain: Reduced cost for Coverage /Capacity extension
Gain: Roaming / Service fee, Data offloading reward
Gain: Selling SUPNet NW, PoC devices
Gain: Reward for participating in
- Data offloading
- Proof of Coverage / Usage

## Slide 8: Examples of business/deployment options
SUPNet network
SUPNet network
SUPNet Provider #B
Shared spectrum
RAN sharing model
MNO#1 spectrum
SUPNet Provider #A
SUPNet supports multi-MNOs
Shared or dedicated bands
SUPNet cell
SUPNet Provider #C
Credential Holder
SUPNet cell
SUPNet cell
MNO#2
Roaming
Roaming
Roaming
Roaming
Roaming
Roaming
Shared band
MNO#1
SUPNet NW shared by two SUPNet providers