## Slide 1
S1-233290
SA1#104, November 13 – 17, Chicago, USA
Discussion on enhancements to IMS for new GEO global call services
Amy Zhang <amy.zhang@vivo.com>
Notes: https://portal.3gpp.org/desktopmodules/Specifications/SpecificationDetails.aspx?specificationId=3373
TR22.823, Study on enhancements to IMS for new real time communication services, R16

## Slide 2
  Motivation of new GEO global call services
  Voice calls via standard mobile phones over satellite connections are becoming increasingly popular in the market, particularly in remote and isolated areas. Traditionally, making voice calls over satellites required specialized terminals.
  GEO (Geostationary Earth Orbit) satellites hold a distinct advantage by theoretically providing global coverage with just three satellites. Moreover, the existing GEO deployment for global communication coverage can be repurposed to deliver worldwide basic voice call services, distinguishing it from NGSO (Non-Geosynchronous Orbit, including Medium/Low Earth orbit) satellites, which need constellations to offer global coverage.
  Consequently, there is a growing demand for enhancements to the IP Multimedia Subsystem (IMS) to facilitate the introduction of new voice call services over GEO satellites within the 3GPP.
NGSO satellite
GEO satellite
S1-233290
Notes: http://dgpaapp.forces.gc.ca/en/defence-capabilities-blueprint/project-details.asp?id=1694

## Slide 3
  Example use cases of new GEO global call services
Use case 1: Emergency call/SMS over GEO for rescue during earthquake
Use case 2: normal phone call over GEO
  In the aftermath of an earthquake that has left ground infrastructures in ruins, the absence of terrestrial coverage creates a dire situation. Bob, in need of urgent assistance, resorts to his mobile phone to call for help. Through the capabilities of GEO global call service, Bob's distress call is swiftly relayed to the rescue center, and his precise location is determined. The rescue team promptly responds, ultimately saving Bob's life.
  While hiking in Yosemite, Alice, who hails from São Paulo and is beyond terrestrial coverage, yearns to connect with her son. She turns to her mobile phone to reach out. Thanks to GEO global call service, their heartfelt communication is made possible, bringing joy to both Alice and her son.
GEO is assumed to be a narrowband satellite https://secwww.jhuapl.edu/techdigest/Content/techdigest/pdf/V33-N01/33-01-Gunduzhan.pdf
GEO is assumed to be an already deployed GEO satellite (in orbit) but has limited bandwidth (narrowband) reserved to communication.
S1-233290

## Slide 4
  Gap analysis
  The origins of IMS service can be traced back to Release 5 (TS22.228), which laid the foundation for basic IMS services supported in 3GPP. Subsequently, various aspects were addressed individually, including group management (Rel-6 TS22.250), IMS messaging (Rel-6 TS22.340), multi-vendor/operator inter-operability (Rel-7 TS22.173), and the combination of CS and IMS sessions (Rel-7 TS22.279).
  Despite being access-independent, the evolution of IMS service closely aligns with the development of terrestrial mobile networks, spanning 3G, 4G, and 5G. Specially in 5G, this evolution encompasses considerations like access control for local operator services in Rel-15 (PARLOS), VR telepresence and IMS enablement through network slicing in Rel-16 (enIMS), IMS emergency service for NPN (IESNPN), unified access control for IMS registration-related signaling in Rel-17, and AR media processing in Rel-18 (eMMTEL).
  Therefore, it is pertinent to extend the scope of IMS service in SA1 to encompass the integration of new GEO global call services.
Current constrains
New requirements
End-to-end latency with GEO-based satellite access is 285ms, which is challenging for the call set-up time for IMS voice
Simplify IMS signaling procedures
GEO narrowband can support limited transmission data rate considering the limited transmission power and antenna gain, to achieve better voice quality, the voice codec rate needs to be consistent with the transmission rate considering the SDP negotiation
  The integration of satellite access into 5G systems has been under examination since Release-16. Various facets, including the use of satellite access for backhaul and video surveillance, were addressed in Release-18. Release-19 brought about enhancements like regenerative payload and store-and-forward operations.
  When the 5G system incorporates satellite access, services such as content delivery and multicast/broadcast have been separately scrutinized. However, there has been a notable absence of comprehensive consideration for IMS service in 5G systems with satellite access, particularly concerning performance requirements, e.g. as outlined in Table 7.4.2-1 of TS22.261.
Lower bitrate voice codec
New KPIs for voice call over GEO
Fundamental assumption: Reusing current 3GPP defined GEO satellite access integration (i.e IoT NTN) architecture
S1-233290
Notes: The network should be involved in the SDP negotiation of the codec in order to select a codec with suitable rate
(session description protocol)

## Slide 5
  Objectives
  Option#1: It is proposed to investigate improvements to IMS to support new GEO global call services, aiming to establish a fundamental global voice call network in Release-20 as a miniWID. The primary requirements encompass:
      Functional requirements
      KPIs related to GEO global voice call over IMS.
  Option#2: It is proposed to investigate improvements to IMS to support new GEO global call services, aiming to establish a fundamental global voice call network in Release-20 as a SID. The primary requirements encompass:
      Investigating use cases and potential requirements associated with new GEO global call services.
      Identifying KPIs relevant to new GEO global call services, encompassing aspects such as voice codec, bandwidth, latency (comprising network and processing latency), reliability, and more.
      Addressing additional aspects, including security, charging mechanisms, and privacy considerations.
S1-233290

## Slide 6
S1-233290

## Slide 7
  Annex - Current GEO satellite access integration in 3GPP
CIoT device
Transparent payload
eNB
EPC
UE
Transparent payload
gNB
5GC
UE
Regenerative payload
gNB
5GC
R17 IoT NTN architecture, including NB-IoT and LTE-M
R17 NR NTN architecture
R19 regenerative payload architecture
UE
Transparent payload
gNB
5GC
R18 Satellite backhaul architecture
GEO
GEO
GEO
GEO
NOTE 1: The NB-IoT NTN architecture naturally aligns with GEO scenarios due to its (available) narrow bandwidth, low latency, and orbital altitude compatibility.
NOTE 2: In the 4 architectures mentioned above, IMS voice call is very challenging due to GEO's limited data rate capability. In particular, the NB-IoT NTN architecture cannot support IMS due to the restrictions imposed by NB-IoT.
We prefer this in 5.5 Advanced Pro
S1-233290
Notes: Gap analysis between the identified requirements and what has been already defined by existing 3GPP requirements.