## Slide 1
S1-240026, 3GPP TSG SA1#105, Athens, Greece, 26 February – 1 March 2024
Motivation for study on distributed device and user-centric trust
InterDigital

## Slide 2: Motivations of distributed device and user trust
Trust Model in 5GS [1]
  A UE-side trust model where the Universal Subscriber Identity Module (USIM) is the trust anchor.
  A Network-side trust model (for roaming and non-roaming) which mainly relies on primary authentication achieving mutual authentication between the network and UE. The primary authentication in 5G is however fully controlled by the home core network.
    The network-side trust model includes secondary authentication, which however is about the authentication with data networks outside the mobile operator domain.
NIST’s Trust Definition [2]
  “Trust A characteristic of an entity that indicates its ability to perform certain functions or services correctly, fairly and impartially, along with assurance that the entity and its identifier are genuine.”
ITU-T’s View on Trust [3]
  Trust in future mobile networks will have broader scope covering multiple aspects such as availability, reliability, dependability, security, and ability.
Trust in future mobile networks will be more than “primary authentication in 5GS”.
  Wireless system evolution toward 5G Advanced will feature the co-existing of increasingly distributed and more different types of networks and services, which devices can access.
  Such distributed networks and services can be offered from different domains (e.g., administrative domains) and without a requirement that there is a pre-established mutual trust relationship (e.g., from mutual authentication) between all such devices or distributed networks.
  Furthermore, different distributed networks may use different authentication and trust mechanisms.
  Researchers in [4] have investigated decentralized trust which could avoid the strict dependency of 5G primary authentication on the home core network. In turn, system availability and reliability will be improved
[1] A. R. Prasad, A. Zugenmaier, A. Escott and M. C. Soveri, “3GPP 5G Security,” August 06, 2018 (https://www.3gpp.org/news-events/3gpp-news/sec-5g).
[2] E. Barker, M. Smid, and D. Branstad, "A Profile for U.S. Federal Cryptographic Key Management Systems", NIST Special Publication 800-152, October 2015 .
[3] Trust in ICT, ITU-T, 2017 (http://handle.itu.int/11.1002/pub/80fd6f3d-en).
[4] S. R. Garzon, H. Yildiz and A. Küpper, "Decentralized Identifiers and Self-Sovereign Identity in 6G," in IEEE Network, July/August 2022

## Slide 3: Clarifications on some concepts
Distributed Trust
  Trust relationship built without fully relying on a centralized party (but such a centralized party may be used to facilitate to build distributed trust relationship).
  Distributed trust can be established among devices, between devices and networks (home, visited, or NPNs), or between networks.
  Distributed trust can enable trustworthy services, such as:
    1) services that a device can provide to another device;
    2) services that a network can provide to a device or vice versa; and
    3) services that a network can provide to another network.
User-Centric Trust
  Trust relationship relying on user credentials instead of fully relying on or in addition to SIM-based primary authentication in current 5GS.
  User-centric trust can be established among devices, and between devices and networks.
  User-centric trust can enable user-centric trustworthiness expanding or beyond existing SIM-based authentication and trust.
There are existing technologies, such as distributed ledgers, Self-Sovereign Identity (SSI), Decentralized Identifiers (DID) and verifiable credentials, that can enable distributed device and user-centric trust.

## Slide 4: A use case – SNPN Cellular Hotspots
When a device/user moves from a network-A to another distributed network-B (e.g., from one SNPN-A to another SNPN-B), the problem of how the device/user that is already authorized in network-A can be efficiently authorized in or by network-B becomes a critical issue.
The existing trust model in 5GS relies on the long-term shared secret K and a centralized party (e.g., home network), which becomes either unavailable or infeasible in such distributed networks.

## Slide 5: Benefits of distributed and user-centric trust
Scenarios | Benefits from Distributed and User-Centric Trust
SNPN Cellular Hotspots (S1-233477) | Smooth SNPN Interconnection: The same credential for a device/user can be efficiently verified and authenticated in different SNPNs, where it is not feasible to have a common credential holder for all SNPNs.
NPN-PLMN Interworking (S1-233100) | Smooth PLMN-to-NPN Switching: A device/user of HPLMN can be efficiently verified and authenticated in NPN without relying on HPLMN. Smooth NPN-to-PLMN Switching: A device/user of NPN without USIM can still be efficiently verified and authenticated by HPLMN.
Multi-Network Interoperability Enhancement (S1-233586) | Smooth NSA/SA Switching: A device/user when switching between NSA 5G and SA 5G can use the same credential for authentication and achieve smooth network switching and access.

## Slide 6: Objectives
Study use cases and potential service requirements for 5GS to support distributed device and user-centric trust:
  New service scenarios which demand and/or can be built upon distributed trust.
  New service scenarios which demand and/or can be built upon user-centric trust.
  The stage-1 impact of distributed and user-centric trust on existing functionality in 5GS, e.g., network access, roaming, security, O&M, energy saving and charging.
  Consideration of how the existing terminology in stage-1 (e.g., access control, confidentiality, integrity protection) and the terminology described for trust models in distributed networks and services can coexist.
  Potential new requirements on distributed device and user-centric trust in the context of SNPNs, PINs, and CPNs
Some Relevant Activities
SP-230236: New SID on Interconnect of SNPN (May 2023)
S1-233100: On the Need to Enhance NPN-PLMN Interworking (November 2023)
S1-233586: Study on Multi-network Interoperability Enhancement (November 2023)
ETSI GR PDL 021 V1.1.1: PDL Use Cases in 3GPP Networks (October 2023)
  “Decentralized certificate management, decentralized credential management, decentralized identity management”
  PDL: Permissioned Distributed Ledger

## Slide 7
Thank you!