## Slide 1
Task-driven Cooperative Dynamic Group
ZTE Corporation, CEPRI, China Unicom, China Telecom

## Slide 2
Motivation
Benefit for the network-controlled group management:
  application layer is unable to make real-time adjustments for the changes in both application layer and the network. Network can dynamically manage the group and data transmission based on the real-time conditions and requirements provided by application layers.
To meet the specific needs of different application tasks and situations, flexible QoS resource allocation and management is needed within the group. This includes dynamic workgroup creation and management.
01
02
Flexible QoS Resource Allocation and Management
Network-controlled Group Management
Notes: # motivation & benefit

## Slide 3
Dynamic group management
  Dynamic group establishing, adding/removing/reconfiguring members during the processing period.
    Network will establish a working group based on the recieved requirement for the application task and the task-level QoS requirement.
    If one or more members are not suitable to continue executing the assigned task due to the status change, network will either search for suitable UEs or re-configure members to resume processing for the group based on the specific requirements of task.
Task-level QoS
  The requirements of both the application task and task-level QoS are transmitted from server to 5G network. Network may select multiple qualified UEs as group members and establishe a working group applicable for the requirements.
  Task-level QoS management including task-level QoS monitoring, measurement, and prediction.
Example of inspection task in factory
Use Case Example
  Different members can be allocated with different application tasks and QoS resources and may be configured with different transmission paths on demand.
  Flexible data offloading within the workgroup is allowed.
Dynamic traffic management

## Slide 4
Gap Analysis
 | GCSE | SOBOT | MCX | 5G LAN | Task-driven Cooperative Dynamic Group
Concept | Distributing a same content to the different users | Different from industry robots, SOBOT to improve the level of daily behaviour | Mission critical service application | Using 5G network to provide virtual LAN type service | Dynamic group management and QoS management based on task requirements
Group components | Receiver group member+transmitter group member | Leader + members | MCX users+MCX administrator | Each single UE accesses to LAN by authorization | Head+member
Group management (including creation, modification, etc) | By authorized users or by the 3rd party | By application layer | By MCX service adminstrator, or by the authorized MCX UE | Each single UE is allowed to establish/release LAN service | By the network to select UEs for specific task
QoS mechanism | / | / | Follow existing QoS requirements | 3rd party to monitor QoS policy | Task-level QoS profile. Synchronization and coordination for multi-flow among multiple
Note | One way communication | / | / | / | On demand communication path configuration

## Slide 5
Objectives
Study of use cases related to 3GPP support of Cooperative Dynamic Group service and potential new requirements, considering the following:
    The Task-level QoS management for the dynamic group including task-level QoS configuration, monitoring and prediction.
    Dynamic group configuration and management of Cooperative Dynamic Group considering different conditions (e.g., application task requirements, location, radio condition, load status of devices...).
    The dynamic traffic management(either direct or indirect communication) among members in the group, including devices status collection and capability exposure, on-demand data transmission via flexible data path.
Gap analysis between the identified requirements and what has already been defined by existing 3GPP requirements.

## Slide 6
Thanks