## Slide 1
S1-240068, 3GPP TSG #105, 26 Feb - 1 Mar 2024, Athens, Grace
Discussion on Multi-network Interoperability Enhancement
China Unicom
3GPP 2024

## Slide 2
The early deployments are adopting NSA as a means of fast launching 5G and may gradually evolve towards SA. Based on operators’ different network development progress and deployment strategies, SA networks and NSA networks will coexist and interact in same PLMN or different PLMNs for a long period of time.
However, it is not always guaranteed for 5G subscribers to obtain consistent provision of 5G services in heterogeneous environment with coexisting SA and NSA networks.
Standard capabilities to enable 5G services offering to all 5G subscribers are essential to guarantee the user service experience and extend service area for users.
To reduce excessive investment and save cost by avoiding implement 5GC network elements at once in network evolution from EPC based NSA to 5GC based SA.
Background & Motivation
3GPP 2024

## Slide 3: Example Use Case 1
HPLMN supports EPC/NSA networks. VPLMN supports 5GC/SA network.
A 5G services subscriber of the HPLMN roams to the VPLMN
There are 5G roaming agreements between the VPLMN and the HPLMN
UE of the 5G roamer is a SA access capable terminal
3GPP 2024
Benefits
  EPC/NSA operators: assure their users of the similar 5G service and user experience as in the home EPC/NSA network when roaming without upgrading their EPC/NSA network
  SA operators: save investment and operating costs with CAPEX and OPEX, and reduce complexity of networks by maintaining only SA networks
EPC/NSA HPLMN
SA VPLMN
Roaming

## Slide 4: Example Use Case 2
There are 5GC/SA area and EPC/NSA area which are separate end to end in a same PLMN
A 5G subscriber data is provisioned on HSS in EPC/NSA area
The subscriber is travelling from the EPC/NSA area to the SA area
UE of the 5G subscriber is a SA access capable terminal
Service continuity is considered
3GPP 2024
Benefits
  Interworking capability between 5GC and EPC is suitable for operators introducing 5G subscriber data without impacting or migrating those subscriber data already provisioned on a legacy HSS.
  To reduce excessive investment and save cost by avoiding implement 5GC network elements all at once in 5G SA migration.
Non-Roaming
5G SA
5G NSA
others
others
MME
SGW
AMF
UPF
gNB
eNB
gNB
NSA area core network
SA area core network
Fig. NSA and SA are deployed in different areas within same PLMN
UDM
HSS
5G subscriber
5G subscriber
PLMN

## Slide 5: Gap Analysis & Proposal
Existing reqs and specs
  TS 22.261 clause 5.1 specified requirements of supporting interworking between 5G systems and interoperability with legacy 3GPP systems
  Stage-2/3 supports non-roaming and roaming interworking between 5GS and EPC/E-UTRAN.
Gaps
  The dedicated entities (i.e., HSS + UDM, SMF + PGW-C, and UPF + PGW-U) are required for the non-roaming and roaming interworking between 5GS and EPC/E-UTRAN defined in stage 2/3. However, there are no such dedicated entities in EPC/NSA region, only HSS and PGW instead.
  The roaming remains undefined where VPLMN has 5GC only and HPLMN has EPC only
  Requirements, service offering capability and mechanisms between 5GC and EPC are remain undefined
3GPP 2024
×
EPC/NSA region
SA only region region
Investigate use case which enable a 5GC/SA network to provide 5G services in the following scenarios:
  when a subscriber of HPLMN supporting only EPC/NSA networks roams to a VPLMN supporting only 5GC/SA networks
  when a subscriber travels, within one PLMN, from an EPC/NSA only area to a 5GC/SA only area
Derive potential requirements from those use cases regarding the following aspects:
  Network access control
  Subscription data retrieval
  Service continuity
  information of subscriber’s type (i.e. subscriber of a 5G SA network or a 5G NSA network)
  Others aspects, if any
Gap analysis between the existing 3GPP requirements and functionalities and identified potential requirements
Proposal

## Slide 6: Thank you
3GPP 2024