## Slide 1
3GPP TSG-SA WG1 Meeting #105, Athens, Greece, 26 Feb-1 March 2024
Discussion on Study of
Vehicle-Mounted Relays Phase3
CATT
Qing Wan (wanqing1@cictmobile.com)
S1 – 240075

## Slide 2: Background & Motivation
With the help of wireless backhaul, as an essential part of 5G network, the mobile base station relay becomes a promising technology to provide available and seamless 5G coverage to UEs located in the area with high mobility, or unrealistic to deploy wired backhaul, e.g. aerial, maritime area
The use cases of mobile base station relays have been studied in SA1 since Rel-17 and Rel-18, mainly focusing on UAV mounted[Figure 1] and ground-vehicle mounted cases[Figure2]. Accordingly, SA2 studied two types of architectures (e.g. IAB, MWAB) for different deployment needs[Figure3,4].
As further support of satellite NG-RAN and satellite backhaul enabled in 3GPP system, it’s possible for VMR to drive more use cases , especially that require NTN to be deeply involved. e.g. UAV-mounted, vessel-mounted usage to promote 5G in verticals like low-attitude aviation, maritime field.
Figure 2. Ground VMR(R18)
Figure 1. UxNB: RAN onboard UAV(R17)
Figure 3. IAB architecture (R18)
Figure 4. MWAB architecture (R19)
Cite: https://crew-center.com/

## Slide 3: UC#1: User Experience during Link Change
UxNB can be used for offering temporary 5G services to the users in/near the patrol ship that sails across non-terrestrial coverage area.
1. UxNB is launched for MNO1 subscribers (e.g. UE#), and connects to MNO1 5GC via MNO1 terrestrial RAN in Area-A.
2. UE# connects to MNO1 5GC via UxNB and obtains services(e.g. data, voice) with the required QoS.
3. As UE# moves to Area-B, UAV flies together and UxNB switches to connect to MNO1 5GC via satellite RAN of MNO2, which has the agreement with MNO1.
4. UE# connects to MNO1 5GC via UxNB as before, and the ongoing communication services are maintained by QoS harmonization. UE# traffic can be processed in MNO1 or MNO2 5GC based on MNO1 & MNO2 policies and agreements.
Current:
Provision QoS for relayed traffic, and UE policy during initial configuration;
The relay link change is transparent to UE and 5GC.
Gap:
5GC shall be aware of relay link change.
5GS shall maintain the service with min impact on the user experience with timely QoS adaption for NR satellite access.
Notes: Minimize the user experience(e.g. QoS, QoE) when mobile base station relay changes the link to the core network.

## Slide 4: UC#2: Concurrent Local Services and Remote Services via Vessel-Mounted Relays
VMRs are deployed by MNO#1 on a luxury cruise ship owned by ROYAL, with connecting the land 5GC via satellite NG-RAN(relay link#1), as well as access local MEC server e.g. provided by the cruise host via wired backhaul(relay link#2).
Bob(UE#1) and Alice(UE#2) are the subscribers of MNO#2 without satellite access capability, can obtain communication services via VMRs as a part of passenger services offered by the cruise host.
Bob intends to share the sea photos with his friend at home. VMR selects Relay Link#1 and transmit his traffic back to land 5GC via satellite access.
Alice is watching movies in app “ROYAL Cruise” which fetches the content from local MEC server via Relay Link #2.
Bob has a voice call with Alice, which can be finished via VMR without going through Land 5GC#2.
Current:
- Support VMR connecting to 5GC via NR satellite access and NR terrestrial access simultaneously.
- Differentiate UE traffic via VMR and collect charging info.
Gap:
- Not support VMR connecting to HPLMN via satellite RAN and to local hosting network simultaneously.
- Not support relay link selection for UE traffic of different services
- Charging for different relay link.

## Slide 5: Objectives
Study additional use cases and potential service requirements for enhancing 5GS to support mobile base station relay mounted on vehicles(e.g. UAV, vessel) using the connectivity to 3GPP satellite NG-RAN, including:
  User/service experience (e.g. minimize the impact for voice, data, and SMS) when the relay connectivity switches between TN access and NTN access
  Local services on the vessels for different purposes (e.g. efficient content delivery to onboard UEs, local switching, public safety with isolated NG-RAN)
  Aspects related to charging, regulatory requirements(e.g. emergency services).
Gap analysis between the identified potential requirements and existing 5GS requirements or functionalities.

## Slide 6
Thank you!