## Slide 1
3GPP TSG-SA WG1 Meeting #105, Athens, Greece, 26 Feb-1 March 2024
Discussion on Control related Services of Critical IoT Applications via Dual 3GPP Access (FS_CritIoTDualAccess)
CATT
Hui Xu (xuhui@catt.cn)
S1 – 240092

## Slide 2: Motivation
The demands on IoT services are gradually diverging but sometimes converging. As 5G location services and carrier-grade messaging are widely used in the management and control tasks of various IoT applications, the stringent requirement of network availability and reliability for those control related services are prevalent, especially in critical IoT applications (e.g. robot control, factory automation, critical medical care).
“Suning” Unmanned Automated Warehouse
The 5G support to critical IoT applications is not a point solution, but requires the collaboration of multiple 5G technologies.
User Plane based Services
Control Plane based Services

## Slide 3: Gap Analysis
Rel-19 SA1 has studied the use cases and normative requirements for user traffic of DualSteer device applied in smartphones, IoT, UAV, etc. (under the above scenarios)
Existing Requirements/Functions
Gap/Potential Requirements
Miss the use cases about control plane based services (e.g. positioning, SMS) on DualSteer device based critical IoT applications
sometimes perform at the same time when user plane based services are ongoing on two separate UEs.
face the DL routing issue between DualSteer device and peer endpoint(e.g. 5GC NF, App Server) when two 3GPP connections coexist.
worth to leverage dual 3GPP connections for better network resource efficiency, service availability, etc as low-hanging fruit.

## Slide 4: Typical Use Cases
The “last gasp” message of Smart Meter will be delivered to the application server via both 3GPP access duplicated for high reliability.
UC#1 AGV Control via dual 3GPP Access
1. AGV sends photos via NR#2 and sensor data via NR#1 simultaneously.
2. The platform initiates 5G positioning service for AGV periodically. The PLMN steers AGV to report location info. via either NR based on e.g. QoS.
3. The platform informs AGV to gasp the box via DL SMS including precise location and commands. PLMN directs SMS delivery via NR#2 considering the AGV is moving into better coverage of NR#2 than NR#1.
Other Use Cases
Location info. of the same DualSteer device will be reused when QoS fulfills the new request or in case of unavailability of one network.
“Last Gasp” Message of Smart Meter
Positioning by 5GC Coordination

## Slide 5
Study the use cases and potential service requirements to improve 5GS for control related services of DualSteer device-based critical IoT applications via dual 3GPP access, including:
  Positioning enhancement(e.g. location source selection, location information directing, etc)
  Messaging services over signalling(e.g. downlink message delivery)
  Aspects related to network capability exposure, charging, etc
Gap analysis between potential new service requirements and existing 3GPP requirements and functionalities.
NOTE: The capability of DualSteer device is aligned with the definition in TS 22.261.
Proposed Objectives

## Slide 6
Thank You!